820-013
Deep Space Mission System (DSMS)
External Interface Specification

JPL D-16765

TRK-2-34

DSMS Tracking System
Data Archival Format

Original Release: April 30, 2000

Revision B: December 15, 2002

| Document Owner: Signature on File in DSMS Library ______________________________ ________ Jeff B. Berner Date Service System Development Engineer, Telecommunications Services Signature on File in DSMS Library ______________________________ ________ Tomas J. Martin-Mur Date Service System Development Engineer, Tracking & Navigation Services |  | Approved by: Approved by: Signature on File in DSMS Library ______________________________ ________ L.A. Cangahuala Date Service System Manager, Tracking & Navigation Services Signature on File in DSMS Library ______________________________ ________ Susan Kurtik Date Service System Manager, Telecommunications Services |
| --- | --- | --- |
| Approved by: Approved by: Signature on File in DSMS Library ______________________________ ________ Wallace Tai Date Manager, DSMS Systems Engineering and Standards Office |  | Approved by: Signature on File in DSMS Library ______________________________ ________ J. Stipanuk Date Interface Engineer and Release Authority |

Prepared By:

| Approved by: Signature on File in DSMS Library ______________________________ ________ Jeff B. Berner Date Service System Development Engineer, Telecommunications Services |  | Approved by: |
| --- | --- | --- |

Reviewed By:

| Approved by: Signature on File in DSMS Library ______________________________ ________ Dana Flora-Adams Date Tracking Data Delivery Service CDE |  | Approved by: Signature not available ______________________________ ________ Charles Ruggier Date DSMS System Engineering |
| --- | --- | --- |
| Signature on File in DSMS Library Approved by: ______________________________ ________ V.I. Altunin Date Telecommunications & Mission Services Manager (RADIOASTRON, 70m CoObsI, HALCA) Signature not available ______________________________ ________ R.D. Benson Date Telecommunications & Mission Services Manager Signature not available ______________________________ ________ P.E. Beyer Date Telecommunications & Mission Services Manager Signature not available ______________________________ ________ A.F. Chang Date Telecommunications & Mission Services Manager Signature not available ______________________________ ________ R.L. Gillette Date Telecommunications & Mission Services Manager |  | Signature on File in DSMS Library Approved by: ______________________________ ________ D.P. Holmes Date Telecommunications & Mission Services Manager Signature not available ______________________________ ________ K. Moyd Date Telecommunications & Mission Services Manager Signature not available ______________________________ ________ P.T. Poon Date Telecommunications & Mission Services Manager Signature not available ______________________________ ________ S. Waldherr Date Telecommunications & Mission Services Manager Signature not available ______________________________ ________ B.G. Yetter Date Telecommunications & Mission Services Manager |
| Approved by: Signature not available ______________________________ ________ David Reece Date DSMS Chief Operations Engineer |  | Approved by: Signature on file in DSMS Library Approved by: ______________________________ ________ Michael Levesque Date Service System Development Engineer, Telecommunications Services |
| Signature not available Approved by: ______________________________ ________ Jeremy Jones Date Cassini Navigation |  | Signature not available Approved by: ______________________________ ________ Pat Esposito Date MSOP Navigation |
| Signature not available Approved by: ______________________________ ________ Jordan Ellis Date Multimission Navigation |  | Signature not available Approved by: ______________________________ ________ Steve Flanagan Date Project Element Manager (PEM), Next Generation Navigation Software |
| Signature not available Approved by: ______________________________ ________ Bobby Williams Date NEAR Navigation |  | Signature on file in DSMS Library ______________________________ ________ Sami Asmar Date Radio Science Systems Group |
| Signature not available Approved by: ______________________________ ________ Michael Connally Date DSN Science Advisor |  |  |

This page is intentionally left blank.

Change Log

| Revision | Issue Date | Pages / Sections Affected | Change Summary |
| --- | --- | --- | --- |
| New issue | 04/30/2000 | All |  |
| A | 05/31/2002 | All | Updated data blocks, added/corrected text descriptions |
| B | 12/15/2002 | Sections 1, 2 and 3, Appendix A and B | Corrected typos, added file header description (Appendix B) |

This page is intentionally left blank.

Contents

Section	Page

1	Introduction	1-1

1.1	Purpose and Scope	1-1

1.1.1	Applicability of This Release	1-1

1.2	Revision and Control	1-1

1.3	Relationship to Other DSMS Documents	1-1

1.4	Applicable Documents	1-2

1.5	Notation and Conventions	1-2

1.5.1	Terminology	1-2

1.5.2	Conventions	1-4

1.6	Abbreviations	1-5

2	Functional Overview	2-1

2.1	General Description	2-1

2.2	Operational Concept	2-1

2.3	Equipment	2-2

3	Detailed Interface Description	3-1

3.1	Data Definition	3-1

3.1.1	Tracking Data SFDU Label	3-2

3.1.2	Aggregation CHDO Label	3-3

3.1.3	Primary CHDO	3-4

3.1.4	Secondary CHDOs	3-5

3.1.4.1	Secondary CHDO 134 (Derived Data Types)	3-6

3.1.4.2	Secondary CHDO 132 (Uplink Data Types)	3-10

3.1.4.3	Secondary CHDO 133 (Downlink Data Types)	3-13

3.1.4.4	Secondary CHDO 135 (Interferometric Data Types)	3-17

3.1.4.5	Secondary CHDO 136 (Filtered Data Types)	3-20

3.1.5	Tracking Data CHDOs	3-23

3.1.5.1	Uplink Data CHDOs	3-24

3.1.5.1.1	Uplink Carrier Phase CHDO (Data Type 0)	3-25

3.1.5.1.2	Uplink Sequential Ranging Phase CHDO (Data Type 2)	3-26

3.1.5.1.3	Uplink PN Ranging Phase CHDO (Data Type 4)	3-29

3.1.5.1.4	Ramp CHDO (Data Type 9)	3-32

3.1.5.2	Downlink Data CHDOs	3-34

3.1.5.2.1	Downlink Carrier Phase CHDO (Data Type 1)	3-34

3.1.5.2.2	Downlink Sequential Ranging Phase CHDO (Data Type 3)	3-39

3.1.5.2.3	Downlink PN Ranging Phase CHDO (Data Type 5)	3-44

3.1.5.3	Derived Data CHDOs	3-50

3.1.5.3.1	Doppler Count CHDO (Data Type 6)	3-50

3.1.5.3.2	Sequential Range CHDO (Data Type 7)	3-55

3.1.5.3.3	Angle CHDO (Data Type 8)	3-59

3.1.5.3.4	DRVID CHDO (Data Type 11)	3-61

3.1.5.3.5	PN Range CHDO (Data Type 14)	3-62

3.1.5.3.6	Tone Range CHDO (Data Type 15)	3-66

3.1.5.3.7	Carrier Frequency Observable CHDO (Data Type 16)	3-67

3.1.5.3.8	Total Count Phase Observable CHDO (Data Type 17)	3-69

3.1.5.4	Interferometric Data CHDOs	3-71

3.1.5.4.1	VLBI CHDO (Data Type 10)	3-71

3.1.5.5	Filtered Data CHDOs	3-72

3.1.5.5.1	Smoothed Noise CHDO (Data Type 12)	3-72

3.1.5.5.2	Allan Deviation CHDO (Data Type 13)	3-74

3.2	Dependencies	3-75

Appendix A	Notes	A-1

Appendix B	File Format	B-1

B.1	LVO Structure of Files	B-1

B.2	Physical Layout of Files	B-1

B.2.1	Primary SFDU Label	B-3

B.2.2  K-Header (or K-Object)	B-4

B.2.2.1  K-Header  SFDU Label	B-4

B.2.3   I-Object SFDU Label	B-7

B.2.4   Binary Data Object	B-8

B.2.5  End of File (EOF)	B-8

Figures

Figure	Page

Figure 3-1.  LVO Structure of the Tracking Data SFDU	3-1

Figure 3-2.  Physical Layout of the Tracking Data SFDU	3-2

Figure B-1.  LVO Structure of Files	B-1

Figure B-2.  File Layout	B-2

Figure B-3.  Sample Header of File	B-3

Tables

Table	Page

Table 3-1.  Tracking SFDU Label Definitions	3-2

Table 3-2.  Aggregation CHDO Label Definitions	3-4

Table 3-3.  Primary CHDO Definitions	3-4

Table 3-4.  Secondary CHDO 134 Definitions	3-6

Table 3-5.  Secondary CHDO 132 Definitions	3-10

Table 3-6.  Secondary CHDO 133 Definitions	3-13

Table 3-7.  Secondary CHDO 135 Definitions	3-17

Table 3-8.  Secondary CHDO 136 Definitions	3-20

Table 3-9. Uplink Carrier Phase CHDO (Data Type 0) Definitions	3-25

Table 3-10. Uplink Sequential Ranging Phase CHDO (Data Type 2) Definitions	3-27

Table 3-11. Uplink PN Ranging Phase CHDO (Data Type 4) Definitions	3-29

Table 3-12. Ramp CHDO (Data Type 9) Definitions	3-33

Table 3-13. Downlink Carrier Phase CHDO (Data Type 1) Definitions	3-34

Table 3-14. Downlink Sequential Ranging Phase CHDO (Data Type 3) Definitions	3-40

Table 3-15. Downlink PN Ranging Phase CHDO (Data Type 5) Definitions	3-44

Table 3-16. Doppler Count CHDO (Data Type 6) Definitions	3-50

Table 3-17. Sequential Range CHDO (Data Type 7) Definitions	3-55

Table 3-18. Angle CHDO (Data Type 8) Definitions	3-60

Table 3-19. DRVID CHDO (Data Type 11) Definitions	3-61

Table 3-20. PN Range CHDO (Data Type 14) Definitions	3-62

Table 3-21. Tone Range CHDO (Data Type 15) Definitions	3-66

Table 3-22. Carrier Frequency Observables CHDO (Data Type 16) Definitions	3-67

Table 3-23. Total Count Phase Observable CHDO (Data Type 17) Definitions	3-69

Table 3-24. VLBI CHDO (Data Type 10) Definitions	3-71

Table 3-25. Smoothed Noise CHDO (Data Type 12) Definitions	3-72

Table 3-26. Allan Deviation CHDO (Data Type 13) Definitions	3-74

Table B-1.  Primary SFDU Label	B-3

Table B-2.  K-Header (or K-Object) SFDU Label	B-4

Table B-3.  Catalog Information (Value Field of the K-Object)	B-5

Table B-4.  I-Object SFDU Label	B-7

This page is intentionally left blank.

# Introduction

Section 1

Introduction

## Purpose and Scope

This module specifies the format and content of radio metric tracking data delivered to navigation and radio science customers from the Telecommunications Services. The method of delivery of the data is outside the scope of this document.

TRK-2-34 is essentially a consolidation of the data that are currently contained in the TRK-2-15A, TRK-2-18, TRK-2-20, TRK-2-25, and TRK-2-30 products delivered to customers.

### Applicability of This Release

This module will supersede the TRK-2-15A module, as the MDAs are retired, and the TRK-2-25 module as the Radio Metric Data Conditioning (RMDC) process is retired.

This release corrects typos and adds description of the file header format.

Certain parameters may not be available in initial TRK-2-34 output.  These parameters will be marked as invalid (using validity flags) in the data or not delivered (in the case of certain data types, such as Allan deviation and smoothed noise).

## Revision and Control

Revisions or changes to the information herein presented may be initiated according to the procedure specified in the Introduction to Document 820-013.

## Relationship to Other DSMS Documents

Currently, TRK-2-15A is generated by the Metric Data Assembly (MDA) of the DSCC Tracking Subsystem (DTK).  In the Network Simplification Project (NSP) era, the MDAs will be replaced by the Uplink Tracking and Command Subsystem (UPL) and the Downlink Telemetry and Tracking Subsystem (DTT).  As a result, TRK-2-15A will not be available.  TRK-2-34 replaces TRK-2-25 as the archival format.  TRK-2-20 and TRK-2-30 will continue to be available to the customers.

## Applicable Documents

| [1] | 820-062 | DSMS Terms and Abbreviations (DSMS internal document, for reference only.) |
| --- | --- | --- |
| [2] | 813-109, D-17818 | Preparation Guidelines and Procedures for Deep Space Mission System (DSMS) Interface Specifications (DSMS internal document, for reference only.) |
| [3] | 820-013, D-16765 | DSMS External Interface Specification (http://jaguar.jpl.nasa.gov) |
| [3a] |  | OPS-6-21A Standard Code Assignments |
| [3b] |  | 0171-Telecomm-NJPL SFDU Global Definitions |
| [3c] |  | 0180-Data_Manage DSMS DOM Electronic Access for External Users |
| [3d] |  | 0183-Telecomm-TDS TDS Query Protocol Specification |
| [4] | SFOC-5-SYS-*DU-NJPL | NJPL SFDU Global Definitions (DSMS internal document, for reference only; to be replaced by Reference [3b].) |
| [5] | 820-013, Module 0172-Telecomm-CHDO | DSMS External Interface Specification—DSMS Created CHDO Structures |
| [6] | CCSDS 620.0-B-2 | CCSDS Recommendation for Space Data System Standards—Standard Formatted Data Units—Structure and Construction Rules (Issue 2, May 1992) |
| [7] | ANSI T-49-12 | ANSI/IEEE STD 754-1985—IEEE Standard for Binary Floating-Point Arithmetic |
| [8] | ANSI X3.4-1986 (R1997) | Information Systems - Coded Character Sets - 1 Bit American National Standard Code for Information Interchange (7-Bit ASCII) |
| [9] | ISO/IEC 646-1991 | Information Technology - ISO 7-bit Coded Character Set for Information Interchange |
| [10] | 810-047 | DSN Antenna and Facility Identifiers (DSMS internal document, for reference only.) |

## Notation and Conventions

### Terminology

Many of the terms used in this module are taken from the literature describing the Standard Formatted Data Unit (SFDU) concept (e.g., Reference [5] and Reference [6]).  The SFDU concept was developed by the Consultative Committee for Space Data Systems (CCSDS) to provide a standardized and internationally recognized methodology for information interchange.  Because the SFDU concept evolved over time, the meaning of some terms has evolved.  The definitions provided herein are intended to clarify the use of certain terms as they apply to this module:

a)	The term ASCII refers to the American Standard Code for Information Interchange, a seven-bit code for representing letters, digits, and symbols which has been standardized by the American National Standards Institute (Reference [8]). This code has been incorporated into the ISO code of the same nature (Reference [9]) which includes other symbols and alphabets.  Since the ISO code is an eight-bit code, the ASCII code is embedded in an eight-bit field in which the most significant bit is set to zero.  In this module, ASCII always refers to the seven-bit ASCII code embedded, as described, in an eight-bit field.  When applied to a multi-byte field, it implies that each byte in the field contains an ASCII code.

b)	The term restricted ASCII (RA) refers to the subset of ASCII consisting of the codes for the twenty-six upper-case letters (‘A’-‘Z’) and the ten decimal digits (‘0’-‘9’).  When applied to a multi-byte field, it implies that each byte in the field contains an RA code.

c)	A label-value-object (LVO) is a data structure that is comprised of a label field and a value field.  The label field provides for the data structure to be self-identifying and self-delimiting.  The value field contains user-defined data in any format.  The LVOs themselves are made up of a sequence of bytes.  In this module, LVO is used in a generic sense to refer to any data structure with these attributes.

d)	An LVO may be a simple LVO or a compound LVO.  If the value field of the LVO contains purely user data, it is a simple LVO.  If the value field of the LVO contains purely LVOs, it is a compound LVO.  The value field of a compound LVO consists of a sequence of one or more LVOs, each of which can be a simple or compound LVO itself.

e)	A standard formatted data unit (SFDU) is an LVO that conforms to a defined set of structure and construction rules, namely the specification in Reference [5] or the specification in Reference [6].  Unfortunately, the two specifications are slightly different, leading to two different definitions of what an SFDU is.  The term DSN tracking SFDU (or, more simply, tracking SFDU) refers to the SFDU defined and controlled by this module.  The DSN tracking SFDU conforms to the structure and construction rules specified in Reference [5].  It does not strictly conform to the internationally recognized SFDU structure and construction rules recommended by CCSDS in Reference [6].

f)	A compressed header data object (CHDO), as defined in Reference [5], is an LVO.  Its design is modeled on the SFDU concept, but a CHDO is not an SFDU.  The CHDO derives its name from the fact that the label field of a CHDO is considerably shorter than the label field of an SFDU (four bytes instead of twenty).  The CHDO provides a means of structuring user data with less overhead than would be required if an SFDU were used.  However, with respect to SFDU structure and construction rules, a CHDO (or a sequence of CHDOs) is merely user data contained in the value field of an SFDU.

g)	The term type attribute is used to refer to the subfield(s) of an LVO label field that affect the self-identifying property of the LVO.  Within the applicable domain, the type attribute is a unique reference to a description of the format and meaning of the data contained in the value field of the LVO.

h)	All of the LVOs described in this module contain a length attribute in their label field.  The length attribute is a subfield of the LVO label field; it contains the length, in bytes, of the value field of the LVO.  When interpreted in the context of the structure and construction rules specified in Reference [5], the length attribute affects the self-delimiting property of the LVO.  The use of a length attribute is not the only means by which an LVO can be self-delimiting; Reference [6], for example, provides several mechanisms that do not rely on an explicit length.

i)	The term data type refers to the SFDU format code.  This term is used when distinguishing between different data blocks.

### Conventions

The following conventions are used in this module:

a)	LVOs are defined as being made up of a sequence of eight-bit bytes, so data structures in this module are illustrated as a sequence of bytes.  All data structures defined in this module must be an even number of bytes in length.  Given a data structure that is N bytes in length, the first byte in the structure is drawn in the most top justified position and is identified as “byte 0.”  The following byte is identified as “byte 1” and so on, to “byte N-1” which is drawn in the most bottom justified position.  Within each byte, the most significant bit is drawn in the most left justified position and is identified as “bit 1.”  The next most significant bit is identified as “bit 2” and so on, to “bit 8” which is drawn in the most right justified position.  Any bit in a data structure is uniquely identified by specifying the byte within which it occurs and its position within that byte (e.g., “byte 5, bit 8”).

b)	Data structures are divided into fields, where a field is a sequence of bits.  Fields are identified by specifying the starting and ending bits of the field.  For fields that cross byte boundaries, bit 8 of byte M is more significant than, and is immediately followed by, bit 1 of byte M+1.  A field may be divided into subfields in a similar manner.

c)	Several conventions for expressing the length of a data structure, or a part of a data structure, are used in this module.  The length attribute of an LVO is always given in bytes and always refers to the length of the value field of the LVO (i.e., excluding the label field).

d)	In the data structure descriptions in this module, many fields are defined to contain a numerical value.  Several different formats for expressing numbers are used, as follows:

1)	Unsigned integer.  An integer number is expressed in binary, using all bits of the field as necessary.  Negative quantities cannot be expressed.  For an n-bit field, the range of values that can be represented is from 0 to 2n-1.  The number of bytes in the unsigned integer (m) is represented by a “-m” after the format statement.

2)	Integer.  An integer number is expressed in binary, using two's complement notation.  For an n-bit field, the range of values that can be represented is from 
-2n-1 to 2n-1-1. The number of bytes in the integer (m) is represented by a “-m” after the format statement.

3)	Restricted ASCII.  Each decimal digit of an integer number is expressed by its corresponding RA code.  The field must be an integral number of bytes in length.  For multi-digit fields, the first byte of the field contains the most significant digit, the second byte contains the next most significant digit, and so on.  If the number of digits is less than the number of bytes in the field, leading zeroes are used to fill the field.  Negative quantities cannot be expressed.  In an n-byte field, the range of values that can be represented is from 0 to 10n-1.  The number of bytes in the Restricted ASCII string (m) is represented by a “-m” after the format statement.

4)	IEEE Single.  A 32-bit, single precision, IEEE floating point-format is used to express real numbers.  Single precision floating-point numbers are expressed in the ANSI/IEEE standard (Reference [7]) single precision format with a sign bit, 8-bit exponent, and 23-bit mantissa.

5)	IEEE Double.  A 64-bit, double precision, IEEE floating-point format is used to express real numbers.  Double precision floating-point numbers are expressed in the ANSI/IEEE (Reference [7]) standard double precision format with a sign bit, 11-bit exponent, and 52-bit mantissa.

e)	For fields defined to contain a constant value, the constant value will be enclosed in single quotes (e.g., ‘2’) if the information is expressed in RA, and not so enclosed (e.g., 2) if the information is expressed in binary.

f)	Unless explicitly stated otherwise, fields defined as “reserved” are to be set to binary zero by the originator, and are to be ignored by the recipient.

- Time tags are in UTC, as received from the Frequency and Timing Subsystem (FTS) of the DSN:

- 00:00:00 is second 0.0.

- 23:59:59 is second 86399.0.

- Leap second is 86400.0.

h)	The term "UPL-DTT antenna" refers to antennas that have UPL and DTT equipment (currently 34m HEF, 34m BWG, and 70m antennas).  The term "non-UPL-DTT antenna" refers to antennas that do not have this equipment (currently 26m antennas and DSS-27).

## Abbreviations

Abbreviations used in this document are defined with the first textual use of the term.  Abbreviations and acronyms approved for use are listed in Document 820-062.  Abbreviations appearing in this module are:

| ADID AMMOS ASCII ANSI | Authority and Description Identifier Advanced Multimission Operations System American Standard Code for Information Exchange American Nation Standards Institute |
| --- | --- |
| CHDO CCSDS | Compressed Header Data Object Consultative Committee for Space Data Systems |
| dB dBm deg DOD DOR | decibel decibels above the reference level of 1 milliWatt degrees Differential One-way Doppler Differential One-way Ranging |
| DRVID DSCC DSMS DSN | Differenced Range Versus Integrated Doppler Deep Space Communications Complex Deep Space Mission System Deep Space Network |
| DSS | Deep Space Station |
| DTK | DSCC Tracking Subsystem |
| DTT EOF FFT | Downlink Telemetry and Tracking Subsystem End of File Fast Fourier Transform |
| FOM FSP FTS Hz ID IEEE IF JPL K LCP LNA | Figure of Merit Full Spectrum Processing Subsystem Frequency and Timing Subsystem Hertz Identifier Institute of Electrical and Electronics Engineers Intermediate Frequency Jet Propulsion Laboratory Kelvin Left Hand Circular Polarization Low Noise Amplifier |
| LVO | Label Value Object |
| MDA MFR MPA MTA N/A NASA | Metric Data Assembly MultiFunction Receiver Metric Pointing Assembly Metric Tracking Assembly Not Applicable National Aeronautics and Space Administration |
| NOCC | Network Operations Control Center |
| NSP | Network Simplification Project |
| NVP | NOCC VLBI Processor Subsystem |
| PN | Pseudo-Noise |
| RA RCP RF | Restricted ASCII Right Hand Circular Polarization Radio Frequency |
| RMDC RTLT | Radio Metric Data Conditioning Round-Trip Light Time |
| RU sec | Range Unit seconds |
| SFDU SNT | Standard Formatted Data Unit System Noise Temperature |
| UPL | Uplink Tracking and Command Subsystem |
| UTC | Universal Time Coordinated |
| VLBI W | Very Long Baseline Interferometry Watts |

This page is intentionally left blank.

# Functional Overview

Section 2

Functional Overview

## General Description

Radio metric data received from the DSCCs will be processed, validated, and corrected.  The resulting data will be placed into the TRK-2-34 and TRK-2-18 products.  Validated/corrected data are available to (a) remote customers as TRK-2-34 files, and (b) JPL AMMOS customers as files, stream-type queries, or broadcast streams.  The file format is described in Appendix B.  This interface does not describe the transfer mechanisms for the delivery of the data to the customers; they are described, respectively, in References [3c] and [3d].

This processing is done in the AMMOS system.  It includes the software tools that are used to perform radio metric data processing, validation, correction, and visualization, and to generate the tracking data file products. The function of the processing is to process, generate, and deliver radio metric data to projects and end users to support spacecraft navigation and scientific study.

Listed below are the documents and 820-013 interface modules that define specific fields in the TRK-2-34 headers:

Reference [3a]: DSN spacecraft ID, AMMOS mission ID

Reference [10]: station ID

Reference [4]: originator ID, last modifier ID

## Operational Concept

Users provide spacecraft configuration data (such as transponder number, spacecraft oscillator frequency values, etc.) and light time data.  The user also specifies data delivery options (such as data decimation rate).  This data, along with the DSN physical data maintained in internal tables, are combined with the raw measurements from the DSN to generate the radiometric data described by this document.

TRK-2-15A data will continue to be produced by DSSs until the Metric Data Assembly (MDA) has been completely retired.  The existing Radio Metric Data Conditioning (RMDC) software will continue to be used until the TRK-2-15A data are no longer produced.

Parameters and data types that require predicted values, such as prefit residuals and Allan deviation, will not be available if the trajectory data for generating the predicted values is not available.  If this happens, the parameter status will be marked as invalid (using validity flags) and the data types will not be generated.

## Equipment

All equipment used in the measurement or generation of tracking data get their frequency and timing references from the Frequency and Timing Subsystem (FTS) of the DSN.

The non-UPL-DTT antennas have a mixture of tracking equipment.  The 26m subnet uses the Metric Pointing Assembly (MPA).  DSS-27, a 34m antenna, uses the Metric Tracking Assembly (MTA).

Arraying at a complex is done with the Full Spectrum Processing Subsytem (FSP).

# Detailed Interface Description

Section 3

Detailed Interface Description

## Data Definition

Viewed as a compound LVO, the value field of the tracking data SFDU contains two LVOs, an aggregation CHDO and a tracking data CHDO.  The aggregation CHDO is a compound LVO; its value field contains two simple LVOs, a primary CHDO and a secondary CHDO.  The aggregation CHDO exists solely for the purpose of allowing the primary and secondary CHDOs to be grouped together and treated as a single LVO.  The value fields of the primary and secondary CHDOs contain annotation data (identification, configuration, status, and performance parameters) that pertain to the data in the tracking data SFDU.  The tracking data CHDO is a simple LVO; its value field contains the actual tracking data.

+---------------------------------------------+

L¦  Tracking Data SFDU                         ¦

+-+  +---------------------------------------+¦

¦ L¦  Aggregation CHDO                     ¦¦

¦  +-+  +---------------------------------+¦¦

¦    ¦ L¦ Primary CHDO                    ¦¦¦

¦    ¦  +-+                               ¦¦¦

¦    ¦   V¦                               ¦¦¦

¦   V¦  +---------------------------------¦¦¦

¦    ¦ L¦ Secondary CHDO                  ¦¦¦

¦    ¦  +-+                               ¦¦¦

V¦    ¦   V¦                               ¦¦¦

¦  +---------------------------------------¦¦

¦ L¦  Tracking Data CHDO                   ¦¦

¦  +-+                                     ¦¦

¦    ¦                                     ¦¦

¦    ¦                                     ¦¦

¦    ¦                                     ¦¦

¦   V¦                                     ¦¦

¦    ¦                                     ¦¦

¦    ¦                                     ¦¦

¦    ¦                                     ¦¦

+-------------------------------------------+

L = label field         V = value field

Figure 3-1.  LVO Structure of the Tracking Data SFDU

Figure 3-2 shows the physical layout of the tracking data SFDU.  It is divided into the following sections: the tracking SFDU label, the aggregation CHDO label, the primary CHDO, the secondary CHDOs, and the tracking data CHDOs.  There are five different types of secondary CHDOs, and 18 types of tracking data CHDOs.

The following sections present the detailed definition of the tracking data SFDU.

BIT

+-----------------------------------------------+

¦1 ¦2 ¦3 ¦4 ¦5 ¦6 ¦7 ¦8 ¦1 ¦2 ¦3 ¦4 ¦5 ¦6 ¦7 ¦8 ¦

+-----------------------------------------------¦

BYTE 0¦                                               ¦

+-                                             -¦

...                  SFDU LABEL                 ...

...                                             ...

+-                                             -¦

18¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

20¦                                               ¦

+-            AGGREGATION CHDO LABEL           -¦

22¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

24¦                                               ¦

+-                                             -¦

...                PRIMARY CHDO                 ...

...                                             ...

+-                                             -¦

30¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

32¦                                               ¦

+-                                             -¦

...               SECONDARY CHDO                ...

...                                             ...

+-                                             -¦

xx¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

xx¦                                               ¦

+-                                             -¦

...             TRACKING DATA CHDO             ...

...                                            ...

+-                                             -¦

N-2¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

¦1 ¦2 ¦3 ¦4 ¦5 ¦6 ¦7 ¦8 ¦1 ¦2 ¦3 ¦4 ¦5 ¦6 ¦7 ¦8 ¦

+-----------------------------------------------+

N Depends on Data Type

Figure 3-2.  Physical Layout of the Tracking Data SFDU

### Tracking Data SFDU Label

Bytes 0 through 19 of the tracking SFDU contain the SFDU label field.  The format and content of the SFDU label are defined in Table 3-1.  The concatenation of Bytes 0 through 3, and 8 through 11, constitutes the type attribute of the SFDU; in CCSDS parlance, this concatenated field is known as the Authority and Description Identifier (ADID).  Bytes 12 to 19 constitute the length attribute.

Table 3-1.  Tracking SFDU Label Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| control_auth_id | 0 | Control authority identifier. ‘NJPL’ indicates that the data description information for this SFDU is maintained and disseminated by NASA/JPL. | Restricted ASCII –4 | N/A | ‘NJPL’ |  |
| sfdu_version_id | 4 | SFDU label version ID. ‘2’ indicates that the length attribute field in bytes 12 to 19 is formatted as a binary unsigned integer. | Restricted ASCII –1 | N/A | ‘2’ |  |
| sfdu_class_id | 5 | SFDU class ID. ‘I’ indicates that this SFDU contains data to be used by an application process. | Restricted ASCII –1 | N/A | ‘I’ |  |
| reserve2 | 6 | Reserved. Two bytes. | Restricted ASCII –2 | N/A | ‘00’ |  |
| data_description_id | 8 | Data description identifier. Uniquely identifies the data description information held by the control authority identified in the ‘Control authority identifier’ item for this type of SFDU. C123 => Uplink types C124 => Downlink types C125 => Derived types C126 => Interferometric types C127 => Filtered types | Restricted ASCII –4 | N/A | ‘C123’, ‘C124’, ‘C125’, ‘C126’, ‘C127’ |  |
| sfdu_length | 12 | Length attribute of the tracking data SFDU. Indicates the length of the data following this element. DT0 => 162 DT1 => 358 DT2 => 194 DT3 => 304 DT4 => 218 DT5 => 332 DT6 => 320 DT7 => 330 DT8 => 178 DT9 => 124 DT10 => 204 DT11 => 182 DT12 => 164 DT13 => 160 DT14 => 304 DT15 => 194 DT16 => 182 + 18 * num_obs DT17 => 194 + 22 * num_obs | Unsigned Integer –8 | Bytes | 124, 160, 162, 164, 178, 182, 194, 204, 218, 304, 304, 320, 330, 332, 358, 182 + 18 * num_obs, 194 + 22 * num_obs (num_obs < 100) |  |

### Aggregation CHDO Label

Bytes 20 through 23 of the tracking data SFDU contain the aggregation CHDO label field, which is defined in Table 3-2.  The value field of the aggregation CHDO is composed of the primary CHDO and a secondary CHDO.  The primary CHDO is described in Section 3.1.3.  The secondary CHDOs, of which there are five types, are described in Section 3.1.4.

Table 3-2.  Aggregation CHDO Label Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the aggregation CHDO. A value of 1 indicates that this CHDO is an aggregation of CHDOs | Unsigned Integer –2 | N/A | 1 |  |
| chdo_length | 2 | Length attribute of the aggregation CHDO. Indicates the length of the sum of the primary and secondary CHDOs. CHDO 132 => 78 CHDO 133 => 122 CHDO 134 => 136 CHDO 135 => 100 CHDO 136 => 110 | Unsigned Integer –2 | Bytes | 78, 100, 110, 122, 136 |  |

### Primary CHDO

Bytes 24 through 31 of the tracking SFDU contain the primary CHDO, which is  defined in Table 3-3. Bytes 0 through 3 are the label field.  Bytes 4 through 7 are the value field.  The primary specifies the mission and the data type of the tracking data contained in the SFDU.

Table 3-3.  Primary CHDO Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the primary CHDO. A value of 2 indicates that this CHDO is a primary CHDO. | Unsigned Integer –2 | N/A | 2 |  |
| chdo_length | 2 | Length attribute of the primary CHDO. Indicates the length, in bytes, of the value field (bytes after this item) of the primary CHDO. | Unsigned Integer –2 | Bytes | 4 |  |
| mjr_data_class | 4 | Major data class. A value of 6 indicates that the data in this SFDU is ground station monitor data. | Unsigned Integer –1 | N/A | 6 |  |
| mnr_data_class | 5 | Minor data class. Indicates data is processed tracking data. | Unsigned Integer –1 | N/A | 14 |  |
| mission_id | 6 | Mission ID. Per Reference [3a], Table 3-4. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| format_code | 7 | Format code. Also referred to as the data type. 0 => Uplink Carrier Phase 1 => Downlink Carrier Phase 2 => Uplink Sequential Ranging Phase 3 => Downlink Sequential Ranging Phase 4 => Uplink PN Ranging Phase 5 => Downlink PN Ranging Phase 6 => Doppler 7 => Sequential Ranging 8 => Angles 9 => Ramps 10 => VLBI 11 => DRVID 12 => Smoothed Noise 13 => Allan Deviation 14 => PN Ranging 15 => Tone Ranging 16 => Carrier Observable 17 => Total Phase Observable | Unsigned Integer –1 | N/A | 0 to 17 |  |

### Secondary CHDOs

There are five types of secondary CHDOs, all of which start at Byte 32 of the tracking data SFDU.  The five types are organized as follows (data type is equivalent to format code):

- CHDO 134:  Derived data types - Doppler Count (data type 6), Sequential Range (data type 7), Angles (data type 8), DRVID (data type 11), PN Range (data type 14), Tone Range (data type 15), Carrier Frequency Observable (data type 16), and Total Count Phase Observable (data type 17).

- CHDO 132:  Uplink data types - Uplink Carrier Phase (data type 0), Uplink Sequential Ranging Phase (data type 2), Uplink PN Ranging Phase (data type 4), and Ramps (data type 9).

- CHDO 133:  Downlink data types - Downlink Carrier Phase (data type 1), Downlink Sequential Ranging Phase (data type 3), and Downlink PN Ranging Phase (data type 5).

- CHDO 135:  Interferometric data types - VLBI (data type 10).

- CHDO 136:  Filtered data types - Smoothed Noise (data type 12) and Allan Deviation (data type 13).

The secondary CHDOs are defined in Tables 3-4 through 3-8.  Bytes 0 through 3 are the label field.  Bytes 4 through M-1 (M being the length of the secondary CHDO) comprise the value field.  The secondary CHDO contains parameters that a user might want to sort or filter on.

#### Secondary CHDO 134 (Derived Data Types)

Secondary CHDO 134 is used for the following derived data types (format codes): Doppler Count (data type 6), Sequential Range (data type 7), Angle (data type 8), DRVID (data type 11), PN Range (data type 14),  Tone Range (data type 15), Carrier Frequency Observable (data type 16), and Total Count Phase Observable (data type 17).  Secondary CHDO 134 is defined in Table 3-4.

Table 3-4.  Secondary CHDO 134 Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the secondary CHDO. | Unsigned Integer –2 | N/A | 134 |  |
| chdo_length | 2 | Length attribute of the secondary CHDO. Indicates the length, in bytes, of the value field (bytes after this item) of the secondary CHDO. | Unsigned Integer –2 | Bytes | 124 |  |
| orig_id | 4 | Originator ID. Indicates where this SFDU was originated. Per Reference[4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| last_modifier_id | 5 | Last modifier ID. Indicates where this SFDU was last modified. Per Reference [4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| reserve1 | 6 | Reserved. For future expansion of scft_id. | Unsigned Integer –1 | N/A | 0 |  |
| scft_id | 7 | Spacecraft number. Per Reference [3a]. | Unsigned Integer –1 | N/A | 1 to 255 |  |
| rec_seq_num | 8 | Record sequence number (RSN). Begins with zero; increments by one for each successive tracking SFDU of the same type; wraps around from 232-1 to zero. Value is reset to zero when software is restarted. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| year | 12 | Time tag year. | Unsigned Integer –2 | N/A | 1958 to 3000 |  |
| doy | 14 | Time tag day of year. | Unsigned Integer –2 | N/A | 1 to 366 |  |
| sec | 16 | Time tag seconds of day. | IEEE Double | Seconds / 0.01 sec | 0.00 to 86,400.99 | 1 |
| rct_day | 24 | Record creation time days. Days since 1/1/1958. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 74 |
| rct_msec | 26 | Record creation time milliseconds of day. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 74 |
| stn_stream_src | 30 | Station stream source. 1 => UPL/DTT 2 => non-UPL-DTT: TRK-2-30 3 => non-UPL-DTT: TRK-2-20 | Unsigned Integer –1 | N/A | 1 to 3 |  |
| ul_band | 31 | Uplink frequency band. 0 => unknown or not applicable 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band | Unsigned Integer -1 | N/A | 0 to 5 | 79 |
| ul_assembly_num | 32 | Uplink Assembly Number. Note that this is to allow for potential future cases where there might be more than one uplink of the same band at the same antenna. 0 => Unknown/Not applicable 1 => S-/X-band uplink 2 => Ka-band uplink | Unsigned Integer –1 | N/A | 0 to 2 | 79 |
| transmit_num | 33 | Transmitter number. Value depends on transmitter used. A value of 0 means that the number is unknown or not applicable. | Unsigned Integer –1 | N/A | 0 to 3 | 79 |
| transmit_stat | 34 | Transmit Status. 0 => not transmitting out the horn 1 => transmitting out the horn 2 => invalid or unknown | Unsigned Integer –1 | N/A | 0 to 2 | 79 |
| transmit_mode | 35 | Transmitter mode. 0 => low power 1 => high power 2 => invalid or unknown | Unsigned Integer –1 | N/A | 0 to 2 | 79 |
| cmd_modul_stat | 36 | Command modulation status. 0 => OFF 1 => ON 2 => invalid or unknown | Unsigned Integer –1 | N/A | 0 to 2 | 79 |
| rng_modul_stat | 37 | Ranging modulation status. 0 => OFF 1 => ON 2 => invalid or unknown | Unsigned Integer –1 | N/A | 0 to 2 | 79 |
| transmit_time_tag_delay | 38 | Transmit time tag delay. Value used to offset uplink time tag (e.g., for Goldstone Beam Waveguide antennas). A value of -1.0 indicates invalid (or not provided). | IEEE Double | Seconds / 0.1 nsec | -1.0, 0.0 to 1.0 | 2, 79 |
| ul_zheight_corr | 46 | Uplink Z-height correction. Value of -99.0 indicates invalid. | IEEE Single | Seconds / 0.1 nsec | -99.0, -1.000 to 1.000 | 60, 72, 79 |
| dl_dss_id | 50 | Downlink antenna number. Per Reference [10]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| reserve1a | 51 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| dl_chan_num | 52 | Downlink channel number. Value of 0 implies unknown. | Unsigned Integer –1 | N/A | 0 to 24 |  |
| prdx_mode | 53 | Predicts mode. Predicts subset used by downlink channel. 0 => No Predicts 1 => One-way 2 => Two-way 3 => Three-way 4 => Unknown | Unsigned Integer –1 | N/A | 0 to 4 |  |
| ul_prdx_stn | 54 | Uplink station used for predicts. Valid only if prdx_mode is 2 or 3. Per Reference [10]. A value of 0 means that the number is unknown or not valid (e.g., no uplink). | Unsigned Integer –1 | N/A | 0 to 255 |  |
| ul_band_dl | 55 | Uplink frequency band assumed by downlink. Uplink band value used by downlink for turn around computations. 0 => Unknown or not applicable 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band | Unsigned Integer –1 | N/A | 0 to 5 |  |
| array_delay | 56 | Array delay value. Time delay added to path by arraying equipment. Obtained from arraying equipment. Any measurements include this delay. Valid only if Array Flag (array_flag) is non-zero. | IEEE Double | Seconds / 0.1 nsec | 0.0 to 1.0 | 4 |
| fts_vld_flag | 64 | Frequency and Timing (FTS) validity. 0 => Equipment is not synced with FTS 1 => Equipment is synced with FTS | Unsigned Integer –1 | N/A | 0 or 1 |  |
| carr_lock_stat | 65 | Carrier lock status. 0 => Off 1 => Open (using only predicts) 2 => Acquiring, FFT Search 3 => Acquiring, Waiting for Lock Decision 4 => In Lock 5 => Out of Lock | Unsigned Integer –1 | N/A | 0 to 5 | 83 |
| array_flag | 66 | Array flag. 0 => Non-arrayed 1 => Arrayed with FSP #1 2 => Arrayed with FSP #2 | Unsigned Integer –1 | N/A | 0 to 2 | 87 |
| lna_num | 67 | LNA Number. Value of 0 indicates unknown. | Unsigned Integer –1 | N/A | 0 to 4 |  |
| rcv_time_tag_delay | 68 | Receive time tag delay. Value used to offset downlink time tag (e.g., for Goldstone Beam Waveguide antennas). A value of -1.0 indicates invalid (or not provided). | IEEE Double | Seconds / 0.1 nsec | -1.0, 0.0 to 1.0 | 3 |
| dl_zheight_corr | 76 | Downlink Z-height correction. Value of -99.0 indicates invalid. | IEEE Single | Seconds / 0.1 nsec | -99.0, -1.000 to 1.000 | 60, 72 |
| vld_ul_stn | 80 | Validated uplink station. Per Reference [10]. The uplink station per the validation process. A value of 0 means that the antenna is unknown or not valid. | Unsigned Integer –1 | N/A | 0 to 255 | 61, 79 |
| vld_dop_mode | 81 | Validated doppler mode. 0 => Unknown or not applicable 1 => One-way 2 => Two-way 3 => Three-way | Unsigned Integer –1 | N/A | 0 to 3 | 61, 79 |
| vld_scft_coh | 82 | Validated spacecraft coherency. 0 => Unknown or not applicable 1 => Coherent 2 => Non-coherent 3 => Transponded, non-coherent | Unsigned Integer –1 | N/A | 0 to 3 | 79 |
| vld_dl_band | 83 | Validated downlink frequency band. 0 => unknown 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band 6 => S or X band (26m stations) | Unsigned Integer –1 | N/A | 0 to 6 | 82 |
| scft_transpd_lock | 84 | Spacecraft transponder lock. 0 => Unknown 1 => Out-of-lock 2 => In Lock | Unsigned Integer –1 | N/A | 0 to 2 | 5 |
| scft_transpd_num | 85 | Spacecraft transponder number. 0 if unknown, transponder number otherwise. | Unsigned Integer –1 | N/A | 0 to 5 | 5 |
| Reserve2 | 86 | Reserved. Two bytes. | Unsigned Integer –2 | N/A | 0 |  |
| scft_osc_freq | 88 | Spacecraft oscillator frequency. Spacecraft one-way frequency. 0.0 if unknown. | IEEE Double | Hz / 1.0 mHz | 0.0, 2.0e9 to 32.3e9 | 6 |
| scft_transpd_delay | 96 | Spacecraft transponder delay. Coherent ranging delay. Value of -1.0 indicates invalid. | IEEE Double | Seconds / 0.1 nsec | -1.0, 0.0 to 1.0 | 7 |
| scft_transpd_turn_num | 104 | Spacecraft transponder turn around ratio numerator. A value of 0 indicates unknown. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| scft_transpd_turn_den | 108 | Spacecraft transponder turn around ratio denominator. A value of 0 indicates unknown. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| scft_twnc_stat | 112 | Spacecraft two-way non-coherent (TWNC) status. 0 => Unknown 1 => OFF 2 => ON | Unsigned Integer-1 | N/A | 0 to 2 | 5 |
| scft_osc_type | 113 | Spacecraft oscillator type. 0 => Unknown 1 => AUX OSC (auxiliary oscillator) 2 => USO (ultra-stable oscillator) | Unsigned Integer –1 | N/A | 0 to 2 | 5 |
| mod_day | 114 | Modification time days. Days since 1/1/1958. Last modification time. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 73 |
| mod_msec | 116 | Modification time milliseconds of day. Last modification time. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 73 |
| cnt_time | 120 | Count time. Integration time of the counts. Value of 0 indicates Not Applicable | IEEE Single | Seconds / 0.1 sec | 0.0 to 3600.0 | 88 |
| Reserve4 | 124 | Reserved. Four bytes. | Unsigned Integer –4 | N/A | 0 |  |

#### Secondary CHDO 132 (Uplink Data Types)

Secondary CHDO 132 is used for the following Uplink data types (format codes): Uplink Carrier Phase (data type 0), Uplink Sequential Ranging Phase (data type 2), Uplink PN Ranging Phase (data type 4), and Ramps (data type 9).  Secondary CHDO 132 is defined in Table 3-5.

Table 3-5.  Secondary CHDO 132 Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the secondary CHDO. | Unsigned Integer –2 | N/A | 132 |  |
| chdo_length | 2 | Length attribute of the secondary CHDO. Indicates the length, in bytes, of the value field (bytes after this item) of the secondary CHDO. | Unsigned Integer –2 | bytes | 66 |  |
| orig_id | 4 | Originator ID. Indicates where this SFDU was originated. Per Reference [4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| last_modifier_id | 5 | Last modifier ID. Indicates where the contents of this SFDU were last modified. Per Reference [4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| reserve1 | 6 | Reserved. For future expansion of scft_id. | Unsigned Integer –1 | N/A | 0 |  |
| scft_id | 7 | Spacecraft number. Per Reference [3a]. | Unsigned Integer –1 | N/A | 1 to 255 |  |
| upl_rec_seq_num | 8 | Uplink record sequence number (UPL RSN). This is the record sequence number reported by the uplink subsystem (UPL) equipment. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| rec_seq_num | 12 | Record sequence number (RSN). Begins with zero; increments by one for each successive uplink tracking SFDU of the same data type; wraps around from 232-1 to zero. Value is reset to zero when the data processing system software is restarted. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| year | 16 | Time tag year. | Unsigned Integer –2 | N/A | 1958 to 3000 |  |
| doy | 18 | Time tag day of year. | Unsigned Integer –2 | N/A | 1 to 366 |  |
| sec | 20 | Time tag seconds of day. | IEEE Double | Seconds / 0.01 sec | 0.00 to 86,400.99 | 1 |
| rct_day | 28 | Record creation time days. Days since 1/1/1958. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 74 |
| rct_msec | 30 | Record creation time milliseconds of day. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 74 |
| ul_dss_id | 34 | Uplink antenna number. Per Reference [10]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| ul_band | 35 | Uplink frequency band. 0 => unknown 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band | Unsigned Integer –1 | N/A | 0 to 5 |  |
| ul_assembly_num | 36 | Uplink Assembly Number. Note that this is to allow for potential future cases where there might be more than one uplink of the same band at the same antenna. 1 => S-/X-band uplink 2 => Ka-band uplink | Unsigned Integer –1 | N/A | 1 or 2 |  |
| transmit_num | 37 | Transmitter number. Value depends on transmitter used. A value of 0 indicates unknown. | Unsigned Integer –1 | N/A | 0 to 3 |  |
| transmit_stat | 38 | Transmit status. 0 => not transmitting out the horn 1 => transmitting out the horn 2 => invalid/unknown | Unsigned Integer –1 | N/A | 0 to 2 |  |
| transmit_mode | 39 | Transmitter mode. 0 => low power 1 => high power 2 => invalid/unknown | Unsigned Integer –1 | N/A | 0 to 2 |  |
| cmd_modul_stat | 40 | Command modulation status. 0 => OFF 1 => ON 2 => invalid/unknown | Unsigned Integer –1 | N/A | 0 to 2 |  |
| rng_modul_stat | 41 | Ranging modulation status. 0 => OFF 1 => ON 2 => invalid/unknown | Unsigned Integer –1 | N/A | 0 to 2 |  |
| fts_vld_flag | 42 | Frequency and Timing (FTS) validity. 0 => Equipment is not synced with FTS 1 => Equipment is synced with FTS | Unsigned Integer –1 | N/A | 0 or 1 |  |
| reserve1a | 43 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| transmit_time_tag_delay | 44 | Transmit time tag delay. Value used to offset uplink time tag (e.g., for Goldstone Beam Waveguide antennas). Value of -1.0 indicates invalid (or not provided). | IEEE Double | seconds / 0.1 nsec | -1.0, 0.0 to 1.0 | 2 |
| ul_zheight_corr | 52 | Uplink Z-height correction. Value of -99.0 indicates invalid. | IEEE Single | seconds / 0.1 nsec | -99.0, -1.000 to 1.000 | 60 |
| mod_day | 56 | Modification time days. Days since 1/1/1958. Last modification time. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 73 |
| mod_msec | 58 | Modification time milliseconds of day. Last modification time. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 73 |
| reserve8 | 62 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

#### Secondary CHDO 133 (Downlink Data Types)

Secondary CHDO 133 is used for the following Downlink data types (format codes):  Downlink Carrier Phase (data type 1), Downlink Sequential Ranging Phase (data type 3), and Downlink PN Ranging Phase (data type 5).  Secondary CHDO 133 is defined in Table 3-6.

Table 3-6.  Secondary CHDO 133 Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the secondary CHDO. | Unsigned Integer –2 | N/A | 133 |  |
| chdo_length | 2 | Length attribute of the secondary CHDO. Indicates the length, in bytes, of the value field (bytes after this item) of the secondary CHDO. | Unsigned Integer –2 | bytes | 110 |  |
| orig_id | 4 | Originator ID. Indicates where this SFDU was originated. Per Reference [4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| last_modifier_id | 5 | Last modifier ID. Indicates where the contents of this SFDU were last modified. Per Reference [4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| reserve1 | 6 | Reserved. For future expansion of scft_id. | Unsigned Integer –1 | N/A | 0 |  |
| scft_id | 7 | Spacecraft number. Per Reference [3a]. | Unsigned Integer –1 | N/A | 1 to 255 |  |
| dtt_rec_seq_num | 8 | Downlink Record sequence number (DTT RSN). This is the record sequence number reported by the downlink subsystem (DTT) equipment. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| rec_seq_num | 12 | Record sequence number (RSN). Begins with zero; increments by one for each successive downlink tracking SFDU of the same data type; wraps around from 232-1 to zero. Value is reset to zero when the data processing system software is restarted. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| year | 16 | Time tag year. | Unsigned Integer –2 | N/A | 1958 to 3000 |  |
| doy | 18 | Time tag day of year. | Unsigned Integer –2 | N/A | 1 to 366 |  |
| sec | 20 | Time tag seconds of day. | IEEE Double | Seconds / 0.01 sec | 0.00 to 86,400.99 | 1 |
| rct_day | 28 | Record creation time days. Days since 1/1/1958. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 74 |
| rct_msec | 30 | Record creation time milliseconds of day. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 74 |
| dl_dss_id | 34 | Downlink antenna number. Per Reference [10]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| dl_band | 35 | Downlink frequency band. 0 => Unknown 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band | Unsigned Integer –1 | N/A | 0 to 5 |  |
| dl_chan_num | 36 | Downlink channel number. | Unsigned Integer –1 | N/A | 1 to 24 |  |
| prdx_mode | 37 | Predicts mode. Predicts subset used by downlink channel. 0 => No Predicts 1 => One-way 2 => Two-way 3 => Three-way | Unsigned Integer –1 | N/A | 0 to 3 |  |
| ul_prdx_stn | 38 | Uplink station used for predicts. Valid only if prdx_mode is 2 or 3. Per Reference [10]. A value of 0 means that the number is unknown or not valid (e.g., no uplink). | Unsigned Integer –1 | N/A | 0 to 255 |  |
| ul_band_dl | 39 | Uplink frequency band assumed by downlink. 0 => Unknown 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band | Unsigned Integer –1 | N/A | 0 to 5 |  |
| array_delay | 40 | Array delay value. Time delay added to path by arraying equipment. Obtained from arraying equipment. Any measurements include this delay. Valid only if Array Flag (array_flag) is non-zero. | IEEE Double | seconds / 0.1 nsec | 0.0 to 1.0 | 4 |
| fts_vld_flag | 48 | Frequency and Timing (FTS) validity. 0 => Equipment is not synced with FTS 1 => Equipment is synced with FTS | Unsigned Integer –1 | N/A | 0 or 1 |  |
| carr_lock_stat | 49 | Carrier lock status. 0 => Off 1 => Open (only using predicts) 2 => Acquiring, FFT Search 3 => Acquiring, Waiting for Lock Decision 4 => In Lock 5 => Out of Lock | Unsigned Integer –1 | N/A | 0 to 5 |  |
| array_flag | 50 | Array flag. 0 => Not arrayed 1 => Arrayed with FSP #1 2 => Arrayed with FSP #2 | Unsigned Integer –1 | N/A | 0 to 2 | 87 |
| polarization | 51 | Polarization. 0 => RCP 1 => LCP | Unsigned Integer –1 | N/A | 0 or 1 |  |
| diplxr_stat | 52 | Diplexer status. 0 => Low noise 1 => Diplexed | Unsigned Integer –1 | N/A | 0 or 1 |  |
| lna_num | 53 | LNA Number. | Unsigned Integer –1 | N/A | 1 to 4 |  |
| rf_if_chan_num | 54 | RF-to-IF Downconverter Channel number. | Unsigned Integer –1 | N/A | 1 or 2 |  |
| if_num | 55 | IF input number. Defines path into downlink channel. | Unsigned Integer –1 | N/A | 1 to 3 |  |
| rcv_time_tag_delay | 56 | Receive time tag delay. Value used to offset downlink time tag (e.g., for Goldstone Beam Waveguide antennas). A value of -1.0 indicates invalid (or not provided). | IEEE Double | seconds / 0.1 nsec | -1.0, 0.0 to 1.0 | 3 |
| dl_zheight_corr | 64 | Downlink Z-height correction. Value of -99.0 indicates invalid. | IEEE Single | seconds / 0.1 nsec | -99.0, -1.000 to 1.000 | 60 |
| vld_ul_stn | 68 | Validated uplink station. Per Reference [10]. The uplink station per the validation process. A value of 0 means that the antenna is unknown or not valid. | Unsigned Integer –1 | N/A | 0 to 255 | 61, 79 |
| vld_dop_mode | 69 | Validated doppler mode. 0 => Unknown or not applicable 1 => One-way 2 => Two-way 3 => Three-way | Unsigned Integer –1 | N/A | 0 to 3 | 61, 79 |
| vld_scft_coh | 70 | Validated spacecraft coherency. 0 => Unknown or not applicable 1 => Coherent 2 => Non-coherent 3 => Transponded, non-coherent | Unsigned Integer –1 | N/A | 0 to 3 | 79 |
| scft_transpd_lock | 71 | Spacecraft transponder lock. 0 => Unknown 1 => Out-of-lock 2 => In Lock | Unsigned Integer –1 | N/A | 0 to 2 | 5 |
| scft_transpd_num | 72 | Spacecraft transponder number. 0 if unknown, transponder number otherwise. | Unsigned Integer –1 | N/A | 0 to 5 | 5 |
| reserve1a | 73 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| scft_osc_freq | 74 | Spacecraft oscillator frequency. Spacecraft one-way frequency. 0.0 if unknown. | IEEE Double | Hz / 1 mHz | 0.0, 2.0e9 to 32.3e9 | 6 |
| scft_transpd_delay | 82 | Spacecraft transponder delay. Coherent ranging delay. Value of -1.0 indicates invalid. | IEEE Double | Seconds / 0.1 nsec | -1.0, 0.0 to 1.0 | 7 |
| scft_transpd_turn_num | 90 | Spacecraft transponder turn around ratio numerator. A value of 0 indicates unknown. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| scft_transpd_turn_den | 94 | Spacecraft transponder turn around ratio denominator. A value of 0 indicates unknown. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| scft_twnc_stat | 98 | Spacecraft two-way non-coherent (TWNC) status. 0 => Unknown 1 => OFF 2 => ON | Unsigned Integer –1 | N/A | 0 to 2 | 5 |
| scft_osc_type | 99 | Spacecraft oscillator type. 0 => Unknown 1 => AUX OSC (auxiliary oscillator) 2 => USO (ultra-stable oscillator) | Unsigned Integer –1 | N/A | 0 to 2 | 5 |
| mod_day | 100 | Modification time days. Days since 1/1/1958. Last modification time. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 73 |
| mod_msec | 102 | Modification time milliseconds of day. Last modification time. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 73 |
| reserve8 | 106 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

#### Secondary CHDO 135 (Interferometric Data Types)

Secondary CHDO 135 is used for the following Interferometric data type (format code): VLBI (data type 10). Secondary CHDO 135 is defined in Table 3-7.

Table 3-7.  Secondary CHDO 135 Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the secondary CHDO. | Unsigned Integer –2 | N/A | 135 |  |
| chdo_length | 2 | Length attribute of the secondary CHDO. Indicates the length, in bytes, of the value field (bytes after this item) of the secondary CHDO. | Unsigned Integer –2 | bytes | 88 |  |
| orig_id | 4 | Originator ID. Indicates where this SFDU was originated. Per Reference [4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| last_modifier_id | 5 | Last modifier ID. Indicates that the contents of this SFDU were last modified by the VLBI system. Per Reference [4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| reserve1 | 6 | Reserved. For future expansion of scft_id. | Unsigned Integer –1 | N/A | 0 |  |
| scft_id | 7 | Spacecraft number. Per Reference [3a] (set to 0 if quasar sample). | Unsigned Integer –1 | N/A | 1 to 255 |  |
| rec_seq_num | 8 | Record sequence number (RSN). Begins with zero; increments by one for each successive VLBI tracking SFDU of the same data type; wraps around from 232-1 to zero. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| year | 12 | Time tag year. | Unsigned Integer –2 | N/A | 1958 to 3000 |  |
| doy | 14 | Time tag day of year. | Unsigned Integer –2 | N/A | 1 to 366 |  |
| sec | 16 | Time tag seconds of day. | IEEE Double | seconds / 0.1 msec | 0.00 to 86,400.9999 | 1 |
| rct_day | 24 | Record creation time days. Days since 1/1/1958. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 74 |
| rct_msec | 26 | Record creation time milliseconds of day. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 74 |
| ul_dss_id | 30 | Primary uplink antenna number. Per Reference [10]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| dl_dss_id | 31 | Primary downlink antenna number. Per Reference [10]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| dl_band | 32 | Downlink frequency band. 0 => unknown 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band | Unsigned Integer –1 | N/A | 0 to 5 |  |
| dl_chan_num | 33 | Downlink channel number. | Unsigned Integer –1 | N/A | 1 to 24 |  |
| prdx_mode | 34 | Predicts mode. 0 => No Predicts 1 => One-way 2 => Two-way 3 => Three-way | Unsigned Integer –1 | N/A | 0 to 3 |  |
| ul_prdx_stn | 35 | Uplink station used for predicts. Valid only if prdx_mode is 2 or 3. Per Reference [10]. A value of 0 means that the number is unknown or not valid (e.g., no uplink). | Unsigned Integer –1 | N/A | 0 to 255 |  |
| ul_band_dl | 36 | Uplink frequency band assumed by downlink. 0 => Unknown 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band | Unsigned Integer –1 | N/A | 0 to 5 |  |
| rec_type | 37 | Record type. 71 => spacecraft DOD 72 => quasar DOD 73 => spacecraft DOR 74 => quasar DOR | Unsigned Integer –1 | N/A | 71 to 74 |  |
| rcv_time_tag_delay | 38 | Receive time tag delay at primary antenna. Value used to offset downlink time tag (e.g, for Goldstone Beam Waveguide antennas). A value of -1.0 indicates invalid (or not provided). | IEEE Double | seconds / 0.1 nsec | -1.0, 0.0 to 1.0 |  |
| array_delay | 46 | Array delay value at primary antenna. Time delay added to path by arraying equipment. Obtained from arraying equipment. Any measurements include this delay. Valid only if Array Flag (array_flag) is non-zero. | IEEE Double | seconds / 0.1 nsec | 0.0 to 1.0 | 4 |
| dl_dss_id_2 | 54 | Secondary downlink antenna number. Per Reference [10]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| reserve1a | 55 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| rcv_time_tag_ delay_2 | 56 | Receive time tag delay at secondary antenna. Value used to offset downlink time tag (e.g., for Goldstone Beam Waveguide antennas). A value of -1.0 indicates invalid (or not provided). | IEEE Double | seconds / 0.1 nsec | -1.0, 0.0 to 1.0 |  |
| array_delay_2 | 64 | Array delay value at secondary antenna. Time delay added to path by arraying equipment. Obtained from arraying equipment. Any measurements include this delay. Valid only if Secondary Antenna Array Flag (array_flag_2) is non-zero. | IEEE Double | seconds / 0.1 nsec | 0.0 to 1.0 | 4 |
| fts_vld_flag | 72 | Frequency and Timing (FTS) validity. 0 => Equipment is not synced with FTS 1 => Equipment is synced with FTS | Unsigned Integer –1 | N/A | 0 or 1 |  |
| carr_lock_stat | 73 | Carrier lock status. 0 => Off 1 => Open 2 => Acquiring, FFT Search 3 => Acquiring, Waiting for Lock Decision 4 => In Lock 5 => Out-of-Lock | Unsigned Integer –1 | N/A | 0 to 5 |  |
| array_flag | 74 | Array flag for primary antenna. 0 => Not arrayed 1 => Arrayed with FSP #1 2 => Arrayed with FSP #2 | Unsigned Integer –1 | N/A | 0 to 2 | 87 |
| source_type | 75 | VLBI source. 0 => quasar 1 => spacecraft | Unsigned Integer –1 | N/A | 0 or 1 |  |
| lna_num | 76 | LNA Number. | Unsigned Integer –1 | N/A | 1 to 4 |  |
| array_flag_2 | 77 | Array flag for secondary antenna. 0 => Not arrayed 1 => Arrayed with FSP #1 2 => Arrayed with FSP #2 | Unsigned Integer –1 | N/A | 0 to 2 | 87 |
| mod_day | 78 | Modification time days. Days since 1/1/1958. Last modification time. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 73 |
| mod_msec | 80 | Modification time milliseconds of day. Last modification time. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 73 |
| reserve8 | 84 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

#### Secondary CHDO 136 (Filtered Data Types)

Secondary CHDO 136 is used for the following Filtered data types (format codes): Smoothed Noise (data type 12) and Allan Deviation (data type 13).  These data types are only generated for DTT-type antennas.  Secondary CHDO 136 is defined in Table 3-8.

Table 3-8.  Secondary CHDO 136 Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the secondary CHDO. | Unsigned Integer –2 | N/A | 136 |  |
| chdo_length | 2 | Length attribute of the secondary CHDO. Indicates the length, in bytes, of the value field (bytes following this item) of the secondary CHDO. | Unsigned Integer –2 | Bytes | 98 |  |
| orig_id | 4 | Originator ID. Indicates where this SFDU was originated. Per Reference [4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| last_modifier_id | 5 | Last modifier ID. Indicates where the contents of this SFDU were last modified. Per Reference [4]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| reserve1 | 6 | Reserved. For future expansion of scft_id. | Unsigned Integer –1 | N/A | 0 |  |
| scft_id | 7 | Spacecraft number. Per Reference [3a]. | Unsigned Integer –1 | N/A | 1 to 255 |  |
| rec_seq_num | 8 | Record sequence number (RSN). Begins with zero; increments by one for each successive filtered SFDU of the same data type; wraps around from 232-1 to zero. Value is reset to zero when the data processing system software is restarted. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| year | 12 | Time tag year. | Unsigned Integer –2 | N/A | 1958 to 3000 |  |
| doy | 14 | Time tag day of year. | Unsigned Integer –2 | N/A | 1 to 366 |  |
| sec | 16 | Time tag seconds of day. | IEEE Double | seconds / 0.01 sec | 0.00 to 86,400.99 | 1 |
| rct_day | 24 | Record creation time days. Days since 1/1/1958. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 74 |
| rct_msec | 26 | Record creation time milliseconds of day. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 74 |
| dl_dss_id | 30 | Downlink antenna number. Per Reference [10]. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| dl_band | 31 | Downlink frequency band. 0 => unknown 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band | Unsigned Integer –1 | N/A | 0 to 5 |  |
| dl_chan_num | 32 | Downlink channel number. | Unsigned Integer –1 | N/A | 1 to 24 |  |
| prdx_mode | 33 | Predicts mode. 0 => No Predicts 1 => One-way 2 => Two-way 3 => Three-way | Unsigned Integer –1 | N/A | 0 to 3 |  |
| ul_prdx_stn | 34 | Uplink station used for predicts. Valid only if prdx_mode is 2 or 3. Per Reference [10]. A value of 0 means that the number is unknown or not valid (e.g., no uplink). | Unsigned Integer –1 | N/A | 0 to 255 |  |
| ul_band_dl | 35 | Uplink band assumed by downlink. 0 => Unknown or not applicable 1 => S-band 2 => X-band 3 => Ka-band 4 => Ku-band 5 => L-band | Unsigned Integer –1 | N/A | 0 to 5 |  |
| rcv_time_tag_ delay | 36 | Receive time tag delay. Value used to offset downlink time tag (e.g., for Goldstone Beam Waveguide antennas). A value of -1.0 indicates invalid (or not provided). | IEEE Double | seconds / 0.1 nsec | -1.0, 0.0 to 1.0 | 3 |
| array_delay | 44 | Array delay value. Time delay added to path by arraying equipment. Obtained from arraying equipment. Any measurements include this delay. Valid only if Array Flag (array_flag) is non-zero. | IEEE Double | seconds / 0.1 nsec | 0.0 to 1.0 | 4 |
| fts_vld_flag | 52 | Frequency and Timing (FTS) validity. 0 => Equipment is not synced with FTS 1 => Equipment is synced with FTS | Unsigned Integer –1 | N/A | 0 or 1 |  |
| carr_lock_stat | 53 | Carrier lock status. 0 => Off 1 => Open (only using predicts) 2 => Acquiring, FFT Search 3 => Acquiring, Waiting for Lock Decision 4 => In Lock 5 => Out of Lock | Unsigned Integer –1 | N/A | 0 to 5 |  |
| array_flag | 54 | Array flag. 0 => Not arrayed 1 => Arrayed with FSP #1 2 => Arrayed with FSP #2 | Unsigned Integer –1 | N/A | 0 to 2 | 87 |
| lna_num | 55 | LNA Number. | Unsigned Integer –1 | N/A | 1 to 4 |  |
| vld_ul_stn | 56 | Validated uplink station. Per Reference [10]. The uplink station per the validation process. A value of 0 means that the antenna is unknown or not valid. | Unsigned Integer –1 | N/A | 0 to 255 | 61, 79 |
| vld_dop_mode | 57 | Validated doppler mode. 0 => Unknown or not applicable 1 => One-way 2 => Two-way 3 => Three-way | Unsigned Integer –1 | N/A | 0 to 3 | 61, 79 |
| vld_scft_coh | 58 | Validated spacecraft coherency. 0 => Unknown or not applicable 1 => Coherent 2 => Non-coherent 3 => Transponded, non-coherent | Unsigned Integer –1 | N/A | 0 to 3 | 79 |
| scft_transpd_lock | 59 | Spacecraft transponder lock. 0 => Unknown 1 => Out-of-lock 2 => Locked | Unsigned Integer –1 | N/A | 0 to 2 | 5 |
| scft_transpd_num | 60 | Spacecraft transponder number. 0 if unknown, transponder number otherwise. | Unsigned Integer –1 | N/A | 0 to 5 | 5 |
| reserve1a | 61 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| scft_osc_freq | 62 | Spacecraft oscillator frequency. Spacecraft one-way frequency. 0.0 if unknown. | IEEE Double | Hz / 1 mHz | 0.0, 2.0e9 to 32.3e9 | 6 |
| scft_transpd_delay | 70 | Spacecraft transponder delay. Coherent ranging delay. Value of -1.0 indicates invalid. | IEEE Double | Seconds / 0.1 nsec | -1.0, 0.0 to 1.0 | 7 |
| scft_transpd_turn_num | 78 | Spacecraft transponder turn around ratio numerator. A value of 0 indicates unknown. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| scft_transpd_turn_den | 82 | Spacecraft transponder turn around ratio denominator. A value of 0 indicates unknown. | Unsigned Integer –4 | N/A | 0 to 232-1 |  |
| scft_twnc_stat | 86 | Spacecraft two-way non-coherent (TWNC) status. 0 => Unknown 1 => OFF 2 => ON | Unsigned Integer –1 | N/A | 0 to 2 | 5 |
| scft_osc_type | 87 | Spacecraft oscillator type. 0 => Unknown 1 => AUX OSC (auxiliary oscillator) 2 => USO (ultra-stable oscillator) | Unsigned Integer –1 | N/A | 0 to 2 | 5 |
| mod_day | 88 | Modification time days. Days since 1/1/1958. Last modification time. | Unsigned Integer –2 | Days / 1 day | 0 to 216 - 1 | 73 |
| mod_msec | 90 | Modification time milliseconds of day. Last modification time. | Unsigned Integer –4 | msec / 1 msec | 0 to 86,400,999 | 73 |
| reserve8 | 94 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

### Tracking Data CHDOs

There are 18 types of Tracking Data CHDOs, split into five categories: uplink data, downlink data, derived data, interferometric data, and filtered data.  Uplink data are the validated uplink phases from the UPL-DTT antennas and the uplink ramps.  Downlink data are the validated downlink phases from the UPL-DTT antennas.  Derived data are the data from the non-UPL-DTT antennas, and the processed doppler, range and DRVID data from the UPL-DTT antennas.  Interferometric data are the VLBI data.  Filtered data are the measurements derived from the accumulated downlink carrier phase data (smoothed noise and Allan Deviation) and are only available for UPL-DTT antennas.  The data types are as follows:

- Uplink Data

- Uplink Carrier Phase (data type 0)

- Uplink Sequential Ranging Phase (data type 2)

- Uplink PN Ranging Phase (data type 4)

- Ramp (data type 9)

- Downlink Data

- Downlink Carrier Phase (data type 1)

- Downlink Sequential Ranging Phase (data type 3)

- Downlink PN Ranging Phase (data type 5)

- Derived Data

- Doppler Count (data type 6)

- Sequential Range (data type 7)

- Angle (data type 8)

- DRVID (data type 11)

- PN Range (data type 14)

- Tone Range (data type 15)

- Carrier Frequency Observable (data type 16)

- Total Count Phase Observable (data type 17)

- Interferometric Data

- VLBI (data type 10)

- Filtered Data

- Smoothed Noise (data type 12)

- Allan Deviation (data type 13)

#### Uplink Data CHDOs

There are four Uplink Data CHDOs: Uplink Carrier Phase (data type 0), Uplink Sequential Ranging Phase (data type 2), Uplink PN Ranging Phase (data type 4), and Ramp (data type 9).  Their formats and contents are specified in sections 3.1.5.1.1 to 3.1.5.1.4.

##### Uplink Carrier Phase CHDO (Data Type 0)

The Uplink Carrier Phase CHDO is defined in Table 3-9.

Table 3-9. Uplink Carrier Phase CHDO (Data Type 0) Definitions

| Identifier | Byte Offsets | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the uplink carrier phase data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the uplink carrier phase data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 76 |  |
| ul_hi_phs_cycles | 4 | High part phase data whole cycles. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| ul_lo_phs_cycles | 8 | Low part phase data whole cycles. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| ul_frac_phs_cycles | 12 | Fractional part phase data cycles. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| ramp_freq | 16 | Ramp frequency. Precision varies with band (phase data gives higher precision). A value of 0.0 indicates an invalid or unknown value S-band => 0.5 (Hz X-band => 1.6 (Hz Ka-band => 7.7 (Hz | IEEE Double | Sky level Hz, at least 7.7 (Hz precision (band dependent) | 0.0, 2.0e9 to 34.7e9 |  |
| ramp_rate | 24 | Ramp rate. | IEEE Double | Sky level Hz/sec, (Hz/sec precision | -3.2e5 to 3.2e5 |  |
| transmit_switch_stat | 32 | Transmitter switch status. 0 => antenna 1 => water load 2 => invalid/unknown | Unsigned Integer –1 | N/A | 0 to 2 |  |
| ramp_type | 33 | Ramp type. 0 => snap 1 => start of new ramp 2 => medial report 3 => periodic report 4 => end of ramps 5 => ramping terminated by operator 6 => invalid/unknown | Unsigned Integer –1 | N/A | 0 to 6 |  |
| transmit_op_pwr | 34 | Transmitter output power. | IEEE Single | W / 0.1 W | 0.0 to 500,000.0 |  |
| sup_data_id | 38 | Support data ID. Name of the frequency predicts set used. | ASCII –8 | N/A | ASCII string |  |
| sup_data_rev | 46 | Support data revision. Revision of the frequency predicts set used. | ASCII –8 | N/A | ASCII string |  |
| prdx_time_offset | 54 | Predicts time offset. Seconds added to current time. | IEEE Double | Seconds / 0.1 sec | -31,536,000.0 to 31,536,000.0 | 54 |
| prdx_freq_offset | 62 | Predicts frequency offset. Hz added to predicted value. | IEEE Double | Hz / 1 mHz | -4.8e6 to 4.8e6 | 55 |
| time_tag_corr_flag | 70 | Time tag correction flag. Indicates results of validation of the block time tag. 0 => no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| type_time_corr_flag | 71 | Type of time tag correction flag. Indicates what type of time tag correction was made. 0 => no correction 1 => Year correction 2 => DOY correction 3 => Both Year and DOY correction | Unsigned Integer –1 | N/A | 0 to 3 |  |
| reserve8 | 72 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### Uplink Sequential Ranging Phase CHDO (Data Type 2)

The Uplink Sequential Ranging Phase CHDO is defined in Table 3-10.

Table 3-10. Uplink Sequential Ranging Phase CHDO (Data Type 2) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the uplink sequential ranging phase data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the uplink sequential ranging phase data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 108 |  |
| stn_cal | 4 | Station calibration value. (Two-way). Value includes the equipment in the path, but not the Z-height correction. (0.0 if not measured.) | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.8e5 | 24 |
| ul_stn_cal | 12 | Uplink station calibration value. Value includes the uplink equipment in the path, but not the Z-height correction. (0.0 if not measured.) | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.8e5 | 10,24 |
| ul_cal_freq | 20 | Uplink calibration frequency. Frequency the calibration was done at. | IEEE Double | Sky level Hz / 1 mHz | 2.0e9 to 34.4e9 |  |
| cal_std_dev | 28 | Standard deviation of station calibration value. For stn_cal and ul_stn_cal. | IEEE Single | Range Units / 0.01 RU | 0.0 to 1.8e5 | 24 |
| cal_pts | 32 | Calibration points. Number of measurements made in computing station calibration values (stn_cal, ul_stn_cal, cal_std_dev). | Unsigned Integer –2 | N/A | 0 to 65,535 |  |
| ul_rng_phs | 34 | Measured range phase. Range phase. | IEEE Double | Range Units / 0.01 RU | 0.0 to 230 | 11,24 |
| transmit_switch_stat | 42 | Transmitter switch status. 0 => antenna 1 => water load 2 => invalid/unknown | Unsigned Integer –1 | N/A | 0 to 2 |  |
| invert | 43 | Invert. Polarity of modulation. 0 => not inverted 1 => inverted | Unsigned Integer –1 | N/A | 0 or 1 | 52 |
| transmit_op_pwr | 44 | Transmitter output power. | IEEE Single | W / 0.1 W | 0.0 to 500,000.0 |  |
| template_id | 48 | Template ID. Value is the file name of the ranging parameter file. | ASCII –8 | N/A | ASCII string |  |
| t1 | 56 | T1 setting. | Unsigned Integer –2 | Seconds / 1 sec | 1 to 3600 | 12 |
| t2 | 58 | T2 setting. | Unsigned Integer –2 | Seconds / 1 sec | 1 to 1800 | 13 |
| t3 | 60 | T3 setting. | Unsigned Integer –2 | Seconds / 1 sec | 0 to 1800 | 14 |
| first_comp_num | 62 | First component number. | Unsigned Integer –1 | N/A | 1 to 24 | 15 |
| last_comp_num | 63 | Last component number. | Unsigned Integer –1 | N/A | 1 to 24 | 15 |
| chop_comp_num | 64 | Chop component number. This is the component used to chop the other components. | Unsigned Integer –1 | N/A | 0 to 10 | 15,16 |
| num_drvid | 65 | Number of DRVID measurements. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| transmit_inphs_time_year | 66 | Transmit In-phase time – year. Year of the time of zero phase on uplink range generation. | Unsigned Integer –2 | N/A | 1958 to 3000 | 75 |
| transmit_inphs_time_doy | 68 | Transmit In-phase time – day of year. Day of year of the time of zero phase on uplink range generation. | Unsigned Integer –2 | N/A | 1 to 366 | 75 |
| transmit_inphs_time_sec | 70 | Transmit In-phase time – seconds of day. Seconds of day of the time of zero phase on uplink range generation. | IEEE Double | Seconds / 1 (sec | 0.000000 to 86,400.999999 | 75 |
| carr_sup_rng_modul | 78 | Carrier Suppression by ranging modulation. Reduction in carrier power due to ranging modulation. | IEEE Single | dB / 0.1 dB | 0.0 to -15.0 |  |
| rng_modul_amp | 82 | Ranging modulation amplitude. Actual digital modulation amplitude used by the ranging hardware. | Unsigned Integer –2 | N/A | 0 to 212 |  |
| exc_scalar_num | 84 | Exciter Scalar Numerator. Numerator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| exc_scalar_den | 88 | Exciter Scalar Denominator. Denominator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| rng_cycle_time | 92 | Ranging cycle time. Time to complete one cycle of the ranging code. | IEEE Double | Seconds / 0.1 sec | 4.0 to 504,536.0 | 18 |
| time_tag_corr_flag | 100 | Time tag correction flag. Indicates results of validation of the block time tag. 0 => no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| type_time_corr_flag | 101 | Type of time tag correction flag. Indicates what type of time tag correction was made. 0 => no correction 1 => Year correction 2 => DOY correction 3 => Both Year and DOY correction | Unsigned Integer –1 | N/A | 0 to 3 |  |
| clock_waveform | 102 | Clock waveform type. 0 => squarewave 1 => sinewave | Unsigned Integer -1 | N/A | 0 or 1 |  |
| chop_start_num | 103 | Chop Start. The first component chopped. | Unsigned Integer –1 | N/A | 0 to 25 | 16 |
| reserve8 | 104 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### Uplink PN Ranging Phase CHDO (Data Type 4)

The Uplink PN Ranging Phase CHDO is defined in Table 3-11.

Table 3-11. Uplink PN Ranging Phase CHDO (Data Type 4) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the uplink PN ranging phase data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the uplink PN ranging phase data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 132 |  |
| stn_cal | 4 | Station calibration value. (two-way). Value includes the equipment in the path, but not the Z-height correction. (0.0 if not measured.) | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.8e5 | 24 |
| ul_stn_cal | 12 | Uplink station calibration value. Value includes the uplink equipment in the path, but not the Z-height correction. (0.0 if not measured.) | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.8e5 | 10,24 |
| ul_cal_freq | 20 | Uplink calibration frequency. Frequency the calibration was done at. | IEEE Double | Sky level Hz / 1 mHz | 2.0e9 to 34.4e9 |  |
| cal_std_dev | 28 | Standard deviation of station calibration value. For stn_cal and ul_stn_cal. | IEEE Single | Range Units / 0.01 RU | 0.0 to 1.8e5 | 24 |
| cal_pts | 32 | Calibration points. Number of measurements made in computing station calibration values (stn_cal, ul_stn_cal, and cal_std_dev). | Unsigned Integer –2 | N/A | 0 to 65,535 |  |
| ul_rng_phs | 34 | Measured range phase. Range phase. | IEEE Double | Range Units / 0.01 RU | 0.0 to 230 | 11,24 |
| state_seq1 | 42 | Sequence #1 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 7 | 19 |
| state_seq2 | 43 | Sequence #2 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 15 | 19 |
| state_seq3 | 44 | Sequence #3 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 15 | 19 |
| state_seq4 | 45 | Sequence #4 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 31 | 19 |
| state_seq5 | 46 | Sequence #5 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 31 | 19 |
| state_seq6 | 47 | Sequence #6 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 31 | 19 |
| pn_clk_phs | 48 | PN chip clock phase. Position in the chip at the time tag. | IEEE Double | Cycles / 1 (cycle | to | 19 |
| transmit_switch_stat | 56 | Transmitter switch status. 0 => antenna 1 => water load 2 => invalid/unknown | Unsigned Integer –1 | N/A | 0 to 2 |  |
| invert | 57 | Invert. Polarity of modulation signal. 0 => not inverted 1 => inverted | Unsigned Integer –1 | N/A | 0 or 1 | 52 |
| transmit_op_pwr | 58 | Transmitter output power. | IEEE Single | W / 0.1 W | 0.0 to 500,000.0 |  |
| template_id | 62 | Template ID. Value is the file name of the ranging parameter file. | ASCII –8 | N/A | ASCII string |  |
| clk_divider | 70 | Clock divider. Value that exciter ranging reference frequency is divided by to get PN chip rate. | Unsigned Integer –1 | N/A | 1 to 64 | 20 |
| len_seq1 | 71 | Sequence #1 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 8 | 21 |
| len_seq2 | 72 | Sequence #2 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 16 | 21 |
| len_seq3 | 73 | Sequence #3 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 16 | 21 |
| len_seq4 | 74 | Sequence #4 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 32 | 21 |
| len_seq5 | 75 | Sequence #5 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 32 | 21 |
| len_seq6 | 76 | Sequence #6 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 32 | 21 |
| def_seq1 | 77 | Sequence #1 component value. Definition of the sequence. | Unsigned Integer –1 | N/A | 0 to 28-1 | 21 |
| def_seq2 | 78 | Sequence #2 component value. Definition of the sequence. | Unsigned Integer –2 | N/A | 0 to 216-1 | 21 |
| def_seq3 | 80 | Sequence #3 component value. Definition of the sequence. | Unsigned Integer –2 | N/A | 0 to 216-1 | 21 |
| def_seq4 | 82 | Sequence #4 component value. Definition of the sequence. | Unsigned Integer –4 | N/A | 0 to 232-1 | 21 |
| def_seq5 | 86 | Sequence #5 component value. Definition of the sequence. | Unsigned Integer –4 | N/A | 0 to 232-1 | 21 |
| def_seq6 | 90 | Sequence #6 component value. Definition of the sequence. | Unsigned Integer –4 | N/A | 0 to 232-1 | 21 |
| pn_code_length | 94 | Code Length. | Unsigned Integer –4 | PN chips / 1 chip | 2 to 11000000 | 22 |
| transmit_inphs_time_year | 98 | Transmit In-phase time – year. Year of the time of zero phase on uplink range generation. | Unsigned Integer –2 | N/A | 1958 to 3000 | 75 |
| transmit_inphs_time_doy | 100 | Transmit In-phase time – day of year. Day of year of the time of zero phase on uplink range generation. | Unsigned Integer –2 | N/A | 1 to 366 | 75 |
| transmit_inphs_time_sec | 102 | Transmit In-phase time – seconds of day. Seconds of day of the time of zero phase on uplink range generation. | IEEE Double | Seconds / 1 (sec | 0.000000 to 86,400.999999 | 75 |
| carr_sup_rng_modul | 110 | Carrier Suppression by ranging modulation. Reduction in carrier power due to ranging modulation. | IEEE Single | dB / 0.1 dB | -15.0 to 0.0 |  |
| rng_modul_amp | 114 | Ranging modulation amplitude. Actual digital modulation amplitude used by the ranging hardware. | Unsigned Integer –2 | N/A | 0 to 212 |  |
| exc_scalar_num | 116 | Exciter Scalar Numerator. Numerator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| exc_scalar_den | 120 | Exciter Scalar Denominator. Denominator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| rng_cycle_time | 124 | Ranging cycle time. Time to complete one cycle of ranging code. | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.0e9 | 23,24 |
| time_tag_corr_flag | 132 | Time tag correction flag. Indicates results of validation of the block time tag. 0 => no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| type_time_corr_flag | 133 | Type of time tag correction flag. Indicates what type of time tag correction was made. 0 => no correction 1 => Year correction 2 => DOY correction 3 => Both Year and DOY correction | Unsigned Integer –1 | N/A | 0 to 3 |  |
| clock_waveform | 134 | Clock waveform type. 0 => squarewave 1 => sinewave | Unsigned Integer -1 | N/A | 0 or 1 |  |
| reserve1 | 135 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |

##### Ramp CHDO (Data Type 9)

The Ramp CHDO is generated only when ramp_type equals 0, 1, 4, or 5, and is defined in Table 3-12.

Table 3-12. Ramp CHDO (Data Type 9) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the ramp data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the ramp data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 38 |  |
| ul_hi_phs_cycles | 4 | High part uplink phase data whole cycles. Phase at time tag. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| ul_lo_phs_cycles | 8 | Low part uplink phase data whole cycles. Phase at time tag. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| ul_frac_phs_cycles | 12 | Fractional part uplink phase data cycles. Phase at time tag. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| ramp_freq | 16 | Ramp frequency. Precision varies with band (phase data gives higher precision). A value of 0.0 indicates an invalid or unknown value. S-band => 0.5 (Hz X-band => 1.6 (Hz Ka-band => 7.7 (Hz | IEEE Double | Sky level Hz, at least 7.7 (Hz precision (band dependent) | 0.0, 2.0e9 to 34.7e9 |  |
| ramp_rate | 24 | Ramp rate. | IEEE Double | Sky level Hz/sec, (Hz/sec precision | -3.2e5 to 3.2e5 |  |
| ramp_type | 32 | Ramp type. 0 => snap 1 => start of new ramp 4=> end of ramps 5 => ramping terminated by operator | Unsigned Integer –1 | N/A | 0 to 5 |  |
| reserve1 | 33 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| reserve8 | 34 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

#### Downlink Data CHDOs

There are three Downlink Data CHDOs: Downlink Carrier Phase (data type 1),  Downlink Sequential Ranging Phase (data type 3), and Downlink PN Ranging Phase (data type 5).  Their formats and contents are specified in sections 3.1.5.2.1 to 3.1.5.2.3.

##### Downlink Carrier Phase CHDO (Data Type 1)

The Downlink Carrier Phase CHDO is defined in Table 3-13.

Table 3-13. Downlink Carrier Phase CHDO (Data Type 1) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the downlink carrier phase data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the downlink carrier phase data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 228 |  |
| carr_loop_bw | 4 | Carrier tracking loop bandwidth. | IEEE Single | Hz / 1 mHz | 0.1 to 50.0 |  |
| pcn0 | 8 | Pc/N0. Carrier power to noise spectral density ratio. Has a value of –300.0 if no signal. | IEEE Single | dB-Hz / 0.1 dB-Hz | 0.0 to 90.0, -300.0 |  |
| pcn0_resid | 12 | Pc/N0 residual. Actual value minus predicted value. | IEEE Single | dB-Hz / 0.1 dB-Hz | -90.0 to 90.0 |  |
| pdn0 | 16 | Pd/N0. Data power to noise spectral density ratio. Has a value of –300.0 if no signal. | IEEE Single | dB-Hz / 0.1 dB-Hz | 0.0 to 90.0, -300.0 | 25 |
| pdn0_resid | 20 | Pd/N0 residual. Actual value minus predicted value. | IEEE Single | dB-Hz / 0.1 dB-Hz | -90.0 to 90.0 |  |
| system_noise_temp | 24 | System Noise Temperature. | IEEE Single | k (degrees kelvin) / 0.1 k | 0.1 to 2000.0 |  |
| phs_hi_0 | 28 | Raw phase sample 0 – High part phase data whole cycles. (time tag + 0.0 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_0 | 32 | Raw phase sample 0 – Low part phase data whole cycles. (time tag + 0.0 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_0 | 36 | Raw phase sample 0 – Fractional part phase data cycles. (time tag + 0.0 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_1 | 40 | Raw phase sample 1 – High part phase data whole cycles. (time tag + 0.1 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_1 | 44 | Raw phase sample 1 – Low part phase data whole cycles. (time tag + 0.1 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_1 | 48 | Raw phase sample 1 – Fractional part phase data cycles. (time tag + 0.1 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_2 | 52 | Raw phase sample 2 – High part phase data whole cycles. (time tag + 0.2 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_2 | 56 | Raw phase sample 2 – Low part phase data whole cycles. (time tag + 0.2 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_2 | 60 | Raw phase sample 2 – Fractional part phase data cycles. (time tag + 0.2 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_3 | 64 | Raw phase sample 3 – High part phase data whole cycles. (time tag + 0.3 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_3 | 68 | Raw phase sample 3 – Low part phase data whole cycles. (time tag + 0.3 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_3 | 72 | Raw phase sample 3 – Fractional part phase data cycles. (time tag + 0.3 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_4 | 76 | Raw phase sample 4 – High part phase data whole cycles. (time tag + 0.4 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_4 | 80 | Raw phase sample 4 – Low part phase data whole cycles. (time tag + 0.4 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_4 | 84 | Raw phase sample 4 – Fractional part phase data cycles. (time tag + 0.4 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_5 | 88 | Raw phase sample 5 – High part phase data whole cycles. (time tag + 0.5 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_5 | 92 | Raw phase sample 5 – Low part phase data whole cycles. (time tag + 0.5 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_5 | 96 | Raw phase sample 5 – Fractional part phase data cycles. (time tag + 0.5 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_6 | 100 | Raw phase sample 6 – High part phase data whole cycles. (time tag + 0.6 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_6 | 104 | Raw phase sample 6 – Low part phase data whole cycles. (time tag + 0.6 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_6 | 108 | Raw phase sample 6 – Fractional part phase data cycles. (time tag + 0.6 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_7 | 112 | Raw phase sample 7 – High part phase data whole cycles. (time tag + 0.7 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_7 | 116 | Raw phase sample 7 – Low part phase data whole cycles. (time tag + 0.7 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_7 | 120 | Raw phase sample 7 – Fractional part phase data cycles (time tag + 0.7 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_8 | 124 | Raw phase sample 8 – High part phase data whole cycles. (time tag + 0.8 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_8 | 128 | Raw phase sample 8 – Low part phase data whole cycles. (time tag + 0.8 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_8 | 132 | Raw phase sample 8 – Fractional part phase data cycles. (time tag + 0.8 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_9 | 136 | Raw phase sample 9 – High part phase data whole cycles. (time tag + 0.9 sec) | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_9 | 140 | Raw phase sample 9 – Low part phase data whole cycles. (time tag + 0.9 sec) | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_9 | 144 | Raw phase sample 9 – Fractional part phase data cycles. (time tag + 0.9 sec) | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| phs_hi_avg | 148 | Averaged phase sample – High part phase data whole cycles. One-second average, centered around time tag. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8 |
| phs_lo_avg | 152 | Averaged phase sample – Low part phase data whole cycles. One-second average, centered around time tag. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8 |
| phs_frac_avg | 156 | Averaged phase sample – Fractional part phase data cycles. One-second average, centered around time tag. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8 |
| dl_freq | 160 | Downlink frequency. Frequency at the time tag. | IEEE Double | Sky level Hz / 1 mHz | 2.2e9 to 32.3e9 |  |
| dop_resid | 168 | Doppler residual. Negative of frequency residual. | IEEE Single | Sky level Hz / 1 mHz | -1.0e6 to 1.0e6 |  |
| dop_noise | 172 | Doppler noise. Averaged over 10 points in record. | IEEE Single | Hz / 1 mHz | 0.0 to 1000.0 | 26 |
| slipped_cycles | 176 | Slipped cycles. | Integer –4 | N/A | -10 to 10 | 31 |
| carr_loop_type | 180 | Carrier loop type. | Unsigned Integer –1 | N/A | 1 to 3 | 53 |
| snt_flag | 181 | SNT measurement flag. 0 => SNT value is the predicted value 1 => SNT value is the measured value | Unsigned Integer –1 | N/A | 0 or 1 |  |
| carr_resid_wt | 182 | Carrier residual weight. (Weight value applied to residual phase error in carrier tracking; suppressed carrier weight is 1.0 minus this value.) | IEEE Single | N/A | 0.0 to 1.0 | 27 |
| sup_data_id | 186 | Support data ID. Name of the frequency predicts set used. | ASCII –8 | N/A | ASCII String |  |
| sup_data_rev | 194 | Support data revision. Revision of the frequency predicts set used. | ASCII –8 | N/A | ASCII String |  |
| prdx_time_offset | 202 | Predicts time offset. Seconds added to current time. | IEEE Double | Seconds / 1 msec | -8.64e4 to 8.64e4 | 54 |
| prdx_freq_offset | 210 | Predicts frequency offset. Hz added to predicted value. | IEEE Double | Hz / 1 mHz | -1.0e6 to 1.0e6 | 55 |
| carr_resid_tol_flag | 218 | Carrier residual tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer –1 | N/A | 0 or 1 | 62 |
| time_tag_corr_flag | 219 | Time tag correction flag. Indicates results of validation of the block time tag. 0 => no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| type_time_corr_flag | 220 | Type of time tag correction flag. Indicates what type of time tag correction was made. 0 => no correction 1 => Year correction 2 => DOY correction 3 => Both Year and DOY correction | Unsigned Integer –1 | N/A | 0 to 3 |  |
| dop_mode_corr_flag | 221 | Doppler mode correction flag. Indicates the results of the validation of the doppler mode. 0 => not applicable or no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| ul_stn_corr_flag | 222 | Uplink station correction flag. Indicates the results of the validation of the uplink station. 0 => not applicable or no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| reserve1 | 223 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| reserve8 | 224 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### Downlink Sequential Ranging Phase CHDO (Data Type 3)

The Downlink Sequential Ranging Phase CHDO is defined in Table 3-14.

Table 3-14. Downlink Sequential Ranging Phase CHDO (Data Type 3) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the downlink sequential ranging phase data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 (CHDO contains binary data) |  |
| chdo_length | 2 | Length attribute of the downlink sequential ranging phase data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 174 |  |
| stn_cal | 4 | Station calibration value. (Two-way). Value includes the equipment in the path, but not the Z-height correction. (0.0 if not measured.) | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.8e5 | 24 |
| dl_stn_cal | 12 | Downlink station calibration value. Value includes the downlink equipment in the path, but not the Z-height correction. (0.0 if not measured.) | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.8e5 | 10,24 |
| dl_cal_freq | 20 | Downlink calibration frequency. Frequency the calibration was done at. | IEEE Double | Sky level Hz / 1 mHz | 2.2e9 to 32.3e9 |  |
| cal_std_dev | 28 | Standard deviation of station calibration value. For stn_cal and dl_stn_cal. | IEEE Single | Range Units / 0.01 RU | 0.0 to 1.8e5 | 24 |
| cal_pts | 32 | Calibration points. Number of measurements made in computing station calibration values (stn_cal, dl_stn_cal, and cal_std_dev). | Unsigned Integer –2 | N/A | 0 to 65,535 |  |
| dl_rng_phs | 34 | Measured range phase. Range phase. | IEEE Double | Range Units / 0.01 RU | 0.0 to 230 | 11,24 |
| figure_merit | 42 | Figure of Merit. Rating of the measured range value. | IEEE Single | Percentage / 0.1 percent | 0.0 to 100.0 | 28 |
| rng_resid | 46 | Range residual. Measured range minus predicted range. | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 29 |
| drvid | 54 | DRVID. DRVID measured using phase data from carrier. | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 30, 81 |
| rtlt | 62 | Round trip light time. Predicted value. | IEEE Single | Seconds / 0.1 sec | 0.0 to 86,400.0 |  |
| pcn0 | 66 | Pc/N0. Carrier power to noise spectral density ratio. Has a value of –300.0 if no signal. | IEEE Single | dB-Hz / 0.1 dB-Hz | 0.0 to 90.0, -300.0 |  |
| pcn0_resid | 70 | Pc/N0 residual. Actual value minus predicted value. | IEEE Single | dB-Hz / 0.1 dB-Hz | -90.0 to 90.0 |  |
| pdn0 | 74 | Pd/N0. Data power to noise spectral density ratio. Has a value of –300.0 if no signal. | IEEE Single | dB-Hz / 0.1 dB-Hz | 0.0 to 90.0, -300.0 | 25 |
| pdn0_resid | 78 | Pd/N0 residual. Actual value minus predicted value. | IEEE Single | dB-Hz / 0.1 dB-Hz | -90.0 to 90.0 |  |
| prn0 | 82 | Pr/N0. Ranging power to noise spectral density ratio. Has a value of –300.0 if no signal. | IEEE Single | dB-Hz / 0.1 dB-Hz | -10.0 to 90.0, -300.0 |  |
| prn0_resid | 86 | Pr/N0 residual. Actual value minus predicted value. | IEEE Single | dB-Hz / 0.1 dB-Hz | -90.0 to 90.0 |  |
| system_noise_temp | 90 | System Noise Temperature. | IEEE Single | K (degrees Kelvin) / 0.1 K | 0.1 to 2000.0 |  |
| carr_loop_type | 94 | Carrier loop type. | Unsigned Integer –1 | N/A | 1 to 3 | 53 |
| snt_flag | 95 | SNT measurement flag. 0 => SNT value is the predicted value 1 => SNT value is the measured value | Unsigned Integer –1 | N/A | 0 or 1 |  |
| carr_resid_wt | 96 | Carrier residual weight. (Weight value applied to residual phase error in carrier tracking; suppressed carrier weight is 1.0 minus this value.) | IEEE Single | N/A | to 1.0 | 27 |
| template_id | 100 | Template ID. Value is the file name of the ranging parameter file. | ASCII –8 | N/A | ASCII string |  |
| invert | 108 | Invert. Inverted implies that the polarity of the correlation reference is the invert of what was transmitted. 0 => not inverted 1 => inverted | Unsigned Integer –1 | N/A | 0 or 1 | 52 |
| correl_type | 109 | Correlation type. 0 => squarewave 1 => sinewave | Unsigned Integer –1 | N/A | 0 or 1 |  |
| t1 | 110 | T1 setting. | Unsigned Integer –2 | Seconds / 1 sec | 1 to 3600 | 12 |
| t2 | 112 | T2 setting. | Unsigned Integer –2 | Seconds / 1 sec | 1 to 1800 | 13 |
| t3 | 114 | T3 setting. | Unsigned Integer –2 | Seconds / 1 sec | 0 to 1800 | 14 |
| first_comp_num | 116 | First component number. | Unsigned Integer –1 | N/A | 1 to 24 | 15 |
| last_comp_num | 117 | Last component number. | Unsigned Integer –1 | N/A | 1 to 24 | 15 |
| chop_comp_num | 118 | Chop component number. This is the component used to chop the other components. | Unsigned Integer –1 | N/A | 0 to 10 | 15, 16 |
| num_drvid | 119 | Number of DRVID measurements. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| rcv_inphs_time_year | 120 | Receive In-phase time – year. Year of the time of zero phase on downlink range signal correlation. | Unsigned Integer –2 | N/A | 1958 to 3000 | 75 |
| rcv_inphs_time_doy | 122 | Receive In-phase time – day of year. Day of year of the time of zero phase on downlink range signal correlation. | Unsigned Integer –2 | N/A | 1 to 366 | 75 |
| rcv_inphs_time_sec | 124 | Receive In-phase time – seconds of day. Seconds of day of the time of zero phase on downlink range signal correlation. | IEEE Double | Seconds / 1 (sec | 0.000000 to 86,400.999999 | 75 |
| exc_scalar_num | 132 | Exciter Scalar Numerator. Numerator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| exc_scalar_den | 136 | Exciter Scalar Denominator. Denominator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| rng_cycle_time | 140 | Ranging cycle time. Time to complete one cycle of the ranging code. | IEEE Double | Seconds / 0.1 sec | 4.0 to 504,536.0 | 18 |
| inphs_correl | 148 | In phase correlation value. The in phase value of the clock component correlation. | IEEE Single | N/A | -1.0 to 1.0 |  |
| quad_phs_correl | 152 | Quadrature phase correlation value. The quadrature phase value of the clock component correlation. | IEEE Single | N/A | -1.0 to 1.0 |  |
| metrics_vld_flag | 156 | Metrics validity flag. Validity of the Range Residual (rng_resid) and DRVID (drvid) measurements. 0 => Invalid (No uplink data available) 1 => Invalid (Other reasons) 2 => Valid | Unsigned Integer –1 | N/A | 0 to 2 | 70 |
| correl_vld_flag | 157 | Correlation validity flag. 0 => Invalid 1 => Valid | Unsigned Integer –1 | N/A | 0 or 1 | 56 |
| rng_resid_tol_flag | 158 | Range residual tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer –1 | N/A | 0 or 1 | 63 |
| drvid_tol_flag | 159 | DRVID tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer –1 | N/A | 0 or 1 | 64 |
| prn0_resid_tol_flag | 160 | Pr/N0 residual tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer –1 | N/A | 0 or 1 | 65 |
| rng_sigma_tol_flag | 161 | Range sigma tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer –1 | N/A | 0 or 1 | 66 |
| rng_vld_flag | 162 | Range validity flag. 0 => Invalid 1 => Valid | Unsigned Integer –1 | N/A | 0 or 1 | 67 |
| rng_config_flag | 163 | Range configuration change flag. 0 => Changed 1 => Unchanged | Unsigned Integer –1 | N/A | 0 or 1 | 68 |
| rng_hw_flag | 164 | Ranging hardware status flag. 0 => Bad 1 => Good | Unsigned Integer –1 | N/A | 0 or 1 |  |
| time_tag_corr_flag | 165 | Time tag correction flag. Indicates results of validation of the block time tag. 0 => no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| type_time_corr_flag | 166 | Type of time tag correction flag. Indicates what type of time tag correction was made. 0 => no correction 1 => Year correction 2 => DOY correction 3 => Both Year and DOY correction | Unsigned Integer –1 | N/A | 0 to 3 |  |
| dop_mode_corr_flag | 167 | Doppler mode correction flag. Indicates the results of the validation of the doppler mode. 0 => not applicable or no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| ul_stn_corr_flag | 168 | Uplink station correction flag. Indicates the results of the validation of the uplink station. 0 => not applicable or no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| chop_start_num | 169 | Chop Start. The first component chopped. | Unsigned Integer –1 | N/A | 0 to 25 | 16 |
| reserve8 | 170 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### Downlink PN Ranging Phase CHDO (Data Type 5)

The Downlink PN Ranging Phase CHDO is defined in Table 3-15.

Table 3-15. Downlink PN Ranging Phase CHDO (Data Type 5) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the downlink PN ranging phase data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the downlink PN ranging phase data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 202 |  |
| stn_cal | 4 | Station calibration value. (Two-way) Value includes the equipment in the path, but not the Z-height correction. (0.0 if not measured.) | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.8e5 | 24 |
| dl_stn_cal | 12 | Downlink station calibration value. Value includes the downlink equipment in the path, but not the Z-height correction. (0.0 if not measured.) | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.8e5 | 10, 24 |
| dl_cal_freq | 20 | Downlink calibration frequency. Frequency the calibration was done at. | IEEE Double | Sky level Hz / 1 mHz | 2.2e9 to 32.3e9 |  |
| cal_std_dev | 28 | Standard deviation of station calibration value. For stn_cal and dl_stn_cal. | IEEE Single | Range Units / 0.01 RU | 0.0 to 1.8e5 | 24 |
| cal_pts | 32 | Calibration points. Number of measurements made in computing station calibration values (stn_cal, dl_stn_cal, and cal_std_dev). | Unsigned Integer –2 | N/A | 0 to 65,535 |  |
| dl_rng_phs | 34 | Measured range phase. Range phase. | IEEE Double | Range Units / 0.01 RU | 0.0 to 230 | 11, 24 |
| figure_merit | 42 | Figure of Merit. Rating of the measured range value. | IEEE Single | Percentage / 0.1 percent | 0.0 to 100.0 | 28 |
| rng_resid | 46 | Range residual. Measured range minus predicted range. | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 29 |
| drvid | 54 | DRVID. DRVID measured using doppler data from carrier. | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 30 |
| rtlt | 62 | Round trip light time. Predicted value. | IEEE Single | Seconds / 0.1 sec | 0.0 to 86,400.0 |  |
| pcn0 | 66 | Pc/N0. Carrier power to noise spectral density ratio. Has a value of -300.0 if no signal. | IEEE Single | dB-Hz / 0.1 dB-Hz | 0.0 to 90.0, -300.0 |  |
| pcn0_resid | 70 | Pc/N0 residual. Actual value minus predicted value. | IEEE Single | dB-Hz / 0.1 dB-Hz | -90.0 to 90.0 |  |
| pdn0 | 74 | Pd/N0. Data power to noise spectral density ratio. Has a value of -300.0 if no signal. | IEEE Single | dB-Hz / 0.1 dB-Hz | 0.0 to 90.0, -300.0 | 25 |
| pdn0_resid | 78 | Pd/N0 residual. Actual value minus predicted value. | IEEE Single | dB-Hz / 0.1 dB-Hz | -90.0 to 90.0 |  |
| prn0 | 82 | Pr/N0. Ranging power to noise spectral density ratio. Has a value of –300.0 if no signal. | IEEE Single | dB-Hz / 0.1 dB-Hz | -10.0 to 90.0, -300.0 |  |
| prn0_resid | 86 | Pr/N0 residual. Actual value minus predicted value. | IEEE Single | dB-Hz / 0.1 dB-Hz | -90.0 to 90.0 |  |
| system_noise_temp | 90 | System Noise Temperature. | IEEE Single | K (degrees Kelvin) / 0.1 K | 0.1 to 2000.0 |  |
| state_seq1 | 94 | Sequence #1 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 7 | 19 |
| state_seq2 | 95 | Sequence #2 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 15 | 19 |
| state_seq3 | 96 | Sequence #3 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 15 | 19 |
| state_seq4 | 97 | Sequence #4 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 31 | 19 |
| state_seq5 | 98 | Sequence #5 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 31 | 19 |
| state_seq6 | 99 | Sequence #6 code state. Position in the sequence at the time tag. | Unsigned Integer –1 | N/A | 0 to 31 | 19 |
| pn_clk_phs | 100 | PN chip clock phase. Position in the chip at the time tag. | IEEE Double | Cycles / 1 (cycle | 0.0 to 1.0 | 19 |
| carr_loop_type | 108 | Carrier loop type. | Unsigned Integer –1 | N/A | 1 to 3 | 53 |
| snt_flag | 109 | SNT measurement flag. 0 => SNT value is the predicted value 1 => SNT value is the measured value | Unsigned Integer –1 | N/A | 0 or 1 |  |
| carr_resid_wt | 110 | Carrier residual weight. (Weight value applied to residual phase error in carrier tracking; suppressed carrier weight is 1.0 minus this value.) | IEEE Single | N/A | 0.0 to 1.0 | 27 |
| template_id | 114 | Template ID. Value is the file name of the ranging parameter file. | ASCII –8 | N/A | ASCII string |  |
| invert | 122 | Invert. Inverted implies that the polarity of the correlation reference is the invert of what was transmitted. 0 => not inverted 1 => inverted | Unsigned Integer –1 | N/A | 0 or 1 | 52 |
| correl_type | 123 | Correlation type. 0 => squarewave 1 => sinewave | Unsigned Integer –1 | N/A | 0 or 1 |  |
| int_time | 124 | Integration time. Time, in PN cycle periods, that the signal was integrated over. | Unsigned Integer –4 | Number of PN cycle periods / 1 period | 1 to 232 –1 |  |
| clk_divider | 128 | Clock divider. Value that ranging reference frequency is divided by to get chip rate. | Unsigned Integer –1 | N/A | 1 to 64 | 20 |
| len_seq1 | 129 | Sequence #1 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 8 | 21 |
| len_seq2 | 130 | Sequence #2 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 16 | 21 |
| len_seq3 | 131 | Sequence #3 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 16 | 21 |
| len_seq4 | 132 | Sequence #4 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 32 | 21 |
| len_seq5 | 133 | Sequence #5 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 32 | 21 |
| len_seq6 | 134 | Sequence #6 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 32 | 21 |
| def_seq1 | 135 | Sequence #1 component value. Definition of the sequence. | Unsigned Integer –1 | N/A | 0 to 28-1 | 21 |
| def_seq2 | 136 | Sequence #2 component value. Definition of the sequence. | Unsigned Integer –2 | N/A | 0 to 216-1 | 21 |
| def_seq3 | 138 | Sequence #3 component value. Definition of the sequence. | Unsigned Integer –2 | N/A | 0 to 216-1 | 21 |
| def_seq4 | 140 | Sequence #4 component value. Definition of the sequence. | Unsigned Integer –4 | N/A | 0 to 232-1 | 21 |
| def_seq5 | 144 | Sequence #5 component value. Definition of the sequence. | Unsigned Integer –4 | N/A | 0 to 232-1 | 21 |
| def_seq6 | 148 | Sequence #6 component value. Definition of the sequence. | Unsigned Integer –4 | N/A | 0 to 232-1 | 21 |
| pn_code_length | 152 | PN Code Length. | Unsigned Integer –4 | PN chips / 1 chip | 2 to 11,000,000 | 22 |
| rcv_inphs_time_year | 156 | Receive In-phase time – year. Year of the time of zero phase on downlink range signal correlation. | Unsigned Integer –2 | N/A | 1958 to 3000 | 75 |
| rcv_inphs_time_doy | 158 | Receive In-phase time – day of year. Day of year of the time of zero phase on downlink range signal correlation. | Unsigned Integer –2 | N/A | 1 to 366 | 75 |
| rcv_inphs_time_sec | 160 | Receive In-phase time – seconds of day. Seconds of day of the time of zero phase on downlink range generation. | IEEE Double | Seconds / 1 (sec | 0.000000 to 86,400.999999 | 75 |
| exc_scalar_num | 168 | Exciter Scalar Numerator. Numerator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| exc_scalar_den | 172 | Exciter Scalar Denominator. Denominator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| rng_cycle_time | 176 | Ranging cycle time. Time to complete one cycle of ranging code. | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.0e9 | 23, 24 |
| inphs_correl | 184 | In phase correlation value. The in phase value of the clock component correlation. | IEEE Single | N/A | -1.0 to 1.0 |  |
| quad_phs_correl | 188 | Quadrature phase correlation value. The quadrature phase value of the clock component correlation. | IEEE Single | N/A | -1.0 to 1.0 |  |
| metrics_vld_flag | 192 | Metrics validity flag. Validity of the Range Residual (rng_resid) and DRVID (drvid) measurements. 0 => Invalid (No uplink data available) 1 => Invalid (Other reasons) 2 => Valid | Unsigned Integer –1 | N/A | 0 to 2 | 70 |
| correl_vld_flag | 193 | Correlation validity flag. 0 => Invalid 1 => Valid | Unsigned Integer –1 | N/A | 0 or 1 | 56 |
| rng_resid_tol_flag | 194 | Range residual tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer –1 | N/A | 0 or 1 | 63 |
| drvid_tol_flag | 195 | DRVID tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer –1 | N/A | 0 or 1 | 64 |
| prn0_resid_tol_flag | 196 | Pr/N0 residual tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer –1 | N/A | 0 or 1 | 65 |
| rng_sigma_tol_flag | 197 | Range sigma tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer –1 | N/A | 0 or 1 | 66 |
| rng_vld_flag | 198 | Range validity flag. 0 => Invalid 1 => Valid | Unsigned Integer –1 | N/A | 0 or 1 | 67 |
| rng_config_flag | 199 | Range configuration change flag. 0 => Changed 1 => Unchanged | Unsigned Integer –1 | N/A | 0 or 1 | 68 |
| rng_hw_flag | 200 | Ranging hardware status flag. 0 => Bad 1 => Good | Unsigned Integer –1 | N/A | 0 or 1 |  |
| time_tag_corr_flag | 201 | Time tag correction flag. Indicates results of validation of the block time tag. 0 => no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| type_time_corr_flag | 202 | Type of time tag correction flag. Indicates what type of time tag correction was made. 0 => no correction 1 => Year correction 2 => DOY correction 3 => Both Year and DOY correction | Unsigned Integer –1 | N/A | 0 to 3 |  |
| dop_mode_corr_flag | 203 | Doppler mode correction flag. Indicates the results of the validation of the doppler mode. 0 => not applicable or no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| ul_stn_corr_flag | 204 | Uplink station correction flag. Indicates the results of the validation of the uplink station. 0 => not applicable or no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| reserve1a | 205 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |

#### Derived Data CHDOs

There are seven derived data CHDOs: Doppler Count (data type 6), Sequential Range (data type 7), Angle (data type 8), DRVID (data type 11), PN Range (data type 14), Tone Range (data type 15), Carrier Frequency Observable (data type 16), and Total Count Phase Observable (data type 17).  Their formats and contents are specified in sections 3.1.5.3.1 to 3.1.5.3.7.

##### Doppler Count CHDO (Data Type 6)

The Doppler Count CHDO is defined in Table 3-16.

Table 3-16. Doppler Count CHDO (Data Type 6) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the Doppler Count data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the Doppler Count data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 176 |  |
| ref_rcv_type | 4 | Reference receiver type. 0 => Unknown 1 => DTT 2 => MFR | Unsigned Integer –1 | N/A | 0 to 2 |  |
| sampl_interval | 5 | Sample interval. 1 => 0.1 second 2 => 1 second (non-UPL-DTT) 3 => 10 seconds (non-UPL-DTT) 4 => 60 seconds (non-UPL-DTT) | Unsigned Integer –1 | N/A | 1 to 4 | 84 |
| reserve1a | 6 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| carr_vld_flag | 7 | Received carrier validity indicator. 0 => Invalid Doppler 1 => Valid Doppler | Unsigned Integer-1 | N/A | 0 or 1 | 69 |
| dop_noise | 8 | Doppler noise. Invalid for non-DTT antennas; indicated by value of -1.0. | IEEE Single | Hz / 1 mHz | -1.0, 0.0 to 1000.0 | 26 |
| slipped_cycles_vld_flag | 12 | Slipped cycles validity flag. 0 => Invalid 1 => Valid | Unsigned Integer –1 | N/A | 0 or 1 |  |
| delta_ff_vld_flag | 13 | Delta-f/f validity flag. 0 => Invalid 1 => Valid | Unsigned Integer –1 | N/A | 0 or 1 |  |
| delta_ff | 14 | Delta-f/f. Valid only for UPL-DTT antennas. | IEEE Double | N/A | -1.0 to 1.0 | 32 |
| slipped_cycles | 22 | Slipped cycles. Number of detected slipped cycles at time tag. Valid only for UPL-DTT antennas. | Integer –4 | Number of cycles / 1 cycle | -10,000 to 10,000 | 31 |
| rcv_sig_lvl | 26 | Received signal level. Carrier power or data power (if suppressed carrier tracking). (-300.0 if not valid.) | IEEE Single | dBm / 0.1 dBm | -300.0, -190.0 to –45.0 | 58 |
| ul_freq | 30 | Uplink frequency. Uplink frequency value used in the Doppler computation at time tag. For UPL-DTT antennas, it is determined by the downlink frequency. Otherwise, depends on antenna configuration. | IEEE Double | Hz / 1 mHz | 2.0e9 to 34.7e9 | 34 |
| dop_cnt_bias _freq | 38 | Doppler count bias frequency. | IEEE Double | Hz / 1 mHz | -240.0e3 to 10.0e6 | 34 |
| dop_cnt_hi_0 | 46 | Doppler Count 0 – High part phase data whole cycles. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt_lo_0 | 50 | Doppler Count 0 – Low part phase data whole cycles. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt_frac_0 | 54 | Doppler Count 0 – Fractional part phase data cycles. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _hi_1 | 58 | Doppler Count 1 – High part phase data whole cycles. (time tag + 0.1 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _lo_1 | 62 | Doppler Count 1 – Low part phase data whole cycles. (time tag + 0.1 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _frac_1 | 66 | Doppler Count 1 – Fractional part phase data cycles. (time tag + 0.1 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _hi_2 | 70 | Doppler Count 2 – High part phase data whole cycles. (time tag + 0.2 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _lo_2 | 74 | Doppler Count 2 – Low part phase data whole cycles. (time tag + 0.2 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _frac_2 | 78 | Doppler Count 2 – Fractional part phase data cycles. (time tag + 0.2 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _hi_3 | 82 | Doppler Count 3 – High part phase data whole cycles. (time tag + 0.3 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _lo_3 | 86 | Doppler Count 3 – Low part phase data whole cycles. (time tag + 0.3 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _frac_3 | 90 | Doppler Count 3 – Fractional part phase data cycles. (time tag + 0.3 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _hi_4 | 94 | Doppler Count 4 – High part phase data whole cycles. (time tag + 0.4 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _lo_4 | 98 | Doppler Count 4 – Low part phase data whole cycles. (time tag + 0.4 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _frac_4 | 102 | Doppler Count 4 – Fractional part phase data cycles. (time tag + 0.4 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _hi_5 | 106 | Doppler Count 5 – High part phase data whole cycles. (time tag + 0.5 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _lo_5 | 110 | Doppler Count 5 – Low part phase data whole cycles. (time tag + 0.5 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _frac_5 | 114 | Doppler Count 5 – Fractional part phase data cycles. (time tag + 0.5 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _hi_6 | 118 | Doppler Count 6 – High part phase data whole cycles. (time tag + 0.6 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _lo_6 | 122 | Doppler Count 6 – Low part phase data whole cycles. (time tag + 0.6 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _frac_6 | 126 | Doppler Count 6 – Fractional part phase data cycles. (time tag + 0.6 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _hi_7 | 130 | Doppler Count 7 – High part phase data whole cycles. (time tag + 0.7 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _lo_7 | 134 | Doppler Count 7 – Low part phase data whole cycles. (time tag + 0.7 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _frac_7 | 138 | Doppler Count 7 – Fractional part phase data cycles (time tag + 0.7 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _hi_8 | 142 | Doppler Count 8 – High part phase data whole cycles. (time tag + 0.8 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _lo_8 | 146 | Doppler Count 8 – Low part phase data whole cycles. (time tag + 0.8 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _frac_8 | 150 | Doppler Count 8 – Fractional part phase data cycles. (time tag + 0.8 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _hi_9 | 154 | Doppler Count 9 – High part phase data whole cycles. (time tag + 0.9 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _lo_9 | 158 | Doppler Count 9 – Low part phase data whole cycles. (time tag + 0.9 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 34, 85 |
| dop_cnt _frac_9 | 162 | Doppler Count 9 – Fractional part phase data cycles. (time tag + 0.9 sec) Zero if non-UPL-DTT antenna. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 34, 85 |
| time_tag_corr_flag | 166 | Time tag correction flag. Indicates the results of validation of the block time tag. 0 => no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| type_time_corr_flag | 167 | Type of time tag correction flag. Indicates what type of time tag correction was made. 0 => no correction 1 => Year correction 2 => DOY correction 3 => Both Year and DOY correction | Unsigned Integer –1 | N/A | 0 to 3 |  |
| dop_mode_corr_flag | 168 | Doppler mode correction flag. Indicates the results of validation of the doppler mode. 0 => not applicable or no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| ul_stn_corr_flag | 169 | Uplink station correction flag. Indicates the results of validation of the uplink station. 0 => not applicable or no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| dl_band_corr_flag | 170 | Downlink frequency band correction flag. Indicates the results of validation of downlink band for the 26m stations only. 0 => not applicable or no validation attempted 1 => validated, no change 2 => validated, changed | Unsigned Integer –1 | N/A | 0 to 2 |  |
| reserve1 | 171 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| reserve8 | 172 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### Sequential Range CHDO (Data Type 7)

The Sequential Range CHDO is defined in Table 3-17.

Table 3-17. Sequential Range CHDO (Data Type 7) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the range data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the range data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 186 |  |
| ul_stn_cal | 4 | Uplink station calibration value. Invalid indicated by value of –1.0. | IEEE Double | Range Units / 0.01 RU | -1.0, 0.0 to 1.8e5 | 24, 40 |
| dl_stn_cal | 12 | Downlink station calibration value. Invalid indicated by value of –1.0. | IEEE Double | Range Units / 0.01 RU | -1.0, 0.0 to 1.8e5 | 24, 41 |
| meas_rng | 20 | Measured range value. Does not include compensation for station calibration and other adjustments. Invalid is indicated by value of -1.0. | IEEE Double | Range Units, modulo rng_modulo / 0.01 RU | -1.0, 0.0 to 230 | 24, 38 |
| rng_obs | 28 | Range observable. Includes all measurement adjustments (station calibration, spacecraft delay, and Z-height). Invalid is indicated by value of -1.0. | IEEE Double | Range Units, modulo rng_modulo / 0.01 RU | -1.0, 0.0 to 230 | 24, 39 |
| rng_obs_dl | 36 | Downlink range observable. Includes all measurement adjustments (station calibration, spacecraft delay, and Z-height). A value of -1.0 indicates invalid. | IEEE Double | Range Units, modulo rng_modulo / 0.01 RU | -1.0, 0.0 to 230 | 24, 76 |
| clock_waveform | 44 | Uplink clock waveform type. 0 => squarewave 1 => sinewave | Unsigned Integer -1 | N/A | 0 or 1 |  |
| chop_start_num | 45 | Chop Start. The first component chopped. | Unsigned Integer –1 | N/A | 0 to 25 | 16 |
| figure_merit | 46 | Figure of Merit. Rating of the measured range value. | IEEE Single | Percentage / 0.1 percent | 0.0 to 100.0 | 28 |
| drvid | 50 | DRVID. DRVID measured using phase data from carrier. | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 24, 30, 80 |
| rtlt | 58 | Round trip light time. Predicted value. | IEEE Single | Seconds / 0.1 sec | 0.0 to 86,400.0 |  |
| prn0 | 62 | Pr/N0. Ranging power to noise spectral density ratio. | IEEE Single | dB-Hz / 0.1 dB-Hz | -10.0 to 90.0 |  |
| transmit_pwr | 66 | Transmitter power. | IEEE Single | W / 0.1 W | 0.0 to 500,000.0 |  |
| invert | 70 | Invert. Inverted implies that the polarity of the correlation reference is the invert of what was transmitted. 0 => not inverted 1 => inverted | Unsigned Integer –1 | N/A | 0 or 1 |  |
| correl_type | 71 | Correlation type. 0 => squarewave 1 => sinewave | Unsigned Integer –1 | N/A | 0 or 1 |  |
| t1 | 72 | T1 setting. | Unsigned Integer –2 | Seconds / 1 sec | 1 to 3600 | 12 |
| t2 | 74 | T2 setting. | Unsigned Integer –2 | Seconds / 1 sec | 1 to 1800 | 13 |
| t3 | 76 | T3 setting. | Unsigned Integer –2 | Seconds / 1 sec | 0 to 1800 | 14 |
| first_comp_num | 78 | First component number. | Unsigned Integer –1 | N/A | 1 to 24 | 15 |
| last_comp_num | 79 | Last component number. | Unsigned Integer –1 | N/A | 1 to 24 | 15 |
| chop_comp_num | 80 | Chop component number. This is the component used to chop the other components. | Unsigned Integer –1 | N/A | 0 to 10 | 15, 16 |
| num_drvid | 81 | Number of DRVID measurements. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| transmit_inphs _time | 82 | Transmit In-phase time. Offset from time tag of time of zero phase on uplink range signal generation. | IEEE Single | Seconds / 1 (sec | -86,400.000000 to 86,400.000000 | 59 |
| rcv_inphs_time | 86 | Receive In-phase time. Offset from time tag of time of zero phase on downlink range signal correlation. | IEEE Single | Seconds / 1 (sec | -86,400.000000 to 86,400.000000 | 59 |
| carr_sup_rng _modul | 90 | Carrier suppression by ranging modulation. Amount carrier power is reduced by ranging modulation. | IEEE Single | dB / 0.1 dB | -15.0 to 0.0 |  |
| exc_scalar_num | 94 | Exciter Scalar Numerator. Numerator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| exc_scalar_den | 98 | Exciter Scalar Denominator. Denominator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| rng_cycle_time | 102 | Range cycle time. Time, in seconds, of one complete cycle of the ranging signal. | IEEE Double | Seconds / 0.1 sec | 4.0 to 504,536.0 | 18 |
| rng_modulo | 110 | Range modulo value. Range measurement modulo (ambiguity). | Unsigned Integer –4 | Range Units / 1 RU | 1 to 230 | 37 |
| inphs_correl | 114 | In phase correlation value. The in phase value of the clock component correlation. | IEEE Single | N/A | -1.0 to 1.0 |  |
| quad_phs_correl | 118 | Quadrature phase correlation value. The quadrature phase value of the clock component correlation. | IEEE Single | N/A | -1.0 to 1.0 |  |
| ul_freq | 122 | Uplink frequency. Uplink frequency at time tag.. Set to 0.0 if unavailable. | IEEE Double | Hz / 1 mHz | 0.0, 2.0e9 to 34.4e9 | 42 |
| rng_type | 130 | Range measurement type. Type of sequential measurement. 0 => Ranging measurement 1 => Calibration | Unsigned Integer –1 | N/A | 0 or 1 |  |
| reserve1a | 131 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| rng_noise | 132 | Range noise. Invalid indicated by value of -1.0. | IEEE Single | Range Units / 0.01 RU | -1.0, 0.0 to 230 | 43 |
| rng_prefit_resid | 136 | Range pre-fit residual. Observed range minus predicted range. | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 24, 29, 86 |
| rng_dl_prefit_resid | 144 | Downlink range pre-fit residual. Observed range minus predicted range. | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 24, 29, 86 |
| rng_prefit_resid_vld_flag | 152 | Range pre-fit residual validity indicator. 0 => Invalid pre-fit residual data 1 => Valid pre-fit residual data | Unsigned Integer-1 | N/A | 0 or 1 | 86 |
| rng_dl_prefit_resid_vld_flag | 153 | Downlink range pre-fit residual validity indicator. 0 => Invalid pre-fit residual data 1 => Valid pre-fit residual data | Unsigned Integer-1 | N/A | 0 or 1 | 86 |
| rng_resid_tol_value | 154 | Range residual tolerance value. Value used for setting Range residual tolerance flag. Provided by customer. Applies to both rng_prefit_resid and rng_dl_prefit_resid; not applicable if rng_prefit_resid_vld_flag and rng_dl_prefit_resid_vld_flag are 0. | IEEE Single | Range Units / 0.01 RU | -230 to 230 | 24, 63 |
| drvid_tol_value | 158 | DRVID tolerance value. Value used for setting DRVID tolerance flag. Provided by customer. | IEEE Single | Range Units / 0.01 RU | -230 to 230 | 24, 64 |
| prn0_resid_tol_value | 162 | Pr/N0 residual tolerance value. Value used for setting Pr/N0 residual tolerance flag. Provided by customer. | IEEE Single | dB-Hz / 0.1 dB-Hz | -10.0 to 90.0 | 65 |
| rng_sigma_tol_value | 166 | Range sigma tolerance value. Value used for setting Range sigma tolerance flag. Provided by customer. Not applicable if rng_noise is -1.0. | IEEE Single | Range Units / 0.01 RU | 0.0 to 230 | 43, 66 |
| fom_tol_value | 170 | Figure of Merit tolerance value. Value used in setting of Range Validity flag. Provided by customer. | IEEE Single | Percentage / 0.1 percent | 0.0 to 100.0 | 28 |
| rng_resid_tol_flag | 174 | Range residual tolerance flag. Not applicable if rng_prefit_resid_vld_flag and rng_dl_prefit_resid_vld_flag are 0. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 63 |
| drvid_tol_flag | 175 | DRVID tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 64 |
| prn0_resid_tol_flag | 176 | Pr/N0 residual tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 65 |
| rng_sigma_tol_flag | 177 | Range sigma tolerance flag. Not applicable if rng_noise is set to -1.0. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 66 |
| rng_vld_flag | 178 | Range validity flag. 0 => Invalid 1 => Valid | Unsigned Integer-1 | N/A | 0 or 1 | 67 |
| rng_config_flag | 179 | Range configuration change flag. 0 => Changed 1 => Unchanged | Unsigned Integer-1 | N/A | 0 or 1 | 68 |
| stn_cal_corr_flag | 180 | Station calibration correction flag. Indicates results of validation of the station calibration value. 0 => unable to correct 1 => validated, no change 2 => validated, changed uplink 3 => validated, changed downlink 4 => validated, changed both uplink and downlink | Unsigned Integer –1 | N/A | 0 to 4 |  |
| rng_chan_num | 181 | Ranging channel number. Only provided by 26m antennas. | Unsigned Integer –1 | N/A | 1 or 2 |  |
| reserve8 | 182 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### Angle CHDO (Data Type 8)

The Angle CHDO is defined in Table 3-18.  The Angle CHDO applies only to the 26m antennas.

Table 3-18. Angle CHDO (Data Type 8) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the angle data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the angle data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 34 |  |
| source_type | 4 | Source type. 0 => unknown 2 => MPA (26m), or MTA | Unsigned Integer –1 | N/A | 0 or 2 |  |
| ang_type | 5 | Angles Type. 0 => Unknown 1 => Azimuth / Elevation 2 => Hour angle / Declination 3 => X/Y (where +X is East) 4 => X/Y (where +X is South) | Unsigned Integer –1 | N/A | 0 to 4 |  |
| ang_vld_flag | 6 | Angles validity flag. 0 => Invalid 1 => Valid | Unsigned Integer –1 | N/A | 0 or 1 | 57 |
| ang_mode | 7 | Angle Mode. 0 => Auto Track 1 => Manual Aided 2 => Computer 3 => Sidereal 4 => Brake | Unsigned Integer –1 | N/A | 0 to 4 |  |
| conscan_mode | 8 | Conscan Mode. 0 => Conscan off 1 => Closed loop 2 => Open loop | Unsigned Integer –1 | N/A | 0 to 2 |  |
| reserve1 | 9 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| ang1 | 10 | Angle 1. Azimuth, hour angle, or X. | IEEE Single | Deg / 0.1 deg | -90.0 to 90.0 |  |
| ang2 | 14 | Angle 2. Elevation, declination, or Y. | IEEE Single | Deg / 0.1 deg | -90.0 to 90.0 |  |
| ang1_pseudo _resid | 18 | Angle 1 pseudo-residual. Actual minus predicted. | IEEE Single | Deg / 0.1 deg | -90.0 to 90.0 |  |
| ang2_pseudo _resid | 22 | Angle 2 pseudo-residual. Actual minus predicted. | IEEE Single | Deg / 0.1 deg | -90.0 to 90.0 |  |
| reserve4 | 26 | Reserved. Four bytes. | Unsigned Integer –4 | N/A | 0 |  |
| reserve8 | 30 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### DRVID CHDO (Data Type 11)

The DRVID CHDO is generated for sequential and PN ranging (not tone ranging) from UPL-DTT antennas and is defined in Table 3-19.

Table 3-19. DRVID CHDO (Data Type 11) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the DRVID data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the DRVID data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 38 |  |
| drvid_type | 4 | DRVID type. 0 => Unknown 1 => Sequential 2 => PN | Unsigned Integer –1 | N/A | 0 to 2 |  |
| drvid_pts | 5 | DRVID points. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| drvid | 6 | DRVID measurement. | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 24, 30, 79 |
| prn0 | 14 | Pr/N0. | IEEE Single | dB-Hz / 0.1 dB-Hz | -10.0 to 90.0 |  |
| drvid_noise | 18 | DRVID noise. Invalid indicated by value of -1.0. | IEEE Single | Range Units / 0.01 RU | -1.0, 0.0 to 230 | 24, 44 |
| drvid_tol_value | 22 | DRVID tolerance value. Value used for setting DRVID tolerance flag. Provided by customer. | IEEE Single | Range Units / 0.01 RU | -230 to 230 | 24, 64 |
| prn0_resid_tol_value | 26 | Pr/N0 residual tolerance value. Value used for setting Pr/N0 residual tolerance flag. Provided by customer. | IEEE Single | dB-Hz / 0.1 dB-Hz | -10.0 to 90.0 | 65 |
| reserve1 | 30 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| drvid_tol_flag | 31 | DRVID tolerance flag. 0 => Out of Tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 64 |
| prn0_resid_tol_flag | 32 | Pr/N0 residual tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 65 |
| drvid_noise_pts | 33 | DRVID noise points. Number of points used in DRVID noise computation. | Unsigned Integer –1 | N/A | 0 to 200 |  |
| reserve8 | 34 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### PN Range CHDO (Data Type 14)

The PN Range CHDO is defined in Table 3-20.

Table 3-20. PN Range CHDO (Data Type 14) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the PN range data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the PN range data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 160 |  |
| ul_stn_cal | 4 | Uplink station calibration value. Invalid indicated by value of –1.0. | IEEE Double | Range Units / 0.01 RU | -1.0, 0.0 to 1.8e5 | 24, 40 |
| dl_stn_cal | 12 | Downlink station calibration value. Invalid indicated by value of –1.0. | IEEE Double | Range Units / 0.01 RU | -1.0, 0.0 to 1.8e5 | 24, 41 |
| meas_rng | 20 | Measured range value. Does not include compensation for station calibration and other adjustments. Invalid is indicated by value of -1.0. | IEEE Double | Range Units, modulo rng_modulo / 0.01 RU | -1.0, 0.0 to 230 | 24, 45, 46 |
| rng_obs_dl | 28 | Downlink range observable. Includes measurement adjustments (station calibration, spacecraft delay, and Z-height). Invalid is indicated by value of -1.0. | IEEE Double | Range Units, modulo rng_modulo / 0.01 RU | -1.0, 0.0 to 230 | 24, 76 |
| figure_merit | 36 | Figure of Merit. Rating of the measured range value. | IEEE Single | Percentage / 0.1 percent | 0.0 to 100.0 | 28 |
| drvid | 40 | DRVID. DRVID measured using doppler data from carrier | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 30, 24, 79 |
| rtlt | 48 | Round trip light time. Predicted value. | IEEE Single | Seconds / 0.1 sec | 0.0 to 86,400.0 |  |
| prn0 | 52 | Pr/N0. Ranging power to noise spectral density ratio. | IEEE Single | dB-Hz / 0.1 dB-Hz | -10.0 to 90.0 |  |
| transmit_pwr | 56 | Transmitter power. | IEEE Single | W / 0.1 W | 0.0 to 500,000.0 |  |
| invert | 60 | Invert. Inverted implies that the polarity of the correlation reference is the invert of what was transmitted. 0 => not inverted 1 => inverted | Unsigned Integer –1 | N/A | 0 or 1 | 52 |
| correl_type | 61 | Correlation type. 0 => squarewave 1 => sinewave | Unsigned Integer –1 | N/A | 0 or 1 |  |
| clk_divider | 62 | Clock divider. Value that ranging reference frequency is divided by to get chip rate. | Unsigned Integer –1 | N/A | 1 to 64 | 20 |
| len_seq1 | 63 | Sequence #1 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 8 | 21 |
| len_seq2 | 64 | Sequence #2 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 16 | 21 |
| len_seq3 | 65 | Sequence #3 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 16 | 21 |
| len_seq4 | 66 | Sequence #4 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 32 | 21 |
| len_seq5 | 67 | Sequence #5 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 32 | 21 |
| len_seq6 | 68 | Sequence #6 length. A value of 0 implies no sequence. | Unsigned Integer –1 | Chips / 1 chip | 0 to 32 | 21 |
| def_seq1 | 69 | Sequence #1 component value. Definition of the sequence. | Unsigned Integer –1 | N/A | 0 to 28-1 | 21 |
| def_seq2 | 70 | Sequence #2 component value. Definition of the sequence. | Unsigned Integer –2 | N/A | 0 to 216-1 | 21 |
| def_seq3 | 72 | Sequence #3 component value. Definition of the sequence. | Unsigned Integer –2 | N/A | 0 to 216-1 | 21 |
| def_seq4 | 74 | Sequence #4 component value. Definition of the sequence. | Unsigned Integer –4 | N/A | 0 to 232-1 | 21 |
| def_seq5 | 78 | Sequence #5 component value. Definition of the sequence. | Unsigned Integer –4 | N/A | 0 to 232-1 | 21 |
| def_seq6 | 82 | Sequence #6 component value. Definition of the sequence. | Unsigned Integer –4 | N/A | 0 to 232-1 | 21 |
| pn_code_length | 86 | PN Code Length. | Unsigned Integer –4 | PN chips | 2 to 11,000,000 | 22 |
| transmit_inphs_time | 90 | Transmit In-phase time. Offset from time tag of time of zero phase on uplink range signal generation. | IEEE Single | Seconds / 1 (sec | -86,400.000000 to 86,400.000000 | 59 |
| rcv_inphs_time | 94 | Receive In-phase time. Offset from time tag of time of zero phase on downlink range signal correlation. | IEEE Single | Seconds / 1 (sec | -86,400.000000 to 86,400.000000 | 59 |
| carr_sup_rng _modul | 98 | Carrier suppression by ranging modulation. Reduction in carrier power due to ranging modulation. | IEEE Single | dB / 0.1 dB | -15.0 to 0.0 |  |
| exc_scalar_num | 102 | Exciter Scalar Numerator. Numerator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| exc_scalar_den | 106 | Exciter Scalar Denominator. Denominator of multiplier that is used to generate ranging reference signal from uplink sky frequency. | Unsigned Integer –4 | N/A | 1 to 232-1 | 17 |
| rng_cycle_time | 110 | Range cycle time. Time, in Range Units, of one complete cycle of the ranging signal. | IEEE Double | Range Units / 0.01 RU | 0.0 to 1.0e9 | 23, 24 |
| rng_modulo | 118 | Range modulo value. Range measurement modulo (ambiguity). | Unsigned Integer –4 | Range Units / 1 RU | 0 to 230 | 45 |
| rng_noise | 122 | Range noise. Invalid indicated by value of -1.0. | IEEE Single | Range Units / 0.01 RU | -1.0, 0.0 to 230 | 43 |
| rng_dl_prefit_resid | 126 | Downlink range pre-fit residual. Observed range minus predicted range. | IEEE Double | Range Units / 0.01 RU | -230 to 230 | 24, 29, 86 |
| rng_dl_prefit_resid_vld_flag | 134 | Downlink range pre-fit residual validity indicator. 0 => Invalid pre-fit residual data 1 => Valid pre-fit residual data | Unsigned Integer-1 | N/A | 0 or 1 | 86 |
| clock_waveform | 135 | Uplink clock waveform type. 0 => squarewave 1 => sinewave | Unsigned Integer -1 | N/A | 0 or 1 |  |
| rng_resid_tol_value | 136 | Range residual tolerance value. Value used for setting Range residual tolerance flag. Provided by customer. Applies to rng_dl_prefit_resid; not applicable if rng_dl_prefit_resid_vld_flag is 0. | IEEE Single | Range Units / 0.01 RU | -230 to 230 | 24, 63 |
| drvid_tol_value | 140 | DRVID tolerance value. Value used for setting DRVID tolerance flag. Provided by customer. | IEEE Single | Range Units / 0.01 RU | -230 to 230 | 24, 64 |
| prn0_resid_tol_value | 144 | Pr/N0 residual tolerance value. Value used for setting Pr/N0 residual tolerance flag. Provided by customer. | IEEE Single | dB-Hz / 0.1 dB-Hz | -10.0 to 90.0 | 65 |
| rng_sigma_tol_value | 148 | Range sigma tolerance value. Value used for setting Range sigma tolerance flag. Provided by customer. Not applicable if rng_noise is set to -1.0. | IEEE Single | Range Units / 0.01 RU | 0.0 to 230 | 43, 66 |
| fom_tol_value | 152 | Figure of Merit tolerance value. Value used in setting of Range Validity flag. Provided by customer. | IEEE Single | Percentage / 0.1 percent | 0.0 to 100.0 | 28 |
| rng_resid_tol_flag | 156 | Range residual tolerance flag. Not applicable if rng_dl_prefit_resid_vld_flag is 0. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 63 |
| drvid_tol_flag | 157 | DRVID tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 64 |
| prn0_resid_tol_flag | 158 | Pr/N0 residual tolerance flag. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 65 |
| rng_sigma_tol_flag | 159 | Range sigma tolerance flag. Not applicable if rng_noise is set to -1.0. 0 => Out of tolerance 1 => In tolerance | Unsigned Integer-1 | N/A | 0 or 1 | 66 |
| rng_vld_flag | 160 | Range validity flag. 0 => Invalid 1 => Valid | Unsigned Integer-1 | N/A | 0 or 1 | 67 |
| rng_config_flag | 161 | Range configuration change flag. 0 => Changed 1 => Unchanged | Unsigned Integer-1 | N/A | 0 or 1 | 68 |
| stn_cal_corr_flag | 162 | Station calibration correction flag. Indicates results of validation of the station calibration value. 0 => unable to correct 1 => validated, no change 2 => validated, changed uplink 3 => validated, changed downlink 4 => validated, changed both uplink and downlink | Unsigned Integer –1 | N/A | 0 to 4 |  |
| reserve1b | 163 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |

##### Tone Range CHDO (Data Type 15)

The Tone Range CHDO is defined in Table 3-21.  The Tone Range CHDO applies only to the non-UPL-DTT antennas.

Table 3-21. Tone Range CHDO (Data Type 15) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the tone range data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the tone range data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 50 |  |
| source_type | 4 | Source type. 0 => Unknown 2 => MPA (26m), MTA | Unsigned Integer –1 | N/A | 0 or 2 |  |
| mjr_tone_freq | 5 | Major tone frequency. 0 => Not used 1 => 20 kHz 2 => 100 kHz 3 => 500 kHz | Unsigned Integer –1 | N/A | 0 to 3 |  |
| mnr_tone_freq | 6 | Minor tone frequency. 0 => not used 1 => 10 Hz | Unsigned Integer –1 | N/A | 0 or 1 |  |
| reserve1 | 7 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| meas_rng | 8 | Measured range value. Range as reported by the station; includes corrections for Z-height and station calibration | IEEE Double | nsec, modulo 232 / 0.1 nsec | 0 to 232 - 1 | 72 |
| rng_obs | 16 | Range observable. Includes measurement adjustments (station calibration, spacecraft delay, and Z-height). | IEEE Double | nsec, modulo 232 / 0.1 nsec | 0 to 232 - 1 | 72 |
| stn_cal | 24 | Station calibration. Not currently reported by station; value set to 0.0. | IEEE Double | nsec / 0.1 nsec | 0.0 to 1.8e5 | 72 |
| carr_pwr | 32 | Carrier power. | IEEE Single | dBm / 0.1 dBm | -185.0 to –85.0 |  |
| rng_prefit _resid | 36 | Tone Range pre-fit residual. Observed range minus predicted range. | IEEE Double | nsec / 0.1 nsec | -227 to 227 | 86 |
| rng_prefit_resid_vld_flag | 44 | Tone range pre-fit residual validity indicator. 0 => Invalid pre-fit residual data 1 => Valid pre-fit residual data | Unsigned Integer-1 | N/A | 0 or 1 | 86 |
| reserve1a | 45 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| reserve8 | 46 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### Carrier Frequency Observable CHDO (Data Type 16)

The Carrier Frequency Observable CHDO is defined in Table 3-22.

Table 3-22. Carrier Frequency Observables CHDO (Data Type 16) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the Carrier Frequency Observables data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the Carrier Frequency Observables data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | Bytes | 38 + 18 * num_obs |  |
| ref_rcv_type | 4 | Reference receiver type. 0 => Unknown 1 => DTT 2 => MFR | Unsigned Integer –1 | N/A | 0 to 2 |  |
| reserve1 | 5 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| carr_prefit_resid_tol_value | 6 | Received carrier pre-fit residual tolerance value. Value used for setting received carrier pre-fit residual tolerance flag. Provided by customer. | IEEE Single | Hz / 1 mHz | -1.0e6 to 1.0e6 | 62 |
| reserve2 | 10 | Reserved. Two bytes. | Unsigned Integer –2 | N/A | 0 |  |
| dop_noise | 12 | Doppler noise. Invalid indicated by value of -1.0. | IEEE Single | Hz / 1 mHz | -1.0, 0.0 to 1000.0 | 26 |
| delta_ff | 16 | Delta-f/f. | IEEE Double | N/A | -1.0 to 1.0 | 32 |
| rcv_sig_lvl | 24 | Received signal level. Carrier power or data power (if suppressed carrier tracking). (-300.0 if not valid.) | IEEE Single | dBm / 0.1 dBm | -300.0, -190.0 to –45.0 | 58 |
| num_obs | 28 | Number of Observable measurements. | Unsigned Integer –2 | N/A | 1 to 100 | 33 |
| obs_cnt_time | 30 | Observable count time. Integration time of the observables. | IEEE single | seconds / 0.1 sec | 0.1 to 3600.0 | 33 |
| rcv_carr_obs | 34, 52, …, 34 + 18 * (num_obs – 1) | Received Carrier observable. This measurement is part of a set of measurements that are repeated num_obs times. | IEEE Double | Sky level Hz / 1 mHz | -32.3e9 to -2.0e9 | 35 |
| carr_prefit_resid | 42, 60, …, 42 + 18 * (num_obs – 1) | Received carrier pre-fit residual. Observed minus predicted. | IEEE Single | Hz / 1 mHz | -1.0e6 to 1.0e6 | 86 |
| carr_prefit_resid_vld_flag | 46, 64, …, 46 + 18 * (num_obs – 1) | Received carrier pre-fit residual validity indicator. 0 => Invalid pre-fit residual data 1 => Valid pre-fit residual data | Unsigned Integer –1 | N/A | 0 or 1 | 86 |
| carr_prefit_resid_tol_flag | 47, 65, …, 47 + 18 * (num_obs – 1) | Received carrier pre-fit residual tolerance flag. 0 => Out of tolerance 1 => In tolerance 2 => Not applicable | Unsigned Integer –1 | N/A | 0 to 2 | 62, 86 |
| reserve4 | 48, 66, …, 48 + 18 * (num_obs – 1) | Reserved. Four bytes. | Unsigned Integer –4 | N/A | 0 |  |
| reserve8 | 34 + 18 * num_obs | Reserved. Eight bytes. | Unsigned Integer -8 | N/A | 0 |  |

##### Total Count Phase Observable CHDO (Data Type 17)

The Total Count Phase Observable CHDO is defined in Table 3-23.

Table 3-23. Total Count Phase Observable CHDO (Data Type 17) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the Total Count Phase Observables data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the Total Count Phase Observables data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 50 + 22 * num_obs |  |
| ref_rcv_type | 4 | Reference receiver type. 0 => Unknown 1 => DTT 2 => MFR | Unsigned Integer –1 | N/A | 0 to 2 |  |
| reserve1 | 5 | Reserved. One byte. | Unsigned Integer –1 | N/A | 0 |  |
| total_cnt_phs_prefit_resid_tol_value | 6 | Total Count Phase pre-fit residual tolerance value. Value used for setting total count phase pre-fit residual tolerance flag. Provided by customer. | IEEE Single | Hz / 1 mHz | -1.0e6 to 1.0e6 | 62 |
| reserve2 | 10 | Reserved. Two bytes. | Unsigned Integer –2 | N/A | 0 |  |
| dop_noise | 12 | Doppler noise. Invalid indicated by value of -1.0. | IEEE Single | Hz / 1 mHz | -1.0, 0.0 to 1000.0 | 26 |
| delta_ff | 16 | Delta-f/f. | IEEE Double | N/A | -1.0 to 1.0 | 32 |
| rcv_sig_lvl | 24 | Received signal level. Carrier power or data power (if suppressed carrier tracking). (-300.0 if not valid.) | IEEE Single | dBm / 0.1 dBm | -300.0, -190.0 to –45.0 | 58 |
| num_obs | 28 | Number of Observable measurements. | Unsigned Integer –2 | N/A | 1 to 100 | 33 |
| obs_cnt_time | 30 | Observable count time. Integration time of the observables. | IEEE Single | seconds / 0.1 sec | 0.1 to 3600.0 | 33 |
| total_cnt_phs_st_year | 34 | Total Count Phase observable start time year. | Unsigned Integer –2 | N/A | 1900 to 3000 | 36 |
| total_cnt_phs_st_doy | 36 | Total Count Phase observable start time day of year. | Unsigned Integer –2 | N/A | 1 to 366 | 36 |
| total_cnt_phs_st_sec | 38 | Total Count Phase observable start time seconds. | IEEE Double | Seconds / 0.01 sec | 0.00 to 86,400.99 | 1, 36 |
| total_cnt_phs _obs_hi | 46, 68, …, 46 + 22 * (num_obs – 1) | Negative of Total Count Phase observable - High part phase data whole cycles. This measurement is part of a set of measurements that are repeated num_obs times. | Unsigned Integer –4 | Total integer phase cycles divided by 232 | 0 to 232-1 | 8, 36 |
| total_cnt_phs _obs_lo | 50, 72, …, 50 + 22 * (num_obs – 1) | Negative of Total Count Phase observable - Low part phase data whole cycles. This measurement is part of a set of measurements that are repeated num_obs times. | Unsigned Integer –4 | Total integer phase cycles modulo 232 | 0 to 232-1 | 8, 36 |
| total_cnt_phs _obs_frac | 54, 76, …, 54 + 22 * (num_obs – 1) | Negative of Total Count Phase observable – Fractional part phase data cycles. This measurement is part of a set of measurements that are repeated num_obs times. | Unsigned Integer –4 | Fractional phase cycles multiplied by 232 | 0 to 232-1 | 8, 36 |
| total_cnt_phs_prefit_resid | 58, 80, …, 58 + 22 * (num_obs – 1) | Total Count Phase pre-fit residual. Observed minus predicted. | IEEE Single | Hz / 1 mHz | -1.0e6 to 1.0e6 | 86 |
| total_cnt_phs_prefit_resid_vld_flag | 62, 84, …, 62 + 22 * (num_obs – 1) | Total Count Phase pre-fit residual validity indicator. 0 => Invalid pre-fit residual data 1 => Valid pre-fit residual data | Unsigned Integer –1 | N/A | 0 or 1 | 86 |
| total_cnt_phs_prefit_resid_tol_flag | 63, 85, …, 63 + 22 * (num_obs – 1) | Total Count Phase pre-fit residual tolerance flag. 0 => Out of tolerance 1 => In tolerance 2 => Not applicable | Unsigned Integer –1 | N/A | 0 to 2 | 62, 86 |
| reserve4 | 64, 86, …, 64 + 22 * (num_obs – 1) | Reserved. Four bytes. | Unsigned Integer –4 | N/A | 0 |  |
| reserve8 | 46 + 22 * num_obs | Reserved. Eight bytes. | Unsigned Integer -8 | N/A | 0 |  |

#### Interferometric Data CHDOs

There is one interferometric data CHDO: VLBI (data type 10).  Its format and contents are specified in section 3.1.5.4.1.

##### VLBI CHDO (Data Type 10)

The VLBI CHDO is defined in Table 3-24.

Table 3-24. VLBI CHDO (Data Type 10) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the VLBI data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the VLBI data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 96 |  |
| clk_off_epoch _year | 4 | Clock offset epoch year. | Unsigned Integer –2 | Years | 1958 to 3000 | 78 |
| clk_off_epoch _doy | 6 | Clock offset epoch DOY. | Unsigned Integer –2 | Days | 1 to 366 | 78 |
| clk_off_epoch_sec | 8 | Clock offset epoch seconds. | IEEE Double | seconds / 0.1 msec | 0.0000 to 86,400.9999 | 1, 78 |
| clk_off_1 | 16 | Clock offset at first receiving antenna for scan. (UTC-station time) | Signed Integer –4 | nsec / 1 nsec | -231 to 231 - 1 |  |
| clk_off_2 | 20 | Clock offset at second receiving antenna for scan. (UTC-station time) | Signed Integer –4 | nsec / 1 nsec | -231 to 231 - 1 |  |
| phs_cal_flag | 24 | Phase calibration flag. 0 => unknown 1 => no calibration 2 => default calibration 3 => quasar calibration only 4 => spacecraft calibration only 5 => spacecraft and quasar calibration | Unsigned Integer –1 | N/A | 0 to 5 |  |
| chan_sampl_flag | 25 | Channel sampling flag. 1 => multiplexed 2 => dual-frequency combined 3 => 4 parallel channels | Unsigned Integer –1 | N/A | 1 to 3 |  |
| quasar_id | 26 | Quasar ID. Name of quasar used. | ASCII –12 | N/A | ASCII string |  |
| quasar_id_num | 38 | Quasar ID numeric. Number assigned to the quasar used. | Unsigned Integer –2 | N/A | 0 to 1024 |  |
| data_qual_flag | 40 | Data quality flag. 0 => good 1 => poor | Unsigned Integer –1 | N/A | 0 or 1 |  |
| chan_num | 41 | Channel number. Valid only if rec_type is 71 or 72. | Unsigned Integer –1 | N/A | 0 to 255 |  |
| mode_id | 42 | Mode identifier. Valid only if rec_type is 73; equals 0 otherwise. 0 => one-way 1 => two-way | Unsigned Integer –1 | N/A | 0 or 1 |  |
| modulo_flag | 43 | Modulo flag. Valid only if rec_type is 73 or 74. 0 => modded 1 => unmodded | Unsigned Integer –1 | N/A | 0 or 1 |  |
| ref_freq | 44 | Reference frequency. | IEEE Double | Hz / 1 mHz | 2.0e9 to 34.7e9 |  |
| modulus | 52 | Modulus. Valid only if rec_type is 73 or 74. | IEEE Double | nsec / 0.1 nsec | 0.0 to 100,000.0 |  |
| cnt_time_nar _band_phs | 60 | Count time for narrow-band phase mode observable. | IEEE Single | Seconds / 1 sec | 1 to 100,000 |  |
| nar_band_phs | 64 | Narrow-band phase mode observable. | IEEE Double | Cycles / 1 mcycle | -4.0e12 to 4.0e12 |  |
| cnt_time_nar _band_dop | 72 | Count time for narrow-band Doppler mode observable. | IEEE Single | Seconds / 1 sec | 1 to 100,000 |  |
| nar_band_dop | 76 | Narrow-band Doppler mode observable. | IEEE Double | Hz / 1 mHz | -1.0e6 to 1.0e6 |  |
| wide_band_obs | 84 | Wide-band observable. | IEEE Double | nsec / 0.1 nsec | -4.0e12 to 4.0e12 |  |
| reserve8 | 92 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

#### Filtered Data CHDOs

There are two filtered data CHDOs: Smoothed Noise (data type 12) and Allan Deviation (data type 13).  Their formats and contents are specified in sections 3.1.5.5.1 to 3.1.5.5.2.

##### Smoothed Noise CHDO (Data Type 12)

The Smoothed Noise CHDO is generated for UPL-DTT antennas only and is defined in Table 3-25.  Not generated if predicted frequencies are not available.

Table 3-25. Smoothed Noise CHDO (Data Type 12) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the smoothed noise data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the smoothed noise data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 46 |  |
| 01sec_sm_noise | 4 | 0.1-second smoothed noise measurement. | IEEE Single | Hz / 0.1 Hz | 0.0 to 1000.0 | 47 |
| 1sec_sm_noise | 8 | 1-second smoothed noise measurement. | IEEE Single | Hz / 0.1 Hz | 0.0 to 1000.0 | 47 |
| 10sec_sm_noise | 12 | 10-second smoothed noise measurement. | IEEE Single | Hz / 0.1 Hz | 0.0 to 1000.0 | 47 |
| 100sec_sm_noise | 16 | 100-second smoothed noise measurement. | IEEE Single | Hz / 0.1 Hz | 0.0 to 1000.0 | 47 |
| 200sec_sm_noise | 20 | 200-second smoothed noise measurement. | IEEE Single | Hz / 0.1 Hz | 0.0 to 1000.0 | 47 |
| 600sec_sm_noise | 24 | 600-second smoothed noise measurement. | IEEE Single | Hz / 0.1 Hz | 0.0 to 1000.0 | 47 |
| int_time | 28 | Integration time. Total integration time of measurements. | Unsigned Integer –4 | Seconds / 1 sec | 1 to 10,800 |  |
| percent_data_used | 32 | Percent of data used. | IEEE Single | Percentage / 0.1 percent | 0.0 to 100.0 | 50 |
| new_01sec | 36 | 0.1-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 48 |
| new_1sec | 37 | 1-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 48 |
| new_10sec | 38 | 10-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 48 |
| new_100sec | 39 | 100-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 48 |
| new_200sec | 40 | 200-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 48 |
| new_600sec | 41 | 600-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 48 |
| reserve8 | 42 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

##### Allan Deviation CHDO (Data Type 13)

The Allan Deviation CHDO is generated for UPL-DTT antennas only and is defined in Table 3-26.  Not generated if predicted frequencies are not available.

Table 3-26. Allan Deviation CHDO (Data Type 13) Definitions

| Identifier | Byte Offset | Item Name and Description | Format | Units/ Precision | Range | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| chdo_type | 0 | Type attribute of the Allan Deviation data CHDO. CHDO contains binary data. | Unsigned Integer –2 | N/A | 10 |  |
| chdo_length | 2 | Length attribute of the Allan Deviation data CHDO value field. Number of bytes after this item. | Unsigned Integer –2 | bytes | 42 |  |
| 01sec_allan_dev | 4 | 0.1-second Allan Deviation measurement. | IEEE Single | Unitless | 0.0 to 1.0 | 49 |
| 1sec_allan_dev | 8 | 1-second Allan Deviation measurement. | IEEE Single | Unitless | 0.0 to 1.0 | 49 |
| 10sec_allan_dev | 12 | 10-second Allan Deviation measurement. | IEEE Single | Unitless | 0.0 to 1.0 | 49 |
| 100sec_allan_dev | 16 | 100-second Allan Deviation measurement. | IEEE Single | Unitless | 0.0 to 1.0 | 49 |
| 1000sec_allan _dev | 20 | 1000-second Allan Deviation measurement. | IEEE Single | Unitless | 0.0 to 1.0 | 49 |
| int_time | 24 | Integration time. | Unsigned Integer –4 | Seconds / 1 sec | 1 to 106 |  |
| percent_data_used | 28 | Percent of data used. | IEEE Single | Percentage / 0.1 percent | 0.0 to 100.0 | 50 |
| rpt_cause | 32 | Cause of report generation. 0 => 1000 second report 1 => Doppler mode change 2 => Idle mode | Unsigned Integer –1 | N/A | 0 to 2 |  |
| new_01sec | 33 | 0.1-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 51 |
| new_1sec | 34 | 1-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 51 |
| new_10sec | 35 | 10-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 51 |
| new_100sec | 36 | 100-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 51 |
| new_1000sec | 37 | 1000-second measurement is new. 0 => Old data 1 => New data | Unsigned Integer-1 | N/A | 0 or 1 | 51 |
| reserve8 | 38 | Reserved. Eight bytes. | Unsigned Integer –8 | N/A | 0 |  |

## Dependencies

None identified.  <Identify dependencies of any sort that will make this interface work. Examples are using NASA supplied software, timeliness of other data/models, etc.  Avoid duplicating information controlled by another document.>

This Page Intentionally Left Blank

Notes

- Seconds to HH:MM:SS (UTC) format:

0.0	=>	00:00:00

86399.0 =>	23:59:59

86400.0 =>	Leap second

- This offset (transmit_time_tag_delay) should be added to the time tag.  It is used to compensate for differences in the time tag point and the antenna radiation point.

- This offset (rcv_time_tag_delay) should be subtracted from the time tag.  It is used to compensate for differences in the time tag point and the antenna radiation point.

- Array delay (array_delay) is included in the station calibration value (stn_cal) measurement and should be subtracted from the time tag.

- Spacecraft transponder lock (scft_transpd_lock), spacecraft transponder number (scft_transpd_num), spacecraft two-way non-coherent (TWNC) status (scft_twnc_stat), and spacecraft oscillator type (scft_osc_type) are obtained from spacecraft engineering data, which may not be available.

- Spacecraft oscillator frequency (scft_osc_freq) is obtained from spacecraft project supplied data.

- Spacecraft transponder delay (scft_transpd_delay) is based on spacecraft and configuration data supplied from spacecraft project.  In the future, it may be based on engineering data from the spacecraft.  This is the delay the ranging signal experiences through the spacecraft.

- PHASE = HI * 232 + LO + FRAC * 2-32 , 

where,

HI = ul_hi_phs_cycles, or phs_hi_x (with x = 0 through 9), phs_hi_avg, or dop_cnt_hi, or total_cnt_phs_ob_hi
LO = ul_lo_phs_cycles, or phs_lo_x (with x = 0 through 9), or phs_lo_avg, or dop_cnt_lo, or total_cnt_phs_obs_lo
FRAC = ul_frac_phs_cycles, or phs_frac_x (with x = 0 through 9), or phs_frac_avg, or dop_cnt_frac, or total_cnt_phs_obs_frac

- Not applicable.

- If hardware at station allows splitting the uplink and downlink ranging delays, the value will be included here.  Otherwise, it is set to 0.0.

- Measured code value (ul_rng_phs) and measured range value (dl_rng_phs) are the phase of the ranging signal at the time tag.

- T1 setting (t1) is the length of time that the first component (the clock) is transmitted.

- T2 setting (t2) is the length of time that each subsequent component is transmitted.

- T3 setting (t3) is the length of time that the clock is transmitted for each DRVID measurement.

- Component frequency is F_EXC * 2-(n+2), where n is the component number and F_EXC is the exciter reference signal (see note 17).

- Chopping modulates the ranging signal with a subcarrier at the chop component frequency (chop_comp_num), for all components after and including the chop start component (chop_start_num).  For example, if the chop start component value is 6 and the chop component is 5, all components from 6 on will be modulated with component 5.  If the chop value is zero, all components starting with 15 and larger are chopped with the clock component.

17.	The exciter reference frequency (F_EXC) is defined as follows:

F_EXC = FRQ_UP * (exc_scalar_num/exc_scalar_den)

Where FRQ_UP is the uplink carrier frequency.

18.	Sequential ranging cycle time is defined as follows:

rng_cycle_time = (t1 + 2) + (last_comp_num – first_comp_num) * (t2 + 1) + num_drvid * (t3 + 2) + 1

19.	The PN ranging code is a combination of multiple sequences logically combined.  The code state is the particular bit (or chip) in the sequence, plus the phase of that chip at the time tag.  For a component length L, and a subsequence state S, the code state C is related to L and S by:

S = C mod L

20.	PN chip rate = F_EXC / clk_divider

- The first “n” bits (where n is the length specified in len_seqj) define the PN subsequence, e.g., a value of 46 for def_seq4 gives the following sequence: 0101110, which will have a value of 7 in len_seq4.

22.	Code length (pn_code_length) equals the result of multiplying the lengths of all of the subsequences together.

- PN cycle time is 16 * clk_divider * pn_code_length.

- One Range Unit (RU) is defined as:

1 RU = (exc_scalar_den / exc_scalar_num) / (16 * FRQ_UP)

Where FRQ_UP is the uplink carrier frequency.   Range is measured in RU to give a stable reference measurement when the uplink is being ramped.

- If carrier is suppressed (carr_resid_wt = 0.0), then the data power is used for the carrier tracking.

- Doppler noise (dop_noise) is the standard deviation of the detrended downlink frequency residuals.  The detrending is the removal of the least squares linear fit of the frequency residuals over the sample period.  For the Downlink Carrier Phase data type (data type 1) and Doppler data type (data type 6), the sample period is 1 second.  For the Carrier observable data type (data type 16), the sample period is sample integration time (obs_cnt_time) times the number of samples (num_obs).  The equation for the Doppler noise is (F is the frequency residual, FL is the linear least squares fit of F, and t is the spacing between points):

- carr_resid_wt is the weight value applied to residual phase error in carrier tracking; suppressed carrier weight is 1.0 minus this value, e.g.,

(err = carr_resid_wt * (err_resid + (1 – carr_resid_wt) * (err_suppressed

- Figure of Merit (FOM) (figure_merit) is the estimate of the probability of successfully acquiring all of the lower components (other than the clock component).  It is expressed as a percentage (0.0 to 100.0).  For sequential ranging, it is defined as:

Where Erf(*) is the error function.

For PN ranging, it is defined as:

Where, Cmin and Cmax are the minimum and maximum correlation value for each subsequence and LEN(I) is the length of the ith subsequence (2, 7, 11, 15, 19, and 23).

- Range residual accuracy depends on the accuracy of the predicts and is rarely better than 1 (sec (1000 RU).

- DRVID (drvid) stands for Differenced Range Versus Integrated Doppler.  It is a measurement of the difference between the group and phase delay of the media.  The measurement (at time tag TT) is the difference between two consecutive measured range points (i.e., points separated by the cycle time) minus the scaled difference in the uplink and downlink carrier phases over the same time period.  The measurement is defined below:

D_RNG = (meas_rng(TT) – meas_rng(TT- rng_cycle_time)), mod rng_modulo

I_DOP = {((T(TT) - (T(TT – rng_cycle_time)) –

(scft_transpd_turn_den / scft_transpd_turn_num) *

((R(TT) - (R(TT – rng_cycle_time))}

drvid = D_RNG – [16 * (exc_scalar_num / exc_scalar_den) * I_DOP mod rng_modulo]

This has previously been called pseudo-DRVID, since the measurement does not require increasing the cycle time by adding additional clock transmissions during the measurement.  The method of using additional clock cycles does not measure the carrier phase over the same period of time as the range measurement; this is why the pseudo-DRVID implementation was selected.

- Slipped cycles (slipped_cycles) are estimated by processing the frequency residuals in a software-simulated, digital phase-locked loop and comparing the phase error with slip conditions.  This estimate is subject to degradation during high noise conditions.  The slipped cycles value is the number of cycle slips (both positive and negative) detected in this manner, for the sample interval.

- Delta Frequency/Frequency (delta_ff) is the change in downlink frequency since the last sample, divided by the downlink frequency at this time tag.

- A set of measurements is provided in the Received Carrier and Total Count Phase Observables data types (data types 16 and 17).  For each set, a number of measurements (num_obs) and a time interval (obs_cnt_time) are provided.  The first measurement is at the time tag reported in the header; the ith measurement (i = 1 to number of measurements) is at the time tag (TT) plus (i-1) * obs_cnt_time.  The interval of time covered by the measurements is TT – obs_cnt_time to TT + (number of measurements – 1)* obs_cnt_time.

- The Doppler Count is defined as difference in the uplink carrier phase (generated by integrating ul_freq), scaled by the spacecraft transponder turn around ratio, minus the downlink carrier phase plus a bias term (generated by integrating dop_cnt_bias_freq).  The bias term is used to keep the Doppler Count a positive value.  For UPL-DTT antennas, the ul_freq value is determined by the downlink frequency; for other antennas, it depends on the equipment configuration.  The time tag of the ith measurement (i equals 1 to 10) is TT + (i  - 1) * 0.1.  The time tag is the end of the Doppler Count interval.

Doppler Count = - ((R,i ) + ((scft_transpd_turn_num/scft_transpd_turn_den) * ul_freq

+ dop_cnt_bias_freq )* (TimeI – Timestart)

- The Received Carrier Frequency Observable is defined as the negative of the difference in the downlink phase at the end of the interval and the downlink phase at the start of the interval, divided by the interval time.  The time tag point of the difference is the middle point of the count time interval (note that this means that the time tag may be on the half second).  The time tag of the ith measurement (i equals 1 to num_obs) is TT + (i – 1.0) * obs_cnt_time.

Observable = - ((i - (i-1) / obs_cnt_time

- The Total Count Phase Observable is the difference between the downlink carrier phase at the measurement time tag and the downlink carrier phase at a starting point (a running integration).  The time of the starting point is given by total_cnt_phs_st_year, total_cnt_phs_st_doy, and total_cnt_phs_st_sec.  The starting point changes whenever something causes the carrier lock to be broken, such as spacecraft mode changes or downlink loss of lock.  The time tag of the ith measurement (i equals 1 to num_obs) is TT + (i  - 1) * obs_cnt_time.

Observable = - ((i - (start)

The value reported is the negative of the observable, e.g.:

Reported Observable  = ((i - (start)

- Sequential ranging ambiguity (rng_modulo) in Range Units is defined as 26+last_comp_num.

- Sequential measured range (meas_rng) is the difference between the uplink ranging phase (ul_rng_phs) and the downlink ranging phase (dl_rng_phs) (for UPL-DTT antennas).  For non-UPL-DTT antennas, the Sequential Ranging Assembly range value is used.  The difference is the positive modulo of rng_modulo value.  This measurement is not corrected for any calibration issues.

39.	Range Observable is defined as the measured range (meas_rng) minus the calibration correction.  This observable is valid for both UPL-DTT and non-UPL-DTT antennas and is supplied to maintain compatibility between the two.   The calibration correction is defined as:

Correction = (ul_stn_cal – transmit_time_tag_delay) + ul_zheight_corr  + scft_transpd_delay + (dl_stn_cal – rcv_time_tag_delay – array_delay) + dl_zheight_corr

- If the measured uplink calibration value (ul_stn_cal) as reported in the uplink range SFDUs is non-zero, then the uplink calibration value (ul_stn_cal) in the derived SFDUs for sequential and PN range is this value.  Otherwise, it is one-half of the station calibration value (stn_cal).  If the value is invalid, the parameter is set to –1.0.

- If the measured downlink calibration value (dl_stn_cal) as reported in the downlink ranging SFDUs is non-zero, then the downlink calibration value (dl_stn_cal) in the derived SFDUs for sequential and PN range is this value.  Otherwise, it is one-half of the station calibration value (stn_cal). ).  If the value is invalid, the parameter is set to –1.0.

- The uplink frequency (ul_freq) is provided for computing the Range Unit definition for those antennas that do not support ramped uplinks (i.e., no Data Type 9).

- Range noise (rng_noise) is the standard deviation of up to the last 100 (i.e., if more than 100 data points exist, only the last 100 are used) range residuals, detrended by removing the least squares linear fit of the data.  The equation for the Range noise is (R is the range residual, RL is the linear least squares fit of R, N is the number of points (up to 100), and t is the spacing between points):

- DRVID noise (drvid_noise) is the standard deviation of up to the last 200 (i.e., if more than 200 data points exist, only the last 200 are used) DRVID values.  The equation for the DRVID noise is (D is the DRVID residual, N is the number of points (up to 200), and t is the spacing between points):

- PN ranging ambiguity (modulo value) is defined as:

rng_modulo = 16 * clk_divider * pn_code_length

- PN measured range value (meas_rng)  is the difference between the uplink ranging phase (ul_rng_phs) and the downlink ranging phase (dl_rng_phs).  It is only available from the UPL-DTT antennas.  The difference is the positive modulo of the rng_modulo value.  This measurement is not corrected for any calibration issues.

- Smoothed noise is the standard deviation of the detrended downlink frequency residuals.  The detrending is the removal of the least squares linear fit of the frequency residuals over the sample period.  Estimates are computed for 0.1, 1, 10, 100, 200, and 600-second intervals.  The minimum sample period is 180 seconds, the maximum is 10,800.  The standard deviation is computed over 18 points; if the number of points in the reporting period is more than 18 (e.g., 0.1-second and 1.0-second), the 18-sample standard deviations are averaged.  The equation for the Smoothed noise is (F is the frequency residual, FL is the linear least squares fit of F, and t is the time spacing between points):

- Since the record is generated every 180 seconds and each integration needs 18 points, the longer integrations will not be updated every time.  The new_xxx flags are used to indicate which integrations have been updated.

- Allan deviation is computed for interval (() values of 0.1, 1, 10, 100, and 1000 seconds.  The record is nominally output once every 1000 seconds.  The frequency residuals are used for the computation (to remove the known motion effects, such as earth rotation).  The result is normalized to DSN channel 14 (2295 MHz for S-band, 8415 MHz for X-band, and 31.977 GHz for Ka-band); this value is referred to as F0.  The number of points, N, is equal to the integration time, INT_TIME, divided by (.

- percent_data_used indicates if some data in the integration period was not used (e.g., carrier was out of lock).

- If a record is generated due to a change in system status (e.g., receiver mode change), the report time will be short of the normal 1000 seconds, so the longer integrations may not have a new point computed.  The new_xxx flags are used to indicate which integrations have been updated.

- Some hardware (ground or spacecraft) may invert the ranging modulation.  invert allows these inversions to be corrected on the uplink or downlink processing.

- Loop Type (carr_loop_type) is the number of poles in the carrier phase locked loop transfer function.  The number poles (or order) of the loop filter is the Loop Type minus one.  For each increment in the Loop Type, one higher order derivative of Doppler is tracked out to zero (Type 1 tracks out phase offsets, Type 2 tracks out frequency errors, Type 3 tracks out frequency rate errors).

- The time offset (prdx_time_offset) is a value added to the current time when generating the predicted frequency from the frequency predicts (F(t)).  Thus, the predicted frequency (F_PRED), at time t, used by the tracking loop is:

F_PRED = F(t + prdx_time_offset)

- The frequency offset (prdx_freq_offset) is a value added to the frequency value generated from the frequency predicts (F(t)).  Thus, the predicted frequency (F_PRED), at time t, used by the tracking loop is:

F_PRED = F(t) + prdx_freq_offset

- Correlation validity (correl_vld_flag)  is reported by the downlink ranging equipment.  It is an estimate of whether or not the clock component is properly aligned with the received ranging signal (it measures the power in the inphase and quadrature signals when correlating the lower components – if the clock is properly aligned, the power in the inphase signal is much greater than the quadrature signal).

- The Angles Validity Flag (ang_vld_flag)  is set by the tracking equipment to indicate whether or not the angle data is valid.

- The signal level (rcv_sig_lvl) is either provided by the tracking station (non-UPL-DTT antennas), or derived from other parameters (UPL-DTT antennas).  For the 34m and 70m antennas, the derivation is as follows:

Signal Level = P_N0 – (K_DB + 10 * log10(system_noise_temp))

Where K_DB is Boltzmann’s constant (-198.6 dBm/Hz/k), system_noise_temp is the system noise temperature, and P_N0 is either pcn0 (car_resid_wt > 0.0) or pdn0 (car_resid_wt = 0.0).

- The In Phase Time (transmit_inphs_time or rcv_inphs_time) is the time point that the ranging modulation reference was initialized to zero phase.  It is used for three-way ranging cases.  It is seconds of day offset from the block time tag.

- Distance (in time) to the phase center of the antenna that is not included in the station calibration.  Included in this value is the delay to and from the test translator, the delay inside the test translator, the delay from the range calibration coupler to the phase center of the antenna, and the delay between the main antenna dish and the subreflector.  Z-height is expressed in seconds, so it must be converted to Range Units before it is included in the Range Observables.  The uplink part of this compensation (which is the delay from the point that the test translator taps off of the uplink path to the phase center) is provided in ul_zheight_corr and the downlink part (which is the delay from the phase center to the point where the test translator joins the downlink path, minus the delay of the test translator path) is in dl_zheight_corr.

61.	When downlink carrier data is received, it reports the configuration that was used at the tracking station for the source of the downlink (e.g., three-way with DSS 65).  However, that may not be the actual spacecraft mode (for example, the spacecraft may have been locked to an uplink from DSS 54, but the receiving station did not have any three-way predicts for DSS 54, so the predicts for DSS 65 were used instead).  A validation is done to determine the actual spacecraft mode and is reported in the validated uplink station (vld_ul_stn) and validated doppler mode (vld_dop_mode) fields of the downlink data secondary CHDO.

- The Carrier and Total Phase Count Pre-fit Residual Tolerance flags (carr_prefit_resid_tol_flag and total_phs_cnt_prefit_resid_tol_flag) indicate whether or not the pre-fit residuals are within the tolerance (carr_prefit_resid_tol_value and total_phs_cnt_prefit_resid_tol_value) set by the spacecraft project.  The prefit residual flags (carr_prefit_resid_tol_flag and total_phs_cnt_prefit_resid_tol_flag) are set to Not Applicable if the prefit residual validity flags (carr_prefit_resid_vld_flag and total_phs_cnt_prefit_resid_vld_flag) indicate invalid.

- The Range Residual Tolerance flag (rng_resid_tol_flag) indicates whether or not the range residual is within the tolerance (rng_resid_tol_value) set by the spacecraft project.

- The DRVID Tolerance flag (drvid_tol_flag) indicates whether or not the DRVID value is within the tolerance (drvid_tol_value) set by the spacecraft project.

- The Pr/N0 Residual Tolerance flag (prn0_resid_tol_flag) indicates whether or not the Pr/N0 residual is within the tolerance (prn0_resid_tol_value) set by the spacecraft project.

- The Range Sigma Tolerance flag (rng_sigma_tol_flag) indicates whether or not the range sigma (noise) is within the tolerance (rng_sigma_tol_value) set by the spacecraft project.

- The Range Validity flag (rng_vld_flag) indicates that the range data is valid if the receiver is in-lock, if the Correlation Validity flag (correl_vld_flag) indicates valid data, and the FOM (figure_merit) is above its tolerance value (fom_tol_value).

- The Range Configuration Change flag (rng_config_flag) is set whenever the system determines the microwave configuration has changed since the ranging calibration was done.

- Note 69 has been deleted.

- The Metrics Validity flag (metrics_vld_flag) indicates whether or not the downlink ranging equipment was able to process the ranging data to get a measurement of range and DRVID (for example, the pass may have been three-way and the uplink data was not available).

- Note 71 has been deleted.

- Currently, the equipment that performs the tone range measurement includes the corrections for the calibration and the Z-height correction in the reported range; however, these values are not reported by the station.  Thus, stn_cal, ul_zheight_corr, dl_zheight_corr are set to 0.0.  The range observable (rng_obs) is equal to meas_rng minus the spacecraft transponder delay scft_transpd_delay.  If the equipment at the station is corrected, the values will be non-zero.

- The Modification Time items (day and msec) are set to 0 when the block is first created.  If any data in the block is changed, the items are set to the time of the modification.  The time is expressed as the time (UTC) since the epoch of January 1, 1958.  The time is represented as days since the epoch and milliseconds of the day.

- The record creation time is the time when the data processing task first creates the record.  It is expressed as the time (UTC) since the epoch of January 1, 1958.  The time is represented as days since the epoch and milli-seconds of the day.

75.	The In Phase Time (transmit_inphs_time_xxx or rcv_inphs_time_xxx, where xxx is year, doy, or sec) is the time point (UTC) that the ranging modulation reference was initialized to zero phase.  It is used for three-way ranging cases.  When reported from the DSN stations, it is reported as an absolute time (see note 59 regarding its other format).

76.	The Downlink Range Observable (rng_obs_dl) is defined as the calibration correction minus the downlink ranging phase.  It is only valid for UPL-DTT antennas.  The calibration correction is defined as:

Correction = (ul_stn_cal – transmit_time_tag_delay) + ul_zheight_corr + scft_transpd_delay + (dl_stn_cal – rcv_time_tag_delay – array_delay) + dl_zheight_corr

77.	Downlink range observable validity flag (rng_obs_dl_vld_flag) indicates whether or not the Downlink range observable item (rng_obs_dl) is valid.  It will be invalid if the data is for a non-UPL-DTT antenna.

78.	The Clock Offset Epoch Time (clk_off_epoch_year, clk_off_epoch_doy, and clk_off_epoch_sec) is the time (UTC) that the two clock offsets (clk_off_1 and clk_off_2) where measured .

79.	The uplink data is only valid if the validated spacecraft coherency (vld_scft_coh) indicates an uplink (value of 1 or 3).

80.	The DRVID computation is done by the data processing task in AMMOS.

81.	This computation is done at the station.  The metrics validity flag (metrics_vld_flag) indicates its validity.

82.	For DTT data, the downlink band is assumed to be correct.  For non-DTT data, a validation is done.  In the case of 26m stations, which use the two acquisition aid antennas (for both S- and X-band), if the downlink band cannot be definitively determined, the value gets set to "S or X".

83.	The carrier lock status (carr_lock_stat) for non-DTT antennas is inferred from other values.

84.	The count time (interval), Tc, that is used to form an observable is constrained by the sample interval.

85.	A set of measurements is provided in the Doppler Count data type (data type 6).  For each set, a number of measurements (10 or 1) and a time interval (sampl_time) are provided.  The first measurement is at the time tag reported in the header; if there are 10 measurements, the ith measurement (i = 1 to number of measurements) is at the time tag (TT) plus (i-1) * 0.1.  The interval of time covered by the measurements is TT to TT + (number of measurements – 1)* 0.1.

86.	Until prefit residual values (rng_dl_prefit_resid, rng_prefit_resid, and carr_prefit_resid) are delivered, they will be indicated as invalid by setting their residual flags (rng_dl_prefit_resid_vld_flag, rng_prefit_resid_vld_flag, and carr_prefit_resid_vld_flag, respectively) to a value of 0.

87.	Arraying is done using the Full Spectrum Processor (FSP).  There are two FSPs per complex.

88.	This field only pertains to the Doppler (Data Type 6), the Received Carrier Frequency Observables (Data Type 16) and the Total-Count Phase Observables (Data Type 17) data CHDOs.  Otherwise, when not applicable, the field is set to 0.  In the case of Data Types 16 and 17, this field describes the compression interval, which ranges from 0.1 through 3600.0 seconds.  In the case of Data Type 6, this field describes the sample interval.  26m stations are capable of producing tracking data at sample intervals of 0.1, 1, 10, or 60 seconds.  UPL/DTT stations produce tracking data at a 0.1 second interval.

This Page Intentionally Left Blank

File Format

LVO Structure of Files

When the data defined by this document are stored in a file, the file is wrapped with an attached header.  The file consists of nested LVOs, including a catalog LVO (known as the K-object LVO) and a data LVO (known as the I-object LVO).  The catalog LVO contains the meta-data needed to catalog the actual tracking data.  The data LVO consists of CHDO SFDUs defined in Section 3.  The LVO structure of a file is depicted in Figure B-1. Further details on the contents of the label and value fields of each LVO are provided in the following subsections.

+---------------------------------------------+

L¦  Primary SFDU Label                         ¦

+-+  +---------------------------------------+¦

¦ L¦  K-Object Label                       ¦¦

¦  +-+                                      ¦

¦   V¦  Catalog Information                ¦¦

¦    ¦  End Marker                         ¦¦

V¦  +---------------------------------------¦¦

¦ L¦  I-Object Label                       ¦¦

¦  +-+                                     ¦¦

¦   V¦  CHDO SFDUs                         ¦¦

¦    ¦                                     ¦¦

.    .                                     ..

.    .                                     ..

.    .                                     ..

¦    ¦  EOF                                ¦¦

+-------------------------------------------+

L = label field         V = value field

Figure B-1.  LVO Structure of Files

Physical Layout of Files

The physical layout of the TRK-2-34 file is shown in Figure B-2.  The length in bytes is 88+M+L, where M is the length of the catalog field and L is the length of the CHDO SFDUs.  The structure is divided into three main parts:

- primary label of the entire SFDU (Table B-1 describes the primary label.)

- K-header.  The K-header (or K-object) consists of the K-header SFDU label (or K-object SFDU label), catalog information, and an end marker.  The catalog information consists of meta-data for cataloging the SFDU file.  The meta-data are in the form of keyword-value pairs (hence, the “K” for keyword).  (Tables B-2 and B-3 describe the K-header.)

- I-object.  The I-object (where “I” stands for information) contains the CHDO SFDUs defined by Section 3, preceded by an I-object SFDU label. (Table B-4 describes the I-object SFDU label.)

BIT

+-----------------------------------------------+

¦1 ¦2 ¦3 ¦4 ¦5 ¦6 ¦7 ¦8 ¦1 ¦2 ¦3 ¦4 ¦5 ¦6 ¦7 ¦8 ¦

+-----------------------------------------------¦

BYTE 0¦                                               ¦

+-                                             -¦

...              PRIMARY SFDU LABEL             ...

...                  (20 BYTES)                 ...

+-                                             -¦

18¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

20¦                                               ¦

+-                                             -¦

...             K-OBJECT SFDU LABEL             ...

...                  (20 BYTES)                 ...

+-                                             -¦

38¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

40¦                                               ¦

+-                                             -¦

...            CATALOG INFORMATION              ...

...                                             ...

+-                                             -¦

38+M¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

40+M¦                                               ¦

+-                                             -¦

...             K-OBJECT END MARKER             ...

...                  (20 BYTES)                 ...

+-                                             -¦

58+M¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

60+M¦                                               ¦

+-                                             -¦

...            I-OBJECT SFDU LABEL              ...

...                  (20 BYTES)                 ...

+-                                             -¦

78+M¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

80+M¦                                               ¦

+-                                             -¦

...              BINARY DATA OBJECT             ...

...                                             ...

+-                                             -¦

78+M+L¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

80+M+L¦                                               ¦

+-                                             -¦

...             END OF FILE MARKER              ...

...                  (8 BYTES)                  ...

+-                                             -¦

86+M+L¦                                               ¦

+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--¦

¦1 ¦2 ¦3 ¦4 ¦5 ¦6 ¦7 ¦8 ¦1 ¦2 ¦3 ¦4 ¦5 ¦6 ¦7 ¦8 ¦

+-----------------------------------------------+

M is length of Catalog Information

L is length of Tracking SFDUs

Figure B-2.  File Layout

See Figure B-3 for a sample header of a TRK-2-34 file.

CCSD3ZF0000100000001NJPL3KS0PDSX$T-2-34$

PDS_VERSION_ID = PDS3

RECORD_TYPE = UNDEFINED

MISSION_NAME = CASSINI

SPACECRAFT_NAME = CASSINI

SPACECRAFT_ID = 82

MISSION_ID = 7

DATA_SET_ID = TRK234

FILE_NAME = 20013610115SC82.234

PRODUCER_ID = TDDS

PRODUCT_CREATION_TIME = 2001-361T23:59:59

START_TIME = 2001-361T01:15:10

STOP_TIME = 2001-361T12:30:30

INTERCHANGE_FORMAT = BINARY

NOTE = “Carrier lock status in DT1 changed by Jane Doe.”

CCSD$$MARKER$T-2-34$NJPL3IF0T23400000001

Figure B-3.  Sample Header of File

    - Primary SFDU Label

Bytes 0 through 19 of the tracking SFDU file contain the primary SFDU label field for the files.  The format and content of the label are defined in Table B-1.

Table B-1.  Primary SFDU Label

| Byte | Data Item. Description and Units. | Format | Range |
| --- | --- | --- | --- |
| 0 to 3 | Control authority identifier (CAID). This CAID field indicates that the data description information (referred to in bytes 8 to 11) for this SFDU is maintained and disseminated by the CCSDS control authority. Control authority identifiers are assigned by the CCSDS. Refer to AnyCatalog, p.4-12,4-13; MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; PDS Stds Ref, p.16-5. | Restricted ASCII-4 | ‘CCSD’ |
| 4 | SFDU version identifier. This version field indicates how this primary SFDU label is delimited. The value of ‘3’ indicates that this LVO can be delimited by marker, EOF (end of file), or length. Refer to AnyCatalog, p.4-12,4-13; MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; PDS Stds Ref, p.16-5. | Restricted ASCII-1 | ‘3’ |
| 5 | SFDU class identifier. This class identifier field gives a high-level classification of the content of the value field of this LVO (i.e., this TRK-2-34 LVO that contains the K-header LVO and the I-object LVO). The value of ‘Z’ indicates that the value (V) field of this LVO contains a JPL LVO with a CCSD CAID. Refer to AnyCatalog, p.4-12,4-13; MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; PDS Stds Ref, p.16-5. | Restricted ASCII-1 | ‘Z’ |
| 6 | Delimiter identifier. This delimitation identifier indicates the type of delimiter this primary SFDU label uses for its last eight bytes. A value of ‘F’ indicates this label ends with ‘00000001’, as specified in bytes 12 to 19, which implies that the entire SFDU is closed with an EOF marker. Refer to AnyCatalog, p.4-12,4-13; MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; PDS Stds Ref, p.16-5. | Restricted ASCII-1 | ‘F’ |
| 7 | Reserved. This byte is a spare field. Refer to AnyCatalog, p.4-12,4-13; MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; PDS Stds Ref, p.16-5. | Restricted ASCII-1 | ‘0’ |
| 8 to 11 | Data description package identifier. This field uniquely identifies (for the specified Control Authority, i.e., CCSDS, per bytes 0 to 3) the package that contains the definition of the data object [or value (V) field of this LVO]. The value shown here is registered with the specified control authority. Refer to AnyCatalog, p.4-12,4-13; MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; PDS Stds Ref, p.16-5. | Restricted ASCII-4 | ‘0001’ |
| 12 to 19 | Length attribute of the SFDU. This field is designated the “length” field because data are delimited by length for stream data. However, since this SFDU is considered to be a file SFDU, rather than a stream SFDU, the end of the TRK-2-34 LVO (SFDU) is designated by an EOF marker. The EOF marker is specified in this primary SFDU label as ‘00000001.’ Refer to AnyCatalog, p.4-12,4-13; MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; PDS Stds Ref, p.16-5. | Standard ASCII-8 | ‘00000001’ |

B.2.2  K-Header (or K-Object)

Bytes 20 to 59+M are the K-header (or K-Object) for the file (M is the length of the catalog information, which is variable length).  The three components of the K-header are described below.

B.2.2.1  K-Header  SFDU Label

Bytes 20 to 39 are the label field for the K-Header SFDU (or Catalog LVO) for the files.  The 20 bytes of the label field are defined below in Table B-2.

Table B-2.  K-Header (or K-Object) SFDU Label

| Byte | Data Item. Description and Units. | Format | Range |
| --- | --- | --- | --- |
| 0 to 3 | Control authority identifier (CAID). This CAID field indicates that the data description information (referred to at bytes 8 to 11) for this SFDU is maintained and disseminated by the NASA/JPL control authority. | Restricted ASCII-4 | ‘NJPL’ |
| 4 | SFDU version identifier. This version field indicates how this K-header SFDU label is delimited. The value of ‘3’ indicates that this LVO can be delimited by marker, EOF (end of file), or length. In this case, the actual delimiter is by marker, as indicated by byte 6. The value of ‘3’ is required per <Any Catalog>, p.4-3, and in PDS Stds Ref., p.16-6. Also refer to MGDS User’s Guide/Working with File Data (JPL D-6060), Ch. 2. | Restricted ASCII-1 | ‘3’ |
| 5 | SFDU class identifier. This class identifier field gives a high-level classification of the content of the value field of this LVO (i.e., the K-header LVO). The value of ‘K’ indicates that the value (V) field of this LVO contains a K-header. [The K-header contains metadata that describes the I-object LVO (information or data object) that follows it.] The value of ‘K’ is required per <Any Catalog>, p.4-3, and in PDS Stds Ref., p.16-6. Also refer to MGDS User’s Guide/Working with File Data (JPL D-6060), Ch. 2. | Restricted ASCII-1 | ‘K’ |
| 6 | Delimiter identifier. This delimitation identifier indicates the type of delimiter this K-header SFDU label uses for its last eight bytes. A value of ‘S’ indicates that this label ends with a marker, i.e., a start marker (signifying the start of the value field). [The value (V) field of the K-header LVO is the Catalog information. It is delimited by a start marker at the end of this K-header SFDU label, and then by a matching end marker at the end of the value (V) field.] The marker is specified in the ‘Length attribute’ field of this label at bytes 12 to 19. The value of ‘S’ is required per PDS Stds Ref., p.16-6. Also refer to MGDS User’s Guide/Working with File Data (JPL D-6060), Ch. 2. | Restricted ASCII-1 | ‘S’ |
| 7 | Reserved. This byte is a spare field. | Restricted ASCII-1 | ‘0’ |
| 8 to 11 | Data description package identifier. This field uniquely identifies (for the specified Control Authority, i.e., NJPL, per bytes 0 to 3) the data object [or value (V) field of this LVO]. The value shown here is registered with the specified control authority. The value of ‘PDSX’ is required per <Any Catalog>, p.4-3, and in PDS Stds Ref., p.16-6. Also refer to MGDS User’s Guide/Working with File Data (JPL D-6060), Ch. 2. | Restricted ASCII-4 | ‘PDSX’ |
| 12 to 19 | Length attribute of the SFDU. The Catalog information is delimited with a start and end marker. | Standard ASCII-8 | ‘$T-2-34$’ |

B.2.2.2  Catalog Information

The catalog information for the files starts at byte 40 and is defined below in Table B-3.  This value field of the LVO contains the set of parameters and values, in <keyword/parameter>=<value> format, of attributes that are pertinent to the file data.  Each line is terminated with a carriage return (ASCII decimal code 13, written as <CR> or Ctrl-M), and a line feed (ASCII decimal code 10, written as <LF> or Ctrl-J).  The values must conform to the standard ASCII character set (32 through 127 decimal).  In addition, the values should be in upper case, except for the NOTE field.

Table B-3.  Catalog Information (Value Field of the K-Object)

| Ref # | Keyword-Value Pairs. Description and Units. | Range for Value |
| --- | --- | --- |
| 1 | PDS_VERSION_ID = <value><CR><LF> Represents the version number of the standards document that is valid when the label is created. | ‘PDS3’ |
| 2 | RECORD_TYPE = <value><CR><LF> The record format of this file. | ‘UNDEFINED’ |
| 3 | MISSION_NAME = <value><CR><LF> The name of the mission or project that is associated with the data contained in the I-object. Must be upper case. | Varies |
| 4 | SPACECRAFT_NAME = <value><CR><LF> The full, unabbreviated name of the spacecraft that is associated with the data contained in the I-object. Must be upper case. | Varies |
| 5 | SPACECRAFT_ID = <value><CR><LF> The decimal representation of the applicable DSN spacecraft number as defined in Reference [3a]. | ‘0’ thru ‘255’ |
| 6 | MISSION_ID = <value><CR><LF> The decimal representation of the applicable DSN mission number per Reference [3a]. | ‘0’ thru ‘255’ |
| 7 | DATA_SET_ID = <value><CR><LF> The unique identifier for this data type. | ‘TRK234 ‘ |
| 8 | FILE_NAME = <value><CR><LF> The unique file name, without a directory path specified, for this SFDU file. The file name shall be of the form: yyyydddhhmmSCsssss.234, where, yyyy is the four-digit year ddd is the three-digit day-of-year (001 thru 366) hh is the two-digit hour into the day (00 thru 23) mm is minutes into the hour (00 thru 59) SC is fixed, and denotes that the spacecraft ID is to follow: sssss is the spacecraft ID (per Reference [3a], with leading zeros omitted) . 234 is a fixed suffix, and identifies the file as being a TRK-2-34 file. The time reflects the time of the earliest tracking sample contained in the file. | Varies |
| 9 | PRODUCER_ID = <value><CR><LF> A short name or acronym for the producer or producing team/group (e.g., TDDS) of this file. An ASCII character string, limited to 20 characters (must be upper case). | Varies |
| 10 | PRODUCT_CREATION_TIME = <value><CR><LF> This attribute indicates the UTC time at which this file was created. The value is specified in the following time format: yyyy-dddThh:mm:ss where, yyyy four-digit year ddd day-of-year (001 thru 366) T ASCII literal field (i.e., “T”) hh hours of the day (00 thru 23) mm minutes of the hour (00 thru 59) ss seconds of the minute (00 thru 60), allows for leap second | any valid UTC |
| 11 | START_TIME = <value><CR><LF> This attribute identifies the earliest time tag (in UTC) reported across all SFDU secondary CHDOs included in the data object. The value is specified in the following time format: yyyy-dddThh:mm:ss where, yyyy four-digit year ddd day-of-year (001 thru 366) T ASCII literal field (i.e., “T”) hh hours of the day (00 thru 23) mm minutes of the hour (00 thru 59) ss seconds of the minute (00 thru 60), allows for leap second | any valid UTC |
| 12 | STOP_TIME = <value><CR><LF> This attribute identifies the latest time tag (in UTC) reported across all SFDU secondary CHDOs included in the data object. The value is specified in the following time format: yyyy-dddThh:mm:ss where, yyyy four-digit year ddd day-of-year (001 thru 366) T ASCII literal field (i.e., “T”) hh hours of the day (00 thru 23) mm minutes of the hour (00 thru 59) ss seconds of the minute (00 thru 60), allows for leap second | any valid UTC |
| 13 | INTERCHANGE_FORMAT = <value><CR><LF> Identifies the way the data object is stored. | ‘BINARY” |
| 14 | NOTE = “<value>”<CR><LF> Description of changes made to the data in this TRK-2-34 file as a result of manual editing (may be upper or lower case). | Varies |

B. 2.2.3  K-Object End Marker

After the catalog information, starting at byte 40+M (M being the length of the catalog field), is the marker field.  The marker field delimits the end of the catalog LVO.  The 20 byte field is the following ASCII string:

“CCSD$$MARKER$T-2-34$”.

B.2.3   I-Object SFDU Label

Bytes 60+M to 79+M are the label field for the I-Object SFDU.  The 20 bytes are  defined below in Table B-4.

Table B-4.  I-Object SFDU Label

| Byte | Data Item. Description and Units. | Format | Range |
| --- | --- | --- | --- |
| 0 to 3 | Control authority identifier (CAID). This CAID field indicates that the data description information (referred to at bytes 8 to 11) for this SFDU is maintained and disseminated by the NASA/JPL control authority. | Restricted ASCII-4 | ‘NJPL’ |
| 4 | SFDU version identifier. This version field indicates how this I-object SFDU label is delimited. The value of ‘3’ indicates that this LVO can be delimited by marker, EOF (end of file), or length. In this case, the actual delimiter is by EOF, as indicated by byte 6. The value of ‘3’ is required per PDS Stds Ref., p.16-7. Also refer to MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; AnyCatalog, p.4-12 to 4-13. | Restricted ASCII-1 | ‘3’ |
| 5 | SFDU class identifier. This class identifier field gives a high-level classification of the content of the value field of this LVO (i.e., the I-object LVO). The value of ‘I’ indicates that the value (V) field of this LVO contains an I-object (or information object.) The value of ‘I’ is required per PDS Stds Ref., p.16-7. Also refer to MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; AnyCatalog, p.4-12 to 4-13. | Restricted ASCII-1 | ‘I’ |
| 6 | Delimiter identifier. This delimitation identifier indicates the type of delimiter this I-object SFDU label uses for its last eight bytes. A value of ‘F’ indicates that this label ends with the value specified in bytes 12 to 19, which implies that the I-object ends with an EOF marker. The value of ‘F’ is required per PDS Stds Ref., p.16-7. Also refer to MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; AnyCatalog, p.4-12 to 4-13. | Restricted ASCII-1 | ‘F’ |
| 7 | Reserved. This byte is a spare field. | Restricted ASCII-1 | ‘0’ |
| 8 to 11 | Data description package identifier. This field uniquely identifies (for the specified Control Authority, i.e., NJPL, per bytes 0 to 3) the data object [or value (V) field of this LVO]. | Restricted ASCII-4 | ‘T234’ |
| 12 to 19 | Length attribute of the SFDU. The end of this LVO is designated by marker — in this case, an EOF marker. The EOF marker is specified in this I-object SFDU label as ‘00000001.’ Note that the EOF marker terminating the I-object serves a dual purpose in that it also terminates the entire file, per bytes 12 to 19 of the primary SFDU label. The value of ‘00000001’ is required per PDS Stds Ref., p.16-7. Also refer to MGDS User’s Guide/Working with File Data (JPL D-6060), Ch.2; AnyCatalog, p.4-12 to 4-13. | Standard ASCII-8 | ‘00000001’ |

B.2.4   Binary Data Object

Starting at byte 80+M (M being the length of the catalog field) is the binary data object.  The binary data object of the file contains a series of CHDO SFDUs in time-sorted order.  That is, given a file containing different data types, all the data types are interleaved based on time.  The CHDOs are defined in Section 3.  The total length of the binary data object is L bytes.

B.2.5  End of File (EOF)

Starting at byte 80+M+L (M being the length of the catalog field and L being the length of the binary data object) is the end of the file (EOF) marker.  This 8 byte marker is defined in the Primary Label field, bytes 12 to 19.  The value of the EOF marker is ‘00000001’.