## Slide 1
INTRODUCTION
SuperCam Data Workshop
Roger C. Wiens
LPSC, The Woodlands, Texas, USA
Tuesday, March 11, 2025

## Slide 2: Agenda
Topic | Presenter | Duration | Start Time
Introduction | Roger Wiens | 12 minutes | 5:00 pm
2. VISIR reflectance spectroscopy | Allison Zastrow | 12 minutes | 5:15
3. LIBS / elemental chemistry | Agnes Cousin | 12 minutes | 5:30
4. Time-resolved Raman / luminescence | Ann Ollila | 12 minutes | 5:45
5. Imaging (RMI) | Stéphane Le Mouélic | 12 minutes | 6:00
6. Acoustics (microphone) | Sylvestre Maurice / Baptiste C | 12 minutes | 6:15
7. Group / question time | All | ~15 minutes | 6:30

## Slide 3: INTRODUCTION OUTLINE
Purpose & agenda
SuperCam instrument in a nutshell
Where to find data, PDS nomenclature
Formats of data files
Fields of view, overlap
Operations, order of ops, nomenclature
Other activities
Mission
Papers
Collaborations

## Slide 4: Purpose
To inform scientists how to access SuperCam data and use it
To inform about past and present work; inspire ideas for new research
To foster greater use and collaboration with SuperCam data. Collaboration can be with SuperCam team members (help learn to use the data) or among other researchers.

## Slide 5
SuperCam
In situ,
Characterize habitability
Aid search for organics
LIBS
Elemental Chemistry
VIS-IR
Minerals
Imaging
Raman
Minerals & Organics
MIC
Samples,
Find the most relevant to collect
Document their geological setting
Nearly identical to ChemCam
40 µrad
Highest remote resolution
First near IR from surface of Mars
Includes luminescence
Rock hardness
Sound speed
Wind
Figure by Sylvestre Maurice

## Slide 6
Documentation
Calibration data
Raw Spectra
Calibrated Spectra
Derived Products
--Elemental compositions
--Raman molecular IDs
RMI images
RMI mosaics
Other:
Obs Files (details on all data)
Analyst’s Notebook

## Slide 7: Raster, example
3 RMI
5 LIBS
5 Microphone
3 RAMAN
2 AF
AF
AF
AF = autofocus
This example does not include VISIR, normally done on each point.
P. Pilleri

## Slide 8: How is a raster organized into files?
One “science collect”  One FITS file
AF
RMI
LIBS
MIC
RAMAN
LIBS
MIC
LIBS
MIC
RAMAN
RMI
Point 1
Point 2
Point 3
Containing everything associated with the observation (spectra, SOH, parameters, …)
LIBS 1
MIC 1
RAMAN 1
AF 1
RMI 1
LIBS 2
MIC 2
LIBS 3
MIC 3
RAMAN 3
RMI 3
LIBS Header
Active LIBS Spectra
Dark LIBS spectra
SOH (temperature, focus position…)
List of LIBS commands
=
=
=
This example does not include VISIR, normally done on each point. VIS & IR are separate files
AF = autofocus
…
…
P. Pilleri

## Slide 9
LS__0113_0668703365_088EL1__0010000SCAM01113_000_LUJ01.FITS
Prefix
SolN
SCLOCK_SCLOCK Fraction
Technique Type
Site
Drive
SeqID
Point Number
Compression
Version
Producer
LRE_0299_0625326171_403ECM_N0010044SCAM15282_0000LUJ01
SCAM_0117_0067732593_000_CL0_scam01117_Mendocino____________02P01
Targetname
EDR (non-img):
EDR (imaging):
CDR
Technique types codes
Mosaics
ASCAM_SOL0117_scam01117_MOS_LR08_AFT_RGB_***_Mendocino____________02P01
AFTer/BEFore/FUSioned
Stretch
Annotation: Libs, Raman/VIS, Irs
Resolution
Targetname
P. Pilleri

## Slide 10: Code for extracting the data are in the backup slides

## Slide 11: EDR files structure
 |  | Experiment Data Record – EDR |  |  |  |  |  |  |  |  |  | 
 | Activity | LIBS | RAMAN | TRLS | VIS | IRS | Micro | RMI | RMI JPG | Autofocus | SOH* | 2D
 | Activity tag | EL[0-6] | ER[0-6] | ET[0-6] | EP[0,1,3] | EP2 | EA[0-2] | LRE*EC* | LRF*EJP | EA[0-2] | Various | E[L,R,T,P]S
HDU # | Relevant HDU section | Content |  |  |  |  |  |  |  |  |  | 
0 | Header | Generic Header, Activity keywords (including basic temperature, focus position, ...) |  |  |  |  |  |  |  |  |  | 
1 | Data | ODL Label |  |  |  |  |  |  |  |  |  | 
2 | Data | Timeline (I-cmds and their arguments) |  |  |  |  |  |  |  |  |  | 
3 | Data | MU SOH |  |  |  |  |  |  |  |  |  | 
4 | Data | BU SOH |  |  |  |  |  |  |  |  |  | 
5 | Data | Laser Data | Laser Data | Laser Data |  | Spectel SOH | Laser Data | Red | Red | AF results parameters |  | Laser Data
6 | Data | Darks Before | Darks Before | Darks Before | VIS spectra | Darks | Time series | Green 1 | Green | AF Curve |  | UV Dark
7 | Data | Actives | Actives | Actives | VIS darks | Spectra |  | Green 2 | Blue |  |  | VIO Dark
8 | Data | Darks After | Darks After | Darks After |  | Spectra SOH |  | Blue |  |  |  | G/O/R Dark
9 | Data |  |  |  |  |  |  |  |  |  |  | UV Actives
10 | Data |  |  |  |  |  |  |  |  |  |  | VIO Actives
11 | Data |  |  |  |  |  |  |  |  |  |  | G/O/R Actives
LS__SOLN_0123456789_012EF0__0010000scam12345_____01J00.fits
LRE_SOLN_0123456789_012ECM_N0010000scam12345_S001LUJ00.fits
Filename examples
P. Pilleri

## Slide 12: CDR files structure
 |  | Science product (Clean Data Record – CDR) |  |  |  |  |  |  | 
 | Activity | LIBS | RAMAN | TRLS | VIS | IRSpec | Micro | RMI | AF
 | Activity tag | CL[0-3] | CR[0-3] | CT[0-6] | CP3 | CP2 | CA[0-2] | CI | CA[0-1]
HDU # | HDU section | Content |  |  |  |  |  |  | 
Primary | Header | Generic Header, Status Flags, Activity keywords, Data Processing Keywords |  |  |  |  |  |  | 
1 | Data | ODL Label |  |  |  |  |  |  | 
2 | Data | Timeline (I-cmds and arguments) |  |  |  |  |  |  | 
3 | Data | MU SOH |  |  |  |  |  |  | 
4 | Data | BU SOH |  |  |  |  |  |  | 
5 | Data | Laser Data | Laser Data | Laser Data |  | IRS Spectel SOH | Laser Data | Red | AF result table
6 | Data | Shot-to-shot spectra | Shot-to-shot spectra | Delay Spectra | Shot-to-shot spectra | Spectra | Time series | Green | Autofocus Curve
7 | Data | Statistics spectra | Statistics spectra | Statistics spectra | Statistics spectra | Wavelength | Saturation Mask | Blue | Motor position
8 | Data | Wavelength | Wavelength | Wavelength | Wavelength | IRS Acquisition SOH |  |  | 
9 | Data | Saturation | Saturation | Saturation | Saturation | Saturation |  |  | 
CDR_SOLN_0123456789_CF0_scam12345_TargetNameCharacters_01J00.FITS
Filename example
P. Pilleri

## Slide 13: Example of FITS File Contents by HDU
Example for RMI
Primary Header
DATA
P. Pilleri

## Slide 14: Nomenclature
Shot = single laser pulse; the plasma signal is recorded with a spectrum from
each shot
Observation point = location; the place where the laser fired at a single point.
Almost all location analyses consist of 30 LIBS spectra
Raster = series of points observed on a single target. Usually 1x5, 2x5, 1x10, 3x3
“30 shots per point (LIBS, rock),” “up to 10 points per raster”
LIBS depth profile: > 50 laser shots in the same location, to investigate compositional variations at greater depths
LIBS or Raman “Dark” = non-laser background exposure of the same duration used for the active observation
Sequence = single set of commands that includes a raster, before & after RMI images, and darks. Each SuperCam sequence has SCAM + (single digit) + (last 3 digits of sol number)
Target = region of bedrock, soil, or float rock where the raster is placed. Each target has a name.
AEGIS = onboard autonomous target selection software; picks targets without ground in the loop
SCCT = SuperCam Calibration Targets, on back of rover (see publications)
AF = Autofocus, done occasionally throughout the raster

## Slide 15: Dust Removal By LIBS Enables the Other Techniques
ChemCam target Stephan
Circle shows RMI field of view
(~6 cm at this distance)
Maurice et al. 2021
IR field of view
Notes: This rock did not show up dark at all before the LIBS removed the dust!
The image at right was taken after one more LIBS raster, moving more dust out of the way

## Slide 16: Alignment of Techniques / Order of Techniques
VIS & Raman FoV
LIBS footprint based on laser focus, not spectro FoV; 170-450 µm @ 2-7 m;
Smaller than ChemCam
Order of Techniques
For rock surfaces
RMI image
LIBS (clears dust)
VISIR + Raman
RMI image
For soils, LIBS is done after VISIR & Raman
LIBS pit is much smaller than Raman or VISIR FoV; does not affect them
Maurice et al. 2021

## Slide 17: Other Activities
SuperCam makes regular observations of the sky for atmospheric absorption and opacity
  Data available as EDRs (some CDRs are generated, but don’t use them for sky observations)
  Talk to Tim McConnochie or Franck Montmessin
SuperCam has made observations to detect auroras on Mars. See presentations by Elise Knutsen.
SuperCam has made observations of various rover hardware; the observations consist of imaging, a few rare spectra, and recordings.
SuperCam has used L-shaped (3-point) rasters to mark the top of sample cores

## Slide 18: Status of SuperCam: Science—Rover Traverse
All techniques have contributed to SuperCam’s science
Top discoveries
Landing Site
Crater
Floor
Campaign
2021
Delta Front
& Depot
2022
Delta Top
Campaign
2023
Margin Unit
2023-2024
Crater Rim
2024-
~35 km so far
= SuperCam Observation
= Rover Stop

## Slide 19: 1. Publications 2. Collaboration
SuperCam publications are compiled in a separate document on the SuperCam workshop site. Some will be highlighted in the following presentations.
SuperCam leadership encourages team members to support people who are interested in digging into the data set. For those who would like more help than just answering a few questions, most team members would be happy to collaborate with people outside the team on the SuperCam data set

## Slide 20: Points of Contact
Co-Principal Investigators
  Roger Wiens, Purdue, Indiana, USA, rwiens@purdue.edu
  Agnes Cousin, IRAP, Toulouse, France, agnes.cousin@irap.omp.eu
Deputy Principal Investigators
  Sam Clegg, LANL, Los Alamos, USA, sclegg@lanl.gov
  Olivier Gasnault, IRAP, Toulouse, France, olivier.gasnault@irap.omp.eu
Working Group Leaders
  VISIR
    Allison Zastrow, LANL, Los Alamos, USA, a.m.zastrow@lanl.gov
    Pierre Beck, U. Grenoble, France, pierre.beck@univ-grenoble-alpes.fr
  LIBS / elemental chemistry
    Ann Ollila, LANL, Los Alamos, USA, amo@lanl.gov
    Agnes Cousin (see above)
  Time-resolved Raman & luminescence
Name | Position | Affiliation | E-mail
Roger Wiens | Principal Investigator | Purdue U., Indiana, USA | rwiens@pudue.edu
Agnes Cousin | Principal Investigator, LIBS WG lead | IRAP, Toulouse, France | agnes.cousin@irap.omp.eu
Sam Clegg | Deputy PI | LANL, Los Alamos, NM, USA | sclegg@lanl.gov
Olivier Gasnault | Deputy PI | IRAP, Toulouse, France | olivier.gasnault@irap.omp.eu
Allison Zastrow | VISIR WG Lead | LANL, Los Alamos, NM, USA | a.m.zastrow@lanl.gov
Pierre Beck | VISIR WG Lead | U. Grenoble, France | pierre.beck@univ-grenoble-alpes.fr
Ann Ollila | LIBS WG Lead | LANL, Los Alamos, NM, USA | amo@lanl.gov
Jose-Antonio Manrique | Raman WG Lead | U. Valladolid, Spain | joseantonio.manrique@uva.es
Elise Clave | Raman WG Lead | DLR, Berlin, Germany | elise.clave@dlr.de
Baptiste Chide | Acoustic/Atm Lead | IRAP, Toulouse, France | baptiste.chide@irap.omp.eu
Tim McConnochie | Atm/Acoustic Lead | SSI, New York, USA | tmcconnochie@spacescience.org
Franck Montmessin | Atm/Acoustic Lead | LATMOS, Paris, France | franck.montmessin@latmos.ipsl.fr
Olivier Gasnault | Imaging Lead | IRAP, Toulouse, France | olivier.gasnault@irap.omp.eu
Stéphane Le Mouélic | Imaging Lead | U. Nantes, France | stephane.lemouelic@univ-nantes.fr
See organization chart in backup slides

## Slide 21
Shout out for Analyst Notebook
(Tom Stein, PDS)

## Slide 22
Thank You

## Slide 23
Backup Slides

## Slide 24: Python code for extracting LIBS, Raman, VIS and IRS
from astropy.io import fits
import numpy as np
import matplotlib.pyplot as plt
fits_file = 'Path_to_supercam_CDR_file.fits'
# Open the FITS file
with fits.open(fits_file) as hdul:
# Read Wave, Spectrum from LIBS, RAMAN or VIS CDR
wave = hdul['Wavelength'].data['Wavelength']
mean = hdul['Statistics'].data['Mean']
# Read Wave, Spectrum (including atm correction) from IRS CDR (replace the previous 2 lines)
# wave = hdul['Wavelength'].data['Wavelength (um)’]
# mean = hdul['Spectra'].data['I_F_atm’]
# retrieve metadata
header_entries = hdul[‘Primary'].header
# Plot the data
plt.plot(wave, mean)
plt.show()

## Slide 25: Python code for extracting RMI images
from astropy.io import fits
import numpy as np
import matplotlib.pyplot as plt
fits_file = 'Path_to_supercam_CDR_file.fits'
# Open the FITS file
with fits.open(fits_file) as hdul:
# Read image data from the first RGB HDUs
image_data = [hdul['red'].data, hdul['green'].data, hdul['blue'].data]
# retrieve metadata
header_entries = hdul['Primary'].header
# Normalize the image data (use your own normalization method)
normalized_images = [img / np.max(img) for img in image_data]
# Stack the images to create an RGB image
rgb_image = np.stack(normalized_images, axis=-1)
# Display the imageplt.imshow(rgb_image)
plt.show()
# Save the image to a file
plt.imsave('output_image.png', rgb_image)

## Slide 26: Python code for extracting microphone recordings
from astropy.io import fits
import numpy as np
import matplotlib.pyplot as plt
fits_file = 'Path_to_supercam_CDR_file.fits'
# Open the FITS file
with fits.open(fits_file) as hdul:
# Read time series for SuperCam Audio
sound_data = hdul['Sound'].data['Sound']
# retrieve metadata
header_entries = hdul['Primary'].header
# Plot the data
plt.plot(sound_data)
plt.show()

## Slide 27: Operation Flow Chart

## Slide 28: Building a 1x5 Raster
Focus
RMI image on 1st point
Spectral observations, 1st point: LIBS first to remove dust
Move mast and repeat spectral obs., points 2-4
Focus
Spectral observations, last point
RMI image on last point
(Additional focuses and RMIs are used on longer rasters)
Overlapping region contains image portions with and without the laser pits, depending on which image is used.

## Slide 29: SuperCam’s Characteristic Scales
SuperCam’s characteristic scales are between 100 µm and 1 cm for targets between 2 m and 7 m
1.3-2.6 µm
0.4-0.85 µm

## Slide 30: Fields of View of IR Spectrometer and Body Unit Spectrometers

## Slide 31: Depth of Focus for Each Technique
Depth of field at 2 m (top, left), at 7 m (top, right), at 30 m (bottom) for different performance criteria – see text for their definition: IR collect (blue), BU collect (grey), RMI (orange), plasma creation (yellow). The horizontal axis is variations of the focus distance with regards to the target distance.
2 m
30 m
7 m

## Slide 32: SuperCam Organization Chart
    This document has been reviewed and determined not to contain export controlled technical data.
SuperCam
Co-PI R. Wiens
Co-PI A. Cousin
DPI S. Clegg
DPI O. Gasnault
Operations
Science pipeline
P. Pilleri
M. Brand
Lab. units
LANL (S. Clegg)
IRAP (A. Fau)
Hardware
ePUL, ePDL
LANL
CNES
Staffing
Activity dev.
Characterizations
Anomaly res.
Uplink Tools
Inst. experts
T. Nelson
P. Bernardi
GDS
Data experts
A. Sheridan
P. Pilleri
M. Brand
PDS delivery
A. Sheridan
Ops centers
LANL (S. Robinson)
CNES (M. Bouyssou)
Bilbao (G. Arana)
SCAM Ops Team (leads) S. Robinson, T. Nelson, M. Bouyssou/L. Peret, G. Lacombe
Inst dev.
S. Robinson
Ph. Caïs
Database
P Pilleri
Science
Working groups
LIBS (A. Ollila, A. Cousin)
Raman (J.-A. Manrique, E. Clave)
VISIR (A. Zastrow, P. Beck)
Atmos. (T. McConnochie, F. Montmessin, B. Chide)
RMI (O. Gasnault)
Geochemistry (C. Bedford, C. Royer)
sPUL, sPDL, CI rep., PEL, Project roles
Science team