## Slide 1
VISIR: Reflectance Spectroscopy
SuperCam Data Workshop
Allison Zastrow, on behalf of Pierre Beck, Adrian Brown, and the SuperCam VISIR Working Group
LPSC, The Woodlands, Texas, USA
Tuesday, March 11, 2025

## Slide 2: OUTLINE
Brief explanation of reflectance spectroscopy
SuperCam VISIR Details
  Basics and calibration info
Where to get the data on the PDS
SuperCam-specific “things to watch out for”
SuperCam VISIR papers

## Slide 3
Reflectance Spectroscopy
Chignik, sol 681

## Slide 4: SuperCam VISIR Basics
Two spectral ranges measuring passive reflectance
VIS
  Wavelength range: ~0.38 µm to ~0.85 µm over 5925 wavelength channels, with a gap between 0.465 µm and 0.537 µm
  Spectral resolution: 0.2 nm (@ shorter wavelengths) to 0.65 nm (@ longer wavelengths)
  Field of view: 0.74 mrad
IRS
  Wavelength range: ~1.3 µm to ~2.6 µm over 256 wavelength channels
  Spectral resolution: 5 nm (@ shorter wavelengths) to 20 nm (@ longer wavelengths)
  Field of view: 1.15 mrad
Clavé et al. (2023), JGR-Planets
https://doi.org/10.1029/2022JE007463
Note: this figure doesn’t include the shortest VIS wavelengths (< 0.5 µm)

## Slide 5: Calibration Info
VIS
  Saturation check
  Dark subtraction
  Conversion to radiance
  Conversion to relative reflectance through division by Sol 184 observation of SuperCam calibration target (SCCT) white target, and scaling by illumination geometry
IRS
  Saturation check
  Dark smoothing to keep only the low frequency trend
  Dark subtraction
  Conversion to radiance using Sol 20 white SCCT measurement as reference (in CDR file as “Radiance”)
  Thermal calibration
  Glitch removal
  Spikes removal
  Conversion to reflectance (in CDR file as “I_F”)
  Atmospheric correction (in CDR file as “I_F_Atm”)
For more details: https://pds-geosciences.wustl.edu/m2020/urn-nasa-pds-mars2020_supercam/document/M2020_SuperCam_EDR_RDR_SIS.pdf
https://pds-geosciences.wustl.edu/m2020/urn-nasa-pds-mars2020_supercam/document/SuperCam_PDS_Userguide.pdf
Important notes:
VIS and IRS are separate spectrometer systems with separate calibration methods
VIS region has NOT been corrected for atmospheric opacity

## Slide 6: How to find the data on the PDS
https://pds-geosciences.wustl.edu/m2020/urn-nasa-pds-mars2020_supercam/data_calibrated_spectra/
File identifiers
  VIS  “cp3”
  IRS  “cp2”
IRS
Data (“Spectra”): HDU 6
  Radiance, I_F, I_F_Atm, and other observation-specific calibration data
Wavelength: HDU 8
Other useful data
  Data Quality (HDU 9)
    Saturation, glitches, etc.
  Header (HDU 0)
    “DP_IR_PF”: Power flag
      Good  “False” (should be False in all CDR files)
      Bad  “True” or blank
  ODL Label (HDU 1)
    Observation viewing geometry, etc.
VIS
Data (“Statistics_Reflectance”): HDU 7
  Mean, Median, and Standard Deviation
Wavelength: HDU 8
  Wavelength and IRF info
Other useful data
  Saturation (HDU 9)
  Header (HDU 0)
    Number of wavelength channels for each region of the spectrometer
  ODL Label (HDU 1)
    Observation viewing geometry, etc.

## Slide 7: Things to watch out for
VIS and IRS are separate spectrometer systems with separate calibration methods
VIS region has NOT been corrected for atmospheric opacity
1 µm region is not measured, so band depth can only be interpreted qualitatively, given that offsets between VIS and IRS relative reflectance values may exist
Possible artifacts in both spectrometers due to various reasons (examples in the slides to follow)

## Slide 8: VIS and IRS: Things to watch out for
Shadowed spectra occur and measure only diffuse reflectance
Reflectances in shadowed locations are typically <0.1 in IRS
Reflectances in shadowed locations are typically <0.06 in VIS

## Slide 9: VIS: Things to watch out for
Artifacts at ~620nm and ~714nm
are due to where detector regions join/end
(can be more pronounced for high-reflectance targets)
Note: VIO (violet-blue spectrometer region) is not smoothed in CDR data on the PDS
Organic01
Cyan
IR white
Calcite
Chert
White paint
ZCAM white
Mean

## Slide 10: IRS: Things to watch out for
These wiggles are due to imperfect correction of CO2
Atmospheric correction residuals:
be careful to not make interpretations solely
on these features
RF power failure
Burnt_Island_996
Spectra with power failures are only released to the PDS as EDRs, not as CDRs
Frying_Pan_Spring_1058

## Slide 11: SuperCam VISIR Papers
Instrument/calibration papers:
  Wiens et al., 2021 (Body Unit); https://doi.org/10.1007/s11214-020-00777-5
  Maurice et al., 2021 (Mast Unit); https://doi.org/10.1007/s11214-021-00807-w
  Manrique et al., 2020 (Calibration targets, design); https://doi.org/10.1007/s11214-020-00764-w
  Madariaga et al., 2021 (Calibration targets, homogeneity); https://doi.org/10.1016/j.aca.2022.339837
  Cousin et al., 2021 (Calibration targets, characterization); https://doi.org/10.1016/j.sab.2021.106341
  Legett et al., 2022 (Optical calibration of spectrometers); https://doi.org/10.1364/AO.447680
  Fouchet et al., 2022 (IRS spectrometer); https://doi.org/10.1016/j.icarus.2021.114773
  Royer et al., 2020 (Pre-launch calibration of IRS spectrometer); https://doi.org/10.1063/1.5145390
  Royer et al., 2022 (Post-landing calibration of IRS spectrometer); https://doi.org/10.1029/2022JE007481
VISIR data papers:
  Wiens et al., 2022 (Crater floor synthesis paper); https://doi.org/10.1125/sci-adv.abo3399
  Mandon et al., 2023 (Crater floor mineralogy); https://doi.org/10.1029/2022JE07450
  Clavé et al., 2023 (Carbonate detection); https://doi.org/10.1029/2022JE007463
  Mandon et al., 2024 (Fe-mineralogy); https://doi.org/10.1029/2023JE008254
  Royer et al., 2024 (High-Al rocks); https://doi.org/10.1038/s43247-024-0183702
  Beck et al., 2025 (High-Si rocks); https://doi.org/10.1016/j.epsl.2025.119256
  Royer et al., 2025 (Multi-gaussian modeling of IRS data); in press, Icarus
VISIR papers in progress:
  Connell et al. (Dehydration experiment), in prep
  Quantin-Nataf et al., (Comparisons between CRISM and SCAM observations), in prep
  Zastrow et al., (IRS machine learning), in prep
Please feel free to reach out to the team with data questions or research inquiries!

## Slide 12
Thank You