## Slide 1
Acoustics
SuperCam Data Workshop
Presented by B. Chide on behalf of the SuperCam acoustic working group
LPSC, The Woodlands, Texas, USA
Tuesday, March 11, 2025

## Slide 2: OUTLINE
Mars acoustics and presentation of the microphone subsystem
Instrument Calibration
What kind of data does the microphone record?
Mars’ playlist
Data products and availability on the Planetary Data System
Main publications

## Slide 3: Mars Acoustics
Sound propagation on Mars: low amplitude, large attenuation, c ~ 250 m/s
Maurice et al., 2022, Nature
Mars Soundscape
Atmosphere (turbulence, dust devils, grain impacts)
Laser-induced shock waves -> Geology
Rover sound sources (helicopter, drill, actuators…)
The SuperCam microphone
Records pressure fluctuations
Acoustic bandwidth 50 Hz – 20 kHz
2 sampling frequencies : 25 kHz & 100 kHz
4 amplification gains (can be adjusted manually)
Encoding on 12 bits from 0 to 5 V
Calibrated sound data in Pascal

## Slide 4: Instrument calibration
Gain | Amplification factor | Sensitivity (V/Pa)
0 | X29 | 0.632
1 | X57 | 1.237
2 | X240 | 5.186
3 | X972 | 21.014
Output voltage from the microphone is converted into Pascal using:
  Sensitivity of the microphone
  Amplification factor of the electronics
  See Mimoun et al., 2023

## Slide 5: What kind of data does the microphone record?
Passive recording mode
SuperCam laser
Goal: record environmental noise
Up to 167s long recordings at 25 kHz
Microphone pointed at a given azimuth-elevation angle
Can be run un parallel with rover’s subsystems
Science rational:
  Survey of atmospheric turbulence
  Characterize acoustic environment
  Engineering diagnosis of the rover
Rover pumps
Rover pumps
Wind-induced signal
Atmospheric recording
Remote sensing mast motion recording
Electromagnetic Interferences
Mast Motion
Mast Motion
Wind-induced signal
Things to keep in mind in the data
Rover pumps tones often seen at 780 Hz, 390 Hz, 195 Hz
Wind noise is low frequency < 500 Hz.
Tones higher than 5 kHz, likely electromagnetic interferences
Sol 201 – 16:03 LTST
Sol 114 – 11:38 LTST

## Slide 6: What kind of data does the microphone record?
Laser-synchronized recordings
SuperCam laser
Goal: record laser-induced shock-waves
Microphone pointed at a the target
Recording synchronized with the laser
60 ms long window around each laser shot
Start of the recording triggered on laser ignition
Science rational
  Supports LIBS investigation (Rock hardness)
  Atmospheric science from sound speed
Things to keep in mind in the data
Laser-induced acoustic signal lies between 2 kHz and 20 kHz
SNR < 2 for target distance > 9m
Electromagnetic interferences with laser warm-ups at low frequency (<2kHz)
For a burst of n laser shots, only the first n-1 laser shots are recorded
Titanium calibration target is also recorded when analyzed

## Slide 7: Mars’s playlist
Up to Sol 1420 (i.e. ~2 full Martian Years)
29 hours and 30 min of passive recording
  7 Ingenuity flights recorded
  17 MOXIE runs
  1h and 30 min of rover operations
1021 rock and soil targets recorded
  From 1.56m (SCCT Titanium)
  To 12 m (with detectable acoustic signal)
  Equivalent to 5h of data
Atmospheric recordings
Rover operations
Gain 2
Gain 3
Distribution of the microphone recordings during the first two Martian Years of the Perseverance mission.

## Slide 8: Using and accessing the SuperCam microphone data
Uncalibrated time series
EDR (raw data). Accessible on the Raw Audio collection
Saturation check
Detrending
Calibration into Pa
Calibrated sound data
CDRs (calibrated data)
.fits files -> Pascal VS Time
.wav file** -> unitless time series
Accessible on the Calibrated Audio data collection
More to come soon: Derived data products for LIBS synchronous recordings (extraction of amplitude and propagation time for each shot), stay tuned!
** wave files are not filtered from instrument noise and rover pump noise. LIBS synchronous 60ms long window are concatenated back-to-back in a single file. EMI noise at low frequency not removed

## Slide 9: Main publications
Instrument
  Maurice et al., 2021 (Mast Unit) https://doi.org/10.1007/s11214-020-00777-5
  Wiens et al., 2021 (Body Unit) https://doi.org/10.1007/s11214-020-00777-5
  Mimoun et al., 2023 (Microphone) https://doi.org/10.1007/s11214-022-00945-9
Supporting LIBS investigations
  Chide et al., 2019 (Lab experiments) https://doi.org/10.1016/j.sab.2019.01.008
  Chide et al., 2020 (Lab experiments) https://doi.org/10.1016/j.sab.2020.106000
  Alvarez-Llamas et al., 2023 (Mars data) https://doi.org/10.1016/j.sab.2023.106687
Atmospheric science
  Maurice et al., 2022 (Mars soundscape) https://doi.org/10.1038/s41586-022-04679-0
  Chide et al., 2022 (Sound speed) https://doi.org/10.1029/2022GL100333
  Murdoch et al., 2022 (Dust devil) https://doi.org/10.1038/s41467-022-35100-z
  Stott et al, 2023 (Wind measurement) https://doi.org/10.1029/2022JE007547
  Chide et al., 2023 (Sound properties) https://doi.org/10.1016/j.epsl.2023.118200
  Chide et al., 2024 (Turbulence) https://doi.org/10.1121/10.0024347
Ingenuity
  Lorenz et al., 2023 https://doi.org/10.1016/j.pss.2023.105684
Modelling
  Gillier et al., 2024a (Sound attenuation) https://doi.org/10.1029/2023JE008257
  Gillier et al., 2024b (Sound propagation) https://doi.org/10.1029/2024JE008469